## Slide 1: WF on R17 NR MG enhancements - Multiple concurrent and independent MG patterns
Mediatek Inc.
3GPP TSG-RAN WG4 #98bis-e Meeting
Electronic Meeting, Apr. 12-20, 2021
R4-210xxxx

## Slide 2: Definition
Concurrent gaps are configured by multiple RRC IE MeasGapConfig [during a common period of time]
  FFS on the definition of the “common period of time” and whether it shall be introduced
  FFS how to handle fully overlapping multiple MG case
  FFS how to handle activated/deactivated pre-configured MGs (in case they are defined)
  Detailed RRC configuration is up to RAN2
  UE behavior for measurement of multiple MG patterns is FFS
GTW agreements

## Slide 3: Definition
Common period of time:
  Option 1: Without considering pre-configured gap: The common period of time is the duration in which UE is configured with more than one MGs
  Option 2: With considering pre-configured gap: The common period of time is the duration in which UE is operating with more than one active MGs FFS
    Option 3: General: E.g., The common period of time is the time during which the UE is operating with more than one active MG

## Slide 4: Applicability and configurations
The measurement purposes of concurrent gaps include:
  Different configuration (e.g. periodicity , MGL and/or offset) of reference signals, including SMTC from different cells or frequency layers that cannot be covered by one measurement gap occasion
  Different RSs, e.g., SSB, CSI-RS, PRS, RSSI
  Different RATs
    FFS whether to allow concurrent MG when the UE is configured to perform only non-NR RAT measurements
  FFS relation between the measurement purposes and parameters of the parallel patterns MGPs’ configuration

## Slide 5: Applicability and configurations
FFS whether RAN4 should associate gap(s) to dedicated use case(s).
  If Yes, Option 1: associate gap(s) to dedicated use case(s)
    FFS on whether to associate all gaps or only the new gap
    FFS on which use cases should be associated.
  Option 2: NW configures which MG is to be used for each MO
  Option 3: NW configures which MO is to be measured in new/each MG
Existing configuration mechanism under DC mode can be reused:
  In EN-DC,
    per-UE gap and FR1 gap are configured by MN,
    FR2 gap is configured by SN.
  In NE-DC and NR-DC,
    per-UE gap, FR1 gap and FR2 gap are configured by MN.

## Slide 6: UE capability related issues
When UE doesn’t support per-FR gap,
  All concurrent gaps are per-UE
  The max number of supported concurrent gap is
    Option A: 2
    Option B: Up to UE capability
When UE supports per-FR gap,
  FFS whether to allow any combinations of per-UE gap and per-FR gap to be configured simultaneously
  FFS the max number of supported concurrent gap
  FFS on the combination of the per-UE gap and/or per-FR gap to be configured simultaneously
  FFS on Per-FR gap to be configured with Per-UE concurrent gaps (e.g. not configured with Per-FR gaps but only per-UE concurrent gaps)

## Slide 7: UE capability related issues
FFS whether UE shall support combinations of concurrent gaps comprising any of any the by UE supported MGPs
FFS whether to introduce the applicability conditions that may limit the allowable combinations of MGPs that can be configured concurrently

## Slide 8: Overlapping issues
Definitions of fully overlapped, partial overlapped and fully non-overlapped concurrent gaps
  Start from per-UE gap. FFS how to extend to per-FR gap
  Fully non-overlapped (FNO): All gap occasions of 2 MGs are disjoint in time.
  Fully-overlapped (FO): Every gap occasion of one MG is fully covered by every gap occasion of another MG with the same periodicity
  Partially overlapped
    (FPO#1): Does not belong to FNO but belong to nor FO, and the periodicities are the same.
    (PFO#2 and PPO#2): Does not belong to FNO and does not belong to FO, and the periodicities are different.

## Slide 9: Overlapping issues
Requirement will be defined at least for FNO. FFS other cases
FFS UE’s behavior in collided gap durations, if needed

## Slide 10: Overhead
Whether to define an overhead cap
  Option A: Yes
  Option B: No

## Slide 11: Measurement gap requirements
FFS the legacy gap related requirements that can be re-used for concurrent gaps. Candidates including:
  MG patterns (or sequence),
  MG applicability,
  MG reference timing (including MGTA),
  effective MGRP,
  MG interruption (data scheduling opportunity depends on MG configuration)
  UE UL behaviour after MG
  Other requirements if identified

## Slide 12: Measurement requirements
FFS additional assumptions (on network configuration and for UE behavior) for concurrent gap, e.g.,
  Only one frequency layer can be measured in a single gap instance.
  Only one type of RSs can be performed in a single gap instance.
  One RS configuration can only be measured in one MG pattern
FFS CSSF requirements of concurrent gap
FFS: RRM impact from reconfiguration of concurrent gaps

## Slide 13: Others
The validation delay for concurrent gap is the same as legacy Rel-15/16 RRC processing delay, when pre-configured gap is not considered