## Slide 1
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-210xxxx
Electronic Meeting, 12th – 20th April, 2021
Agenda Item: 8.6.2
WF on FR1 HST RRM
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1912781 WF on RRM for NR HST, RAN4#98-e

## Slide 3: Agreement
  PSS/SSS detection delay, time index detection delay, and measurement period for activated SCell
    Confirm the agreements in last meeting that PCell enhancement in Rel-16 HST are re-used to specify the requirements on PSS/SSS detection, time index detection and measurement period for activated Scell (including both intra-frequency measurement without MG and intra-frequency measurement with MG), i.e. the M2 and Y defined in Rel-16 HST are reused for activated Scell
    Kp is kept for activated Scell measurement

## Slide 4: Agreement
  Enhancement on CSSFoutside_gap,i for SCell measurement
    RAN4 has the following common understanding of the current non-HST specification:
      For CSSFoutside_gap,i, both SCell(s) measured without MG and SCell(s) measured with MG are counted in NSCC_SSB.
        Both activated and deactivated SCells are included
    FFS the enhancement on NSCC_SSB for high speed scenario

## Slide 5: Agreement
  PSS/SSS detection, time index detection, and measurement period for deactivated Scell
    M2 defined in Rel-16 HST is reused for PSS/SSS detection delay requirements for deactivated Scell
    M2 defined in Rel-16 HST is reused for time index detection delay requirements for deactivated Scell
    Enhancement to PCell measurement in R16 HST can be reused for measurement period enhancement on deactivated Scell
    FFS whether Rel-16 Kp requirements modifications (if any) shall also apply for R17 HST
DRX cycle | T SSB_measurement_period_intra
No DRX Note 2 | 5 x measCycleSCell x CSSFintra
DRX cycle≤ 160ms | 5 x max(measCycleSCell, M2 Note 2xDRX cycle) x CSSFintra
160ms < DRX cycle≤ 320ms | 4 x max(measCycleSCell, M2 Note 2xDRX cycle) x CSSFintra
DRX cycle>320ms | Y Note 3 x max(measCycleSCell, DRX cycle) x CSSFintra
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified NOTE 2: M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1 NOTE 3: Y=3 when SMTC <= 40ms, Y=5 when SMTC > 40ms | 

## Slide 6: Agreement
  SCell activation delay
    Legacy SCell activation delay can be reused in high speed scenario
  Inter-frequency measurement
    Define RRC Connected state inter-frequency measurement enhancements
      Support of HST inter-frequency measurement enhancements is up to UE capability. Details are FFS
    FFS whether enhancements for RRC IDLE inter-frequency measurements are needed

## Slide 7: Agreement
  L1-RSRP
    Reuse the SSB- and CSI-RS-based L1-RSRP enhancement for Rel-16 HST PCells for Rel-17 HST Scells
  SS-SINR, SS-RSRP, SS-RSRQ,
    Reuse the Rel-16 HST SS-SINR measurement accuracy requirement for Rel-17 HST SCells and legacy SS-RSRP and SS-RSRQ requirements are applied for Rel-17 HST SCells

## Slide 8: Agreement
  BFD
    For TEvaluate_BFD_CSI-RS, follow the agreement in Rel-16 HST
  Upper bound of DRX cycle for the R17 HST enhancement
    For cell reselection, requirements with 2.56s DRX cycle have not been enhanced for high speed operation
    For PSS/SSS detection delay, time index detection and measurement delay in connected mode, requirements with 2.56s DRX cycle have not been enhanced for high speed operation

## Slide 9: Agreement
  L1-SINR
    Option 1 (MTK): For L1-SINR measurement in Rel-17 HST, the upper bound of the side condition SSB Ês/Iot ≤5 dB should be introduced, for CMR only case at least
    Other options are not precluded
  Scell link recovery
    Option 1 (HW, MTK, Nokia): For Scell link recovery, RAN4 needs to study how many band(s) is supported in R17 HST in FR1
    Option 2 (QC, Ericsson, vivo, CATT, CMCC): no need to have this limitation in the spec

## Slide 10: Agreement
  CSSF
    Option 1(HW, MTK): For CSSF, RAN4 needs to study how many Scell(s) is supported in R17 HST in FR1
    Option 2 (Ericsson, Apple, CATT, CMCC, Intel): no need to have this limitation in the spec
  UE capability
    Option 1 (Ericsson): For RRM measurement, new UE capability like ‘measurementEnhancementsSCell’ can be introduced to indicate the UE supports enhanced measurements on SCC to support [350]km/h velocity with active Scells or deactivated Scells
    Option 2 (QC, MTK, vivo, OPPO): new UE capability should be added for the support of 500km/h as WID listed, no need to add the additional capability for different velocity values in Rel-17 HST

## Slide 11: Agreement
  Release independent
    Option 1 (CMCC): it is proposed that Rel-17 FR1 HST RRM enhancement is release independent from Rel-15
    Option 2 (HW, MTK, Nokia, Apple, DCM): Needs further study