## Slide 1: WF on Rel-17 NR HST FR2 enhancements, RRM requirements
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic Meeting, 12th – 20th April, 2021
Agenda: 8.7.4
R4-210xxxx
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
The Rel-17 NR HST FR2 Enhancements WI is presented in WID RP-202118.
The Work plan of the WI, including RRM core and perfromance part can be found in R4-2016920.
R4-2103679 WF on Rel-17 NR HST FR2 enhancements, RRM requirements has been approved at the previous meeting RAN4#98-e.
Corresponding Email summaries in RAN4#98-bis-e:
  R4-2105691 Email discussion summary for [98-bis-e][221]NR_HST_FR2_RRM, first round.
  R4-210xxx Email discussion summary for [98-bis-e][221]NR_HST_FR2_RRM, second round.

## Slide 3: General Agreements
The discussion on whether an HST FR2 network should be capable to server only HST FR2 CPEs or also other types of UEs shall be continued in the HST FR2 deployments thread.
The discussion on the number of Rx beams shall continue in the HST FR2 deployments thread.

## Slide 4: Way Forward on Maximum Supported Speed from RRM Perspective
Continue evaluation of maximum supported speed from the RRM perspective based on the detailed RRM requirements.

## Slide 5: Way Forward on CONNECTED State Mobility
RRC CONNECTED mode requirements for DRX:
  Option 1: Define requirements for non-DRX case only
  Option 2: Define requirements for the short DRX configurations and apply exiting R16 requirements for longer cycles.
  FFS: the lengths of short DRX cycle with new requirements
Scaling factor N
  Option 1: For FR2 HST, the FR2 scaling factor can be reduced as:
    For uni-directional deployment, N=[1]
    For bi-direcitonal deployment, N=[2].
  Option 2: Scaling factor N (number of Rx beams to sweep) may depend on available network assistant information.
  Option 2: Other options are not precluded

## Slide 6: Way Forward on CONNECTED State Mobility (Continued)
Handover:
  Existing FR2 requirement should be applicable to the HST FR2 deployments when the target cell is known.
  FFS: Handover requirements when the target cell is unknown
  FFS: a need to address the potential change in the scaling factor 8.
Connection mobility control - RRC re-establishment:
  FFS: whether the existing requirements can work for FR2 HST.
Connection Mobility Control - RRC Release with Redirection
  Deprioritize the analysis of the requirement

## Slide 7: Way Forward on Timing
Autonomous time adjustment:
  Option 1: Autonomous timing adjust step Tq for FR2 in high speed scenario is 4.5Ts.
  Option 2: Other options are not precluded
TA mechanism enhancement:
  Option 1: One-time large TA adjustment can be enabled when switching between RRH for uni-directional deployment
  Option 2: Other options are not precluded
Requirements for MRTD/MTTD:
  Not applicable to FR2 HST

## Slide 8: Way Forward on Measurement Procedures
Requirements on inter-frequency measurements
  Option 1: Inter-frequency measurements are required for NR single carrier scenario in FR2
  Option 2: Not applicable to FR2 HST
Requirements on inter-RAT measurements:
  Option 1: Inter-RAT measurements are required for NR SA single carrier scenario in FR2
  Option 2: Not applicable to FR2 HST

## Slide 9: Way Forward on Measurement Procedures (continued)
Cell identification - Intra-frequency measurements:
  The intra-frequency measurement requirement shall be enhanced
  FFS: the enhancements to be introduced
Cell identification - PSS/SSS detection
  The Cell identification - PSS/SSS detection requirements shall be enhanced
  FFS: the enhancements to be introduced
Restriction on SMTC periodicity:
  Option 1: Restriction on SMTC periodicity configuration are preferred in FR2 HST.
  Option 2: No limitation of SMTC and relying on network implementation.
L1 measurements:
  The L1 measurements shall be enhanced
  FFS: the enhancements to be introduced
CSI-RS based L3 measurements:
  The analysis of the requirements to be de-prioritized

## Slide 10: Way Forward on IDLE/INACTIVE State Mobility
IDLE/INACTIVE mode requirements:
  The companies are encouraged to provide their views on the following options and share their proposals on possible enhancements:
    Option 1: Reuse existing Rel-16 requirements
    Option 2: Study and define enhancements to support FR2 HST condition
    Option 2a: For FR2 HST, the cell reselection requirements are enhanced according to Table (Tdetect,NR_Intra, Tmeasure,NR_Intra and Tevaluate,NR_Intra for FR2 HST), where N1 ≤ 4:
  FFS: the way how IDLE/INACTIVE state can be used in HST FR2 deployment
DRX cycle length [s] | Tdetect,NR_Intra [s] (number of DRX cycles) | Tmeasure,NR_Intra [s] (number of DRX cycles) | Tevaluate,NR_Intra [s] (number of DRX cycles)
0.32 | [2.56] x N1 x M2 (8 x N1 x M2) | 0.32 x N1 x M3 (1 x N1 x M3) | 0.96 x N1 x M4 (3 x M4)
0.64 | [5.12] x N1 (8 x N1) | 0.64 x N1 (1 x N1) | 1.92 x N1 (3 x N1)
1.28 | [8.96] x N1 (7 x N1) | 1.28 x N1 (1 x N1) | 3.84 x N1 (3 x N1)
2.56 | 58.88 x N1 (23 x N1) | 2.56 x N1 (1 x N1) | 7.68 x N1 (3 x N1)
Note 1: when SMTC < = 40 ms, M2 = M3 = M4 = 1; and when SMTC > 40 ms, M2 = 1.5, M3 = M4 = 2 |  |  | 

## Slide 11: Way Forward on Signalling
HST FR2 network deployment flag:
  Option 1: Add flag to enable the UE to differentiate between the HST and non-HST scenarios
  Option 2: HST FR2 CPE is a special dedicated device, flag is not needed
  The companies are encouraged to disclose their views on these options and
    FFS: what special requirements or special behavior needs to be indicated to the CPE.
HST FR2 uni-/bi-directional mode flag:
  Continue the discussion after the deployments are fixed between the following options:
    Option 1: Network informs UE whether it operates in bi-directional mode in high-speed in FR2 by corresponding flag.
    Option 2: Such a flag is not needed.
UE support for HST FR2:
  Continue the discussion after the presence of other non-HST UEs in the network is clarified between the following options:
    Option 1: The UE should inform network that it supports HST FR2 (UE capability is needed)
    Option 2: Only roof-mounted CPE is considered that should always have a capability to work in HST FR2 scenario
UE support for bi-directional operation:
  Continue the discussion after the deployments are fixed
    FFS: does CPE support bi-directional mode mandatorily based on the deployment agreements.
FFS: a need of network signalling of DL Tx beam switching pattern and detectable DL Tx beams from the neighbouring cells.
FFS: whether and what network assisted information is needed to reduce the number of RX beams.

## Slide 12: Way Forward on Signalling (continued)
RLM/BFD:
  FFS: The applicability and possible impact of requirements on HST FR2
CBD:
  FFS: The applicability and possible impact of requirements on HST FR2
  FFS: whether CBD procedure before BFD is needed
Active TCI state switching delay:
  Option 1: Consider only known TCI state.
  Option 2: Known or unknown TCI state switching is applied in FR2 HST depends on the deployment.
    If the overlapping area between serving beam and target beam is appropriate, the L1-RSRP measurement can be reported in time. The existing TCI switching delay can be reused in FR2 HST.
    If UE is not able to report L1-RSRP of the approaching beam before network indicates a TCI state switching, L1-RSRP measurement procedure will be additional added. The performance shall be carefully studied
  Option 3: Other options are not precluded
Uplink spatial relation switch delay:
  FFS: The applicability and possible impact of requirements on HST FR2

## Slide 13: Summary of Applicability of Rel-15/16 Requirements to Rel-17 HST FR2
RRM Req. Category | Sub-Category | Whether or not applicable to FR2 HST
Idle/inactive state mobility | Cell selection/re-selection, measurement | FFS
Connected state mobility | Handover | FFS
 | Connection Mobility Control - RRC re-establishment | FFS
 | Connection Mobility Control - Random Access | No impact identified
 | Connection Mobility Control - RRC Release with Redirection | Deprioritize
Timing | Autonomous timing adjustment | FFS
 | TX timing, timer, TA, Cell Phase Sync accuracy, deriveSSB-IndexFromCell tolerance | FFS
 | MRTD/MTTD | No impact identified
Signalling | RLM | FFS
 | Interruption | No impact identified
 | SCell Activation and Deactivation Delay | Not applicable to FR2 HST
 | UE UL carrier RRC reconfiguration delay | Not applicable to FR2 HST
 | Link Recovery | FFS
 | Active BWP switch delay | No impact identified
 | Active TCI state switching delay | FFS
 | PSCell Change | Not applicable to FR2 HST
 | Uplink spatial relation switch delay | FFS
 | UE-specific CBW change | No impact identified
 | Pathloss reference signal switching delay | No impact identified
Measurement Procedure | General measurement requirement | No impact identified
 | NR intra-frequency measurements | FFS
 | NR inter-frequency measurements | FFS
 | Inter-RAT measurement | FFS
 | L1-RSRP/L1-SINR Measurement | FFS
 | CSI-RS based L3 measurements | Deprioritize
 | NR measurements with autonomous gaps | Not applicable to FR2 HST
Requirements’ classification categories:
  Not applicable to FR2 HST: the requirement is not applicable to Rel-17 FR2 HST UE
  No impact identified: no change on Rel-15/16 requirement is needed, and the same requirement applies to Rel-17 FR2 HST UE.
  FFS: need to discuss whether or not the requirement is applicable to Rel-17 FR2 HST UE and/or whether or not Rel-15/16 requirement needs to be changed/enhanced
  Deprioritize: can be discussed and studied further but with low priority.

## Slide 14: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2104851 | Discussion on FR2 HST RRM requirement - geneal | Apple
R4-2104852 | Discussion on RRM requirement for FR2 HST | Apple
R4-2104754 | Discussion on the maximum supported speed analysis for NR HST FR2 | CATT
R4-2104755 | Discussion on RRM requirements for NR FR2 HST | CATT
R4-2104949 | Discussion on RRM requirements for FR2 HST | CMCC
R4-2104814 | RRM general considerations for HST FR2 | Ericsson
R4-2104815 | RRM requirements for HST FR2 | Ericsson
R4-2106937 | Discussion on NR support for high speed train scenario in FR2 | Huawei, HiSilicon
R4-2106504 | RRM requirements for HST in FR2 | Intel Corporation
R4-2106505 | General aspects of RRM requirements for HST in FR2 | Intel Corporation
R4-2106583 | Simulation analysis for HST in FR2 | Nokia, Nokia Shanghai Bell
R4-2106584 | Discussion about RRM requirements for HST in FR2 | Nokia, Nokia Shanghai Bell
R4-2104907 | FR2 HST RRM discussion | Qualcomm, Inc.
R4-2105027 | Maximum Supported Speed from RRM perspective for FR2 HST | Samsung
R4-2106838 | Further discussion on RRM requirements for FR2 HST | Samsung