## Slide 1: WF on NR NTN RRM general and measurement requirements
Moderator: Fraunhofer HHI

## Slide 2: Outline
Proposed way forward based on the outcomes of “Email discussion summary for [98-bis-e][222] NR_NTN_solutions_RRM_1”
See R4-210xxxx

## Slide 3: Content
Topic #1: General RAN4 RRM NTN related aspects
Topic #2: GNSS requirements
Topic #3: PVT Satellite precision
Topic #5: NTN UL frequency synchronization requirement
Topic #6: NTN Measurements

## Slide 4: Summary
Main RRM issues and preliminary proposals have been discussed
  In green: proposals which are agreeable
  In orange: proposals for which a potential agreement may be found with suggested changes (needs further discussion)
  In purple: proposals for which there is no agreement yet

## Slide 5: Topic #1: General RAN4 RRM NTN related aspects
Sub-topic 1-1: RP to be considered for time and frequency synchronization
  Issue 1-1: Definition of reference point
    Moderator suggestion: Do not define timing or frequency RP in RAN4, further study frequency RP after RAN1’s final decision about frequency pre-compensation scheme. Assume frequency RP at gNB as starting point for further requirement discussion.
  Issue 1-2: LS to RAN1 regarding observed implementation impact of DL-UL delay
    Do not send LS to RAN1.

## Slide 6: Topic #1: General RAN4 RRM NTN related aspects (cont’d)
Sub-topic 1-2: In device coexistence (IDC) issue of GNSS and L-band
  Issue 1-3: Confirmation of IDC issue
    Defer discussion about IDC interference from L-Band NTN to GNSS after the issue has been evaluated/confirmed by the RAN4 RF room.

## Slide 7: Topic #2: GNSS requirements
Sub-topic 2-1: GNSS usage
  Issue 2-1: Definition of GNSS requirements
    RAN4 assumes that ephemeris of the satellite/HAPS is made available to UE in defining the RRM requirements. No further discussion on whether the satellite or HAPS has on-board GNSS. Further study on the precision of the ephemeris data.
Sub-topic 2-2: GNSS accuracy
  Issue 2-2: Consideration of on-board GNSS equipment
    Moderator suggestion: Assume on-board GNSS equipment for further PVT accuracy requirement discussion.
  Issue 2-3: GNSS accuracy impact on RRM requirements
    Follow agreement of Issue 2-4: The impact of GNSS accuracy should be considered when defining each RRM requirement

## Slide 8: Topic #2: GNSS requirements (cont’d)
Sub-topic 2-2: GNSS accuracy (cont’d)
  Issue 2-4: Criteria of GNSS accuracy
    The impact of GNSS accuracy should be considered when defining each RRM requirement
      GNSS accuracy (e.g. as a function of UE GNSS capability) and side conditions and exact impact on the RRM requirements are FFS.
      GNSS accuracy enhancements are out of scope
  Issue 2-5: GNSS accuracy for location-based CHO
    GNSS accuracy for location-based CHO need to be checked after location-based CHO is clear in RAN2.
  Issue 2-6: Impact of time to first fix/time to subsequent fix on RRM requirements
    RAN4 shall figure out the accuracy or response time difference between TTFF and TTFS before concluding this issue. The impact on specific RRM requirements and respective scenarios is FFS.

## Slide 9: Topic #2: GNSS requirements (cont’d)
Sub-topic 2-2: GNSS accuracy (cont’d)
  Issue 2-7: Measurement period
    FFS, proposing companies need to elaborate.
  Issue 2-8: Reference GNSS scenario
    Typical and worst-case scenario parameters are FFS. For worst-case parameters, the following minimum requirements can be used as starting point:
    FFS how much total timing error budget the UE can consume
    FFS on how to narrow down from 3GPP spec such as 38.171 to avoid extensive discussion
System | Success rate | 2-D position error | Max response time
All | 95 % | 100 m | 20 s

## Slide 10: Topic #3: PVT Satellite precision
Sub-Topic 1: Requirements for PVT computation and distribution
  Issue 3-1: NTN PVT Accuracy Aspects
    Defer discussion until RAN1 concludes on the issue.

## Slide 11: Topic #5: NTN UL frequency synchronization requirement
Sub-topic 5-1: Frequency accuracy requirements
  Issue 5-1: Time/Frequency pre-compensation accuracy requirements
    Defer discussion on frequency pre-compensation to RF thread [309] and discussion on time pre-compensation to RRM thread [223].

## Slide 12: Topic #6: NTN Measurements
Sub-topic 6-1: General RRM NTN measurement requirements
  Issue 6-1: DRX cycle
    CATT suggestion: RAN4 should further study the applicability of DRX cycle in RRM requirements.
  Issue 6-2: Side condition for RRM measurement requirements
    Moderator suggestion: More discussion on side condition for RRM measurements necessary. The discussion should be done on a case by case basis and take the scenario into account.
  Issue 6-3: Beam sweeping
    Defer discussion about beam sweeping until RAN1 has concluded on the topic.
  Issue 6-4: RRM procedures based on UE position
    For NTN-specific location based measurements, consider the requirements for A-GNSS in 38.171 as a starting point.

## Slide 13: Topic #6: NTN Measurements (cont’d)
Sub-topic 6-1: General RRM NTN measurement requirements (cont’d)
  Issue 6-5: Update rate of ephemeris
    CATT suggestion: RAN4 should further study whether and how update rate of ephemeris has impact when defining detailed RRM requirements.
  Issue 6-6: Feeder link pre-compensation
    Feeder link pre-compensation is outside the scope of this room and WI. Defer discussion until other working groups have reached a conclusion.
Sub-topic 6-2: Mobility
  Issue 6-7: Definition of mobility/measurement aspects
    Frequency reuse factor and beam mapping should be discussed in RAN1/RAN2 first. Defer discussion until conclusion is reached there.

## Slide 14: Topic #6: NTN Measurements (cont’d)
Sub-topic 6-2: Mobility (cont’d)
  Issue 6-8: Intra-satellite/Inter-satellite cell mobility
    Moderator suggestion: RAN1/RAN2 input necessary before conclusion can be made. FFS on location and/or timer based measurement relaxations.
  Issue 6-9: L1/L3 measurement requirements
    Moderator suggestion: RAN1/RAN2 input necessary before conclusion can be made. For further discussion, assume: RAN4 to investigate L1/L3 measurement requirements for GEO and non-GEO separately.
      Whether or not the requirements can be defined in the same manner for GEO and non-GEO will be determined after the investigation
      Whether legacy RLF and BFD requirements are relevant for NTN UEs, e.g. legacy BLER value of a hypothetical PDCCH transmission and/or PDCCH format for out-of-sync and BFD can be reused

## Slide 15: Topic #6: NTN Measurements (cont’d)
Sub-topic 6-2: Mobility (cont’d)
  Issue 6-10: Scenarios for measurement and mobility
    Moderator suggestion: Although further input from RAN1/RAN2 is necessary, RAN4 should discuss measurement and mobility for the following scenarios with high priority:
      Intra-NTN for both RRC Connected and Idle/Inactive modes
      between GEO type satellites
      between LEO type satellites at the same altitude
      between earth moving cells
    The scenario “between NTN and TN for RRC Inactive/Idle modes” is suggested to be deprioritized.

## Slide 16: Topic #6: NTN Measurements (cont’d)
Sub-topic 6-2: Mobility (cont’d)
  Issue 6-11: Cell selection and re-selection
    CMCC suggestion: The existing cell reselection delay requirements and mobility methodologies can be considered as baseline for NTN scenarios with limitation of DRX cycle and the number of measurement samples. RAN4 can consider define reasonable cell reselection margins in NTN scenarios. RAN4 shall furthermore define the RRM requirements for satellite/HAPS ephemeris based cell selection and re-selection once RAN2 completes the cell reselection procedure for NTN.
  Issue 6-12: Conditional hand over requirements
    Moderator suggestion: RAN4 is to define the RRM requirements for time/timer and location based CHO triggering events after RAN2 concludes on the framework.
  Issue 6-13: Feeder link switching based handover
    Defer discussion until RAN2 has concluded on the issue

## Slide 17: Topic #6: NTN Measurements (cont’d)
Sub-topic 6-3: Measurement gap and SMTC
  Issue 6-14: Interruptions or measurement gaps for GNSS measurements
    Defer discussion about this issue. It has to be looked at by the RF session, and only if issues are identified there, the discussion can continue in RRM.
  Issue 6-15: Discussion of SMTC and MG
    Wait for progress in RAN2
  Issue 6-16: SMTC and MG based requirements
    Defer discussion, overlaps with issues 6-10 and 6-15
  Issue 6-17: Measurement gap starting point
    Wait for progress in RAN2, avoid conflicting discussions
  Issue 6-18: SMTC and gap window misalignment
    Defer discussion and wait for input from RAN2