## Slide 1: WF on timing requirements for NR NTN
Xiaomi

## Slide 2: WF on UE specific TA estimation error
    The UE specific TA estimation accuracy is counted into the UE transmit timing error requirement
      UE specific TA estimation accuracy is FFS
      FFS whether the UE specific TA estimation accuracy shall be also defined as a separate accuracy requirement
      Specify UE behavior related to UE specific TA estimation and the detailed behavior is FFS
    FFS on the update periodicity of UE specific TA value

## Slide 3: WF on timing requirement
UE initial transmit timing error (Te)
  Te requirement in NTN is consist of:
    The existing Te requirements defined in TS 38.133 Table 7.1.2-1, Same types of errors as terrestrial UE e.g. DL timing estimation accuracy and UL timing setting accuracy. and;
    UE specific estimation accuracy;
  FFS on whether and how much different relaxations are required for different sets of SCS of SSB and SCS of uplink signals
  It is the total NTN UE Te error that decides UL performance, no matter the source of inaccuracy.
N_TA_offset
  The existing N_TA offset value defined in Table 7.1.2-2 in TS38.133 can be reused in NTN
Gradual timing adjustment
  Define new gradual timing adjustment requirements for NTN UE
    FFS whether and how to count the maximum delay variation;
      Note: In TR38.821, the delay variation measures how fast the round trip delay (function of UE-satellite-NTN gateway distance) varies over time when the satellite moves towards/away from the UE.
    FFS: whether define different requirements for different NTN topologies in terms of, e.g. GEO, MEO, LEO, HAPS, HIBS, altitude, elevation angles for feeder/service links, UE speed, etc;
    One shot timing adjustment
      Not introduce one shot timing adjustment requirement for NTN UE

## Slide 4: WF on TA adjustment accuracy requirement
In RRC_idle mode
  FFS whether to define TA adjustment accuracy requirement;
  In RRC_CONNECTED mode
    Option 1: Reuse the existing TA adjustment accuracy requirement defined in TS 38.133 with considering of UL timing quantization accuracy.
    Option 2: FFS on whether relax the TA adjustment accuracy requirement.
      FFS on UE position and satellite position estimation error;
      FFS on propagation delay change from a slot when UE received timing advance command to a slot when the indicated TA.
    TA adjustment accuracy should scale inversely proportional to SCS (and in current specification it is ±1/4 TA-step (at SCS = 15 kHz)).