## Slide 1: WF on NR UE Power Saving Enhancements (All agreements in RAN4#98-bis-e in email thread #224)
MediaTek, vivo
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2105797
Electronic Meeting, 12th – 20th April, 2021
Agenda Items: 8.9

## Slide 2: General
Issue 1-1: Issues to be further discussed in the work phase
RAN4 should continue to work on the open issues in the work phase, including
  Applicable DRX cycles for relaxation
  The threshold value and/or margins based on further evaluations
  Relaxation factor determination
Other open issues are not precluded.

## Slide 3: Evaluation assumption
Issue 2-1-3: Impact on PDCCH monitoring
RAN4 shall assess the interaction between PDCCH relaxation (as being discussed in RAN1) and RLM/BM relaxation (as being discussed in RAN4) from power consumption perspective once there is more progress in RAN1 on PDCCH relaxation.

## Slide 4: Feasible scenarios for relaxation
RAN4 conclude the feasible scenario and will define the RLM/BFD requirements for R17 UE measurements relaxation for RLM and/or BFD in work phase for the following cases,
  Case 1: SSB based RLM/BFD measurement relaxation in FR1
  Case 2: CSI-RS based RLM/BFD measurement relaxation in FR1
  FFS Case 3: CSI-RS based RLM/BFD measurement relaxation in FR2
  FFS Case 4: SSB based RLM/BFD measurement relaxation in FR2

## Slide 5: Considerations on the feasibility study
Option 1: Negative system level impact due to RLM/BFD relaxation should be minimized e.g. by studying the time of outage with different relaxation factors.
Option 1a: RAN4 should consider the maximum additional delay of RLF declaration within a confidence level due to power saving, i.e., the probability of maximum additional delay within x is larger than y, for power saving evaluation on different schemes.
Option 2: RAN4 needs to study whether the beneficial scenario is a reasonable case for network configuration.

## Slide 6
Issue 2-2-6: DRX cycle applicability
Relaxation is applicable for DRX<=40ms.
  FFS DRX of 80 ms
  FFS adjustment to other DRx cycles is needed to keep the monotonicity of DRx cycles w.r.t. evaluation time
  FFS Maximum relaxation factor should be related to DRX cycle.
Issue 2-2-7: Potential spec impact
  The spec impact of R17 power saving will be discussed in the work phase.

## Slide 7: Relaxation criteria
Issue 2-3-1: Criteria of RLM/BFD relaxation – General
whether relaxed RLM/BFD requirements can be applied depends on both the serving cell quality and UE mobility state
FFS the precise and robust metric for serving cell quality and UE mobility state
Issue 2-3-2/2-3-3: Good serving cell quality criteria of RLM/BFD relaxation
Good serving cell quality criteria of RLM/BFD relaxation is defined as the radio link quality is better than a threshold.
  FFS radio link quality > Qout + X (dB) for RLM
  FFS radio link quality > Qout,LR + Y (dB) for BFD relaxation.
  FFS X, Y
The radio link quality in good serving cell quality criteria for R17 RLM/BFD relaxation is based on SINR
  FFS how to define the metric of SINR
  FFS whether RSRP is also needed for BFD as additional condition

## Slide 8: Issue 2-3-5: Low mobility criteria of RLM/BFD relaxation
Given the this feature is enabled by the network, the low mobility criterion is defined based on
Option A: UE will need to keep verifying whether the low mobility criterion is fulfilled
  Option A1: RSRP variation (reuse R16 low mobility criterion and procedure)
  Option A2: SINR variation
Option B: UE will not need to keep verifying whether the low mobility criterion is fulfilled
  Option B1: UE assumes the low mobility criterion is fulfilled
  Option B2: Network configured whether the low mobility criterion is fulfilled or not
Option C: The low mobility criterion can be left for RAN2 to decide. Send LS to RAN2 to trigger RAN2 discussion.

## Slide 9: Issue 2-3-6: Exiting criteria of RLM relaxation
FFS which of the following options can be used as the exiting criteria of RLM relaxation
Option 1: exit relaxation mode when any relaxation criterion is not met
Option 2: exit relaxation mode when the radio link quality is worse than a certain SINR threshold, which is higher than Qout.
  Option 2a: set different radio link quality threshold for entering and exiting the relaxation
  Option 2b: either the averaged SINR based on reduced number of samples is below Thquit, or the one-shot SINR is below Qout.
Option 3: exit relaxation mode based on out-of-sync indication.
  Option 3a: exit when N310 starts to count, i.e. 1 out-of-sync indication.
  Option 3b: exit when T310 is running witch is triggered by a new counter
  Option 3c: exit when certain number of out-of-indications
  Option 3d: exit when certain consecutive out-of-sync indications
Option 4: Additional time is allowed for UE to evaluate first OOS indication when UE is in power saving mode. UE is in normal mode after first OOS indication. The additional delay for RLF declaration is guaranteed to be within OOS evaluation time (TEvaluate_out_SSB) in normal mode. Relaxation factor and exit SINR threshold (for good cell quality condition) is up to UE implementation, but the “first OOS indication” requirement has to be satisfied.

## Slide 10: Issue 2-3-7: Exiting criteria of BFD relaxation
FFS which of the following options can be used as the exiting criteria of BFD relaxation
Option 1: exit relaxation mode when any relaxation criterion is not met
Option 2: exit relaxation mode when the radio link quality is worse than a certain threshold , which is higher than Qout_LR.
  Option 2a: set different radio link quality threshold for entering and exiting the relaxation
  Option 2b: either the averaged SINR based on reduced number of samples is below Thquit, or the one-shot SINR is below Qout_LR.
Option 3: exit relaxation mode based beam failure instance indication
  Option 3a: exit upon detect 1 beam failure instance indication.
  Option 3b: exit after BFI_COUNTER add to the value of a new counter or a new parameter, the new counter or the new parameter is configured by network.
Other options are not precluded

## Slide 11: Relaxation scheme
Issue 2-4-1: Relaxed evaluation period of RLM/BFD
Scaling factor defining the relaxed RLM/BFD evaluation period is defined based on max(TDRX, TSSB). FFS the following options
Option 1:The similar definition of RLM/BFD evaluation period in Rel-15 can be reused as Max(T, Ceil([Y] x P x N) x Max(TDRX,TSSB))
Option 2: If power saving conditions are satisfied, allow TEvaluate_ps_out_SSB for the first OOS indication and the original TEvaluate_out_SSB doesn’t apply
Configuration | TEvaluate_ps_out_SSB (ms)
no DRX | Max(200, Ceil(10  P)  TSSB)
DRX cycle≤80ms | Max(200, Ceil(30  P)  Max(TDRX,TSSB))
80ms<DRX cycle≤320ms | Max(200, Ceil(20  P)  Max(TDRX,TSSB))
DRX cycle>320ms | Ceil(10  P)  TDRX
NOTE: TSSB is the periodicity of the SSB configured for RLM. TDRX is the DRX cycle length. | 
Configuration | TEvaluate_ps_out_SSB (ms)
no DRX | Max(200, Ceil(10  P)  TSSB)
DRX cycle≤80ms | Max(200, Ceil(15  P)  Max(TDRX,TSSB) + (K-1)  Max(TDRX,TSSB))
80ms<DRX cycle≤320ms | Max(200, Ceil(15  P)  Max(TDRX,TSSB))
DRX cycle>320ms | Ceil(10  P)  TDRX
NOTE: TSSB is the periodicity of the SSB configured for RLM. TDRX is the DRX cycle length, K is the relaxation factor. | 
Option 2a
Option 2b

## Slide 12: Issue 2-4-2: Are the parameters of relaxation criteria predefined or configurable
The parameters of relaxation criteria can be configured by the network.
  Option 1: The relaxation criteria shall be configured by the network to the UE. If the threshold (criteria) is not configured, it means the UE cannot go into relaxation mode.”
  Option 2: The parameters of relaxation criterion of low mobility and entering condition of good cell quality can be configured by the network. Exit condition of good cell quality is FFS.

## Slide 13
Issue 2-4-3: network or UE to determine the relaxation criteria is fulfilled or not
UE determines whether the relaxation criteria can be fulfilled or not.
Issue 2-5-4: Applicability for BFD relaxation requirement
As the legacy BFD requirement, the BFD relaxation requirement is applicable for PCell, PSCell and all configured SCells.

## Slide 14: For information: Observations on the simulation results
On power saving gain:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    With FTP or VoIP model is considered, if L1 measurement intervals for RRM are also extended K times
      For FR1 SSB-based RLM/BFD relaxation with 40ms DRX cycle, at least 3 sources show that the power saving gain is 3.89% to 16.4% for K=2, 13.3% to 20.0% for K=4.
      For FR1 CSI-RS based RLM/BFD relaxation with 40ms DRX cycle, at least 1 source showS that the power saving gain is 4.49% to 6.80% for K=2, 13.41% to 20.34% for K=4
      For FR2 CSI-RS based RLM/BFD relaxation with 40ms DRX cycle, at least 1 source shows that the power saving gain is 5.84% to 9.31% for K=2, 17.79% to 28.63% for K=4.
      For FR1 SSB-based RLM/BFD relaxation with 160ms DRX cycle, at least 1 source show that the power saving gain is 4.95% for K=2, 7.42% for K=4.
    By extending only RLM/BFD measurement interval without reducing RRM measurement samples within RRM measurement period
      At least 2 sources show minimal or no power saving gain.
      Note: Number of RRM measurement samples within RRM measurement period is up to UE implementations
  Therefore, it is concluded that the beneficial scenarios for R17 RLM BFD relaxation are
    When L1 measurement interval for RLM/BFD/RRM can be extended, i.e. number of samples can be reduced, which means SINR is high enough and mobility is low enough, and
    When FTP traffic or Voip traffic is considered, and
    When DRX cycle length is not longer than 80 ms, and
    It is more beneficial if PDCCH-WUS is configured

## Slide 15: For information: Observations on the simulation results
On mobility impact:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    Regarding delta SINR, for FR1 SSB-based RLM OOS relaxation, when DRX cycle is not longer than 80ms
      with mobility of 3 km/h, at least 6 sources show that the delta SINR of max(5%, 95%) is 0.39 dB to 2.15 dB for K=2 , 0.8 dB to 3.02 for K=4, 1.35dB to 4.5dB for K=8.
      with mobility of 30 km/h, at least 3 sources show that the delta SINR of max(5%, 95%) is 1.05 dB to 2.42 dB for K=2 , 2.4 to 5.06 dB for K=4, 3.6 to 7.57 dB for K=8.
    Regarding delta SINR, for FR1 CSI-RS-based RLM OOS relaxation, when DRX cycle is not longer than 80ms
      with mobility of 3 km/h, at least 3 sources show that the delta SINR of max(5%, 95%) is 1.3 dB to 1.5 dB for K=2 , 1.75 dB to 2.08 dB for K=4.
    Regarding delta SINR, for FR2 CSI-RS-based RLM OOS relaxation, when DRX cycle is not longer than 40ms
      with mobility of 3 km/h, at least 2 sources show that the delta SINR of max(5%, 95%) is 1.1 to 3.2 dB for K=2 , 1.27 to 3.8 dB for K=4, 1.4 to 4.2 dB for K=8.
    Regarding delta SINR, for FR2 SSB-based RLM OOS relaxation, when DRX cycle is not longer than 80ms
      with mobility of 3 km/h, at least 2 sources show that the delta SINR of max(5%, 95%) is 1.1 to 1.7 dB for K=2 , 1.69 to 2.67 dB for K=4, 2.05 to 4.87 dB for K=8.
  Therefore, the feasible scenarios for R17 RLM and BFD relaxation are
    When DRX cycle length is not longer than 80 ms, and
    When SINR is above a proper threshold, and
    Either
      when mobility state is below 30km/h for FR1, or,
      when UE speed is less than 3km/h in FR2.

## Slide 16: For information: Observations on the simulation results
On mobility impact:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    Regarding 95%-tile increased RLF latency, for FR1 SSB-based RLM OOS relaxation, when DRX = 40ms
      with mobility of 3 km/h, at least 2 sources show that the increased latency is less than 40ms for K=2, less than 120ms for K=4, and less than 280ms for K=8.
        The increase is less than 2.5% for K=2, less than 7.5% when K=4 and less than 17.5% when K=8, as T310 = 1000ms and N310 = 1.
      with mobility of 30 km/h, at least 2 sources show that the increased latency is less than 40ms for K=2, less than 120ms for K=4, and less than 280ms for K=8 with 95% probability.
        The increase is less than 2.5% for K=2, less than 7.5% when K=4 and less than 17.5% when K=8, as T310 = 1000ms and N310 = 1.
    Regarding averaged increased RLF latency, for FR1 SSB-based RLM OOS relaxation, at least 2 sources show that the averaged increased RLF latency are less than 0.02% for 3km/h mobility and 0.2% for 30km/h, when DRX is not longer than 80ms.