## Slide 1: WF on NR MIMO OTA
vivo, CAICT
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2106092
Electronic Meeting, Apr. 12-20, 2021
Agenda item: 8.1.1
Document for: Approval

## Slide 2: General
Updated Workplan for MIMO OTA WI
  The updated workplan of NR MIMO OTA WI based on the Rel-17 timeline and RAN4 meeting plan is approved [R4-2106096]

## Slide 3: Channel model
FR1 BS antenna element polarization
  Apply Ò polarized antenna model with 45˚ slant angle for FR1 MIMO OTA.
  Use polarization model-2 of section 7.3.2 of TR 38.901 for implementing the +/-45˚ slant angle for FR1 antenna model.
  A TP is needed to add above information into spec next meeting
FR2 BS antenna element polarization
  To provide impact analysis on FR2 BS antenna element polarization type
  Use polarization model-2 of section 7.3.2 of TR 38.901
  FFS for the polarized antenna mode for FR2 MIMO OTA
    Ë polarized antenna model (option 1)
    Ò polarized antenna model with 45˚ slant angle (option 2)
  Infra-vendors are encouraged to provide the feedback on the actual implementation on FR2 BS antenna element polarization
  - Recommendation for FR2 part: keep above proposals as starting point, confirm next meeting.

## Slide 4: Test Method
FR2 blocking issue
  Further study how to address the FR2 blocking issue
  The approach provided by Keysight could be a starting point,
    Three-step simulation/measurement approach to quantify the blocking issue

## Slide 5: Power validation procedure
Update the power validation procedure
  If a horizontally polarized sleeve dipole is used for H component power validation, the horizontal positions should be at least 4.
  A note is needed in the power validation Measurement Procedure: “Note: in step 4, if horizontally polarized sleeve dipole is used, the reference gain correction should be the average of the theta gain pattern cut of the dipole.”
  Correct the mistake of power validation procedure
    For PDP, Doppler, Spatial correlation, and XPR, keep using the sub-bands grouping approach, i.e. same as quality of quite zone
    For power validation, some sub-bands grouping frequencies are not valid, FFS the measurement should be done per-band
      Option 1: Stick to sub-bands grouping approach, redefine some frequencies for power validation only
      Option 2: Change power validation to per-band approach
  The power validation results should be considered as systematic offset, which needs to be used to correct on the final sensitivity value to further reduce measurement uncertainty
Further check the H component measure time with more than 4 averaging (e.g., 8 or 16) is encouraged

## Slide 6: System validation(1)
gNB Beams for Channel model validation
  gNB Beams Usage Criteria for FR1 MIMO OTA Channel Model Validation
    Option 1: Beam specific: (agreed as baseline, to define limits)
    Option 2: Combined beams:
Previous agreements: in WF R4-2103913 RAN4#98e meeting:
  gNB Beams Usage Criteria for FR1 MIMO OTA Channel Model Validation
    Option 1: Beam specific: The two strongest beams are measured separately applied for all channel model validation factors (agreed as baseline, further define validation pass/fail limit based on this approach)
    Option 2: Combined beams: The two strongest beams are combined at the input of the channel emulator for validation of spatial correlation. The PDP validation is done separately for each beam in this case.
  Recommendation: stick to previous agreements.
Notes: OPPO: option 2 aligned with actual test set-up.
vivo: All CE vendors already provide data for option 1 which be helpful for proceeding the work. Option 2 not aligned with actual test set-up. CE vendors’ feeback on implementation required..
Sprient: Option 1 aligned with our assumption.
Keysight: option 2 more favor.
Sprient: With option 2, additional work load expected.

## Slide 7: System validation(2)
Reference curve for Channel model validation
  Reference figure for FR1 spatial correlation validation
    Option 1: Choose simulation curve as reference (previous agreements)
      CE vendors and other companies are encouraged to provide data for generating the reference and further alignment also required.
    Option 2: Choose theoretical curve as reference:
Previous agreements: in WF R4-2017585 RAN4#97e meeting
  Reference figure for channel model validation
    Simulated curve (channel model with BS filtering effect) with limited number of probes (16 probes for FR1 and 6 probes for FR2) is agreed as a reference, to be added into the TR to determine pass fail limits
    Simulated curve (channel model with BS filtering effect) with infinite number of probes is optional to be added
    Simulation results of the reference figure from CE vendors are encouraged next meeting
  Recommendation: stick to previous agreements.

## Slide 8: System validation(3)
Simulated Channel model reference figure
  Reference figure for FR1 channel model validation
    Simulation results have been shared from CE vendors in [R4-2106902，R4-2106097]
    Aligned results from CE vendors and other companies if any on reference channel model curve is required next RAN4 meeting.

## Slide 9: Test Parameters for requirements(1)
Test Parameters for FR1 requirements
  For FR1 2x2 MIMO OTA requirements, the candidate options are:
    Option 1: CDL-A UMi
    Option 2: CDL-C Umi (baseline)
  Note The impact of different channel models on the downlink received power need to be considered
  PRS-EPRE-MAX for band frequency <3GHz, 40MHz bandwidth
    Agreed as -80dBm/15kHz,
    The above value can be modified based on practical measurement in the future
  PRS-EPRE-MAX for band frequency >3GHz, 40MHz bandwidth
    Option 1: -80dBm/15kHz (or equivalent -77dBm/30kHz) (CAICT,vivo,OPPO,Samsung,Xiaomi,MVG)
    Option 2: -79dBm/15kHz (or equivalent -76dBm/30kHz) (Huawei, OPPO,Samsung,QC,MVG)
    The above value can be modified based on practical measurement in the future or missing point requirements can be further modified.
  -Recommendation:
    For FR1 2x2 channel model, select Option2 as baseline for next steps
    For Pmax >3GHz, Option 1 or Option 2 ?
    Note, no matter which option is selected, the above value can be modified based on practical measurement in the future

## Slide 10: Test Parameters for requirements(2)
Test Parameters for FR2 requirements
  RMC for FR2 MIMO OTA: (Background)
    100MHz CHBW with corresponding RMC parameters was selected for FR2 MIMO OTA requirements, which had been captured in the TR 38.827 and TS 38.151
  New proposal was raised last meeting, suggest 200MHz for FR2 Bands, not agreed. Re-discuss this meeting.
  -Recommendation:
    Stick to previous agreement, keep 100MHz RMC for FR2 MIMO OTA requirements and conclude this topic.
    NO further discussion on CHBW parameter for FR2 requirements in RAN4 unless critical issues identified for existing agreements or consensus reached in offline.
Notes: QC: Achievable SNR in Huawei paper is not valid considering the impact of fading. 200MHz is mandatory, but not means we need to follow the largest CHBW, i.e. for FR1, largest 100MHz CHBW is mandatory ,but we only focus on 40MHz, and 10MHz in FR1.
And 200MHz will bring test split for different bands.
Samsung: We already discussed several meetings and technical analysis already provided.

## Slide 11: FR1 MIMO OTA requirements
  FR1 FoM:
    Restriction of Pmode at 90%TP for 10MHz and 40MHz CHBW.
      For 10MHz and 40MHz CHBW, the [10] of total 12 PMODE should reach 90%TP based on the current assumption of PRS-EPRE-MAX value
      The final decision will be concluded during requirement discussion stage

## Slide 12: FR2 MIMO OTA requirements
  FR2 FoM:
    Refinement of MASC calculation
      FR2 MASC is the average of “top N points” instead of “all the values better than 50% percentile of CCDF”.
        Option 1: only consider PC3, N is specified clearly as 18; (in the WID, Smartphone is the first priority); FFS how to handle other PCs
        Option 2: consider all the PCs, specify several N values for each PC; For PC3, N=18, other PCs FFS;
    Additional criterion of FR2 FoM
      The EUT must meet 70% throughput in X points of total 36 3D orientations. If the EUT fails to meet this criterion even under maximum downlink power condition [TBD], the EUT shall fail the FR2 MIMO OTA test.
      If X<18, how to calculate the MASC FFS
      Additional criterion (on other TP outage level) is FFS.
  -Recommendation for MASC calculation:
    Select Option1 or Option 2
    Stabilize the TP R4-2106093, if consensus reached

## Slide 13: FR2 simulation activity
  FR2 simulation to ease the gap:
    The gap between simulation vs measurement should be minimized
      Option 1: Companies should analyse the impact induced by the unaligned channel model parameters between simulation and chamber, i.e. how to reflect the characteristic more close to the condition in a FR2 chamber.
      Option 2:TE vendors to provide a reference probe weights for the 6 probes to facilitate the gap between measurement and simulation
  Specific FR2 simulation parameters for platform alignment between each company
      UE antenna: all options in R4-2103915 can be used? Or only select one ？
      UE beamforming: need to align this parameter for FR2 simulation or not?
      Polarization alignment: need to specify?
  -Recommendation:
    TBD

## Slide 14: Next steps
  Further study the proper Channel model for FR1 2x2 MIMO OTA requirements
  Further discuss the pass/fail limit and reference figure of channel model validation
  Further discuss the DL Pmax for FR1 and FR2
  Measurement results of FR1 or FR2 UEs are encouraged for discussion
  Channel model validation results for FR2 channel models are encourages
  Further discuss how to handle FR2 blocking issue
  Further discuss FR2 simulation