## Slide 1: WF on BS RF TX requirements for 52.6 – 71 GHz
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting # 98-bis-e
Electronic Meeting, 12 – 20 April 2021
Agenda Item: 8.12.5
R4-210xxxx

## Slide 2: Background
Contributions on BS RF TX requirements for 52.6 – 71 GHz in RAN4#98-bis-e have a variety of proposals:
[1] R4-2104456 Proposals on BS transmitter requirements for extending current NR operation to 71 GHz Nokia, Nokia Shanghai Bell
[2] R4-2104731 Discussion on BS TX RF requirements for 52.6-71GHz CATT
[3] R4-2106355 On BS transmitter aspects extending NR to 71 GHz Ericsson
[4] R4-2106589 Discussion on BS Tx requirements for 52.6-71GHz ZTE Corporation
The Way Forward from the discussion of the contributions are summarized in the following slides.

## Slide 3: Way forward on General and output power requirements
The radiated transmitter characteristics requirements applying to the BS type 2-O should be considered as the baseline for NR operation in 52.6 – 71 GHz range.
  Final requirement values need further consideration.
The BS output power for NR operation in 52.6 – 71 GHz range is declared by the manufacturer. Additional regional requirements can be added to specification to align with regulatory requirements.
  Consider further detailed output power accuracy values (EIRP and TRP), taking into account also whether and/or how fractional bandwidth is applied.
Total power dynamic range requirement based on 10*log10(Nrb), similar to current FR2, can be applied to 52.6-71 GHz.
  Details especially on wide channel bandwidths with large SCS and applicability on licensed vs. unlicensed bands need to be further clarified.

## Slide 4: Way forward on Timing and signal quality requirements
Final evaluation of transient times has to consider not only the general ON/OFF mask at start and end slot, for TDD DL/UL boundaries, used in GP timing, but also other use cases related to UE UL, like SRS time mask and PUSCH-PUCCH and SRS time mask. The cases of SRS time mask and PUSCH-PUCCH and SRS time mask have to be investigated in UE RF session.
  Further consider transient time below 3us in case UE transient time is agreed to be shortened too.
Re-use frequency error requirements from current FR2.
New EVM window length is defined for new SCS.
  Further evaluate EVM requirements in 52.6 – 71 GHz range.
Modulations up to 64 QAM are supported.
Further evaluate Tx Off power, considering also whether existing requirement -36 dBm/MHz can be valid.
Further evaluate TAE, considering also impact of UE RF architecture for CA related TAE, if applicable.

## Slide 5: Way forward on Emission requirements
How to handle low emission PSD due to wide carrier BW needs to be studied in RAN4.
For licensed operation, adjust OBUE for 52.6 – 71 GHz.
Further consider EN 303 722 for unwanted emissions in unlicensed operation.
Re-use OTA occupied bandwidth from current FR2.
Further consider whether to derive ACLR based on 70 GHz co-existence study in TR 38.803 or new coexistence study.