## Slide 1
WF on remaining issues for single link tests for NR V2X demodulation performance
3GPP TSG-RAN WG4 Meeting #98-bis-e Electronic Meeting, 12 – 20 April, 2021
Agenda Item: 5.2.1.2
R4-21xxxxx
LG Electronics

## Slide 2: Performance requirements
Impairment results for single link test cases
  The acceptable largest span among the companies’ simulation results to derive performance requirement is 2.5dB
  Handling test cases which alignment results from companies have large span > 2.5dB
    Step 1. Omit results from outliers in the test cases where the span limit can be met by excluding those result
    Step 2. Keep requirements with [ ] for the cases which have larger span > 2.5dB
    Step 3. Allow companies to update results in the next meeting and revise requirement of these test cases.
    Note: Target to remove [ ] for these test cases in the next meeting
Test cases |  | LG | Intel | Huawei | QC | CATT, GOHIGH | MTK | AVE | Margin | Requirement
PSSCH_Test1 (QPSK_TDLA30-2700) |  | 2.73 |  | 2.97 | 3.30 | 2.76 | 2.92 | 2.94 | 0.5 | 3.4
PSSCH_Test2 (16QAM_TDLA30-1400) |  | 7.27 | 8.70 | 8.90 | 9.50 | 7.91 | 7.62 | 8.32 | 0.5 | 8.8
PSSCH_Test3 (64QAM_TDLA30-180) |  | 14.03 | 14.80 | 15.00 | 14.40 | 12.66 | 12.84 | 13.96 | 0.8 | 14.8
PSCCH |  | 4.53 | 5.00 | 4.66 | 3.60 | 3.50 | 3.50 | 4.13 | 0.5 | 4.6
PSBCH |  | -1.82 |  | -1.00 | 0.50 | -0.20 | -2.50 | -1.00 | 0.5 | -0.5
PSFCH |  | 7.48 | 9.70 | 8.36 |  | 9.87 |  | 8.85 | 0.5 | 9.4

## Slide 3: Requirements structure
Table of test parameters and minimum performance
  Add the information for bandwidth/SCS and propagation condition in the table of minimum performance
  Remove the information for 2nd stage SCI configuration, bandwidth/SCS, and propagation condition in the table of test parameters
  Add the information of the number of DMRS symbols in test parameter table for PSSCH test case
RMC table for PSSCH
  Reference measurement channels are defined for different physical channels like LTE V2X
  Remove information about number of DMRS symbols and keep only information about number of DMRS REs
  Add information about overhead for TBS determination (e.g., Overhead for TBS determination = 0)
  Add SCI2 configuration which is required for calculation of number of resource elements
  Add the number of REs allocated for SCI1 transmission

## Slide 4: Requirements structure
Resource pool configuration
  Capture common parameters into General section of V2X requirements as below
Parameter |  | Unit | Value
Carrier configuration | Offset between Point A and the lowest usable subcarrier on this carrier (Note 1) | RBs | 0
 | Subcarrier spacing | kHz | 30
SL BWP configuration #1 | Cyclic prefix |  | Normal
 | RB offset | RBs | 0
 | Number of contiguous PRB | PRBs | Maximum transmission bandwidth configuration as specified in clause 5.3.2 of TS 38.101-1 [6] for tested channel bandwidth and subcarrier spacing
PT-RS configuration |  |  | PT-RS is not configured
Resource pool configuration | PSCCH Time resource | Symbols | 2
 | PSCCH Frequency resource | PRBs | 10
 | PSFCH number of cyclic shift pairs |  | n1
 | PSFCH hopping ID |  | 0
 | PSFCH candidate resource type |  | allocSubCH
 | Set of PRBs for PSFCH transmission |  | ones(1,100) for 40 MHz and ones(1,50) for 20 MHz
 | PSSCH RSRP threshold |  | 66 (infinity dBm)
 | Synchronization reference |  | GNSS
 | Subchannel size | PRBs | 10
 | Number of sub-channels |  | 5 for 20 MHz and 10 for 40 MHz
 | Start PRB for first sub-channel |  | 0
 | Time resource bitmap |  | ones(1, 160)
Note 1: Point A coincides with minimum guard band as specified in Table 5.3.3-1 from TS 38.101-1 [6] for tested channel bandwidth and subcarrier spacing. |  |  |