## Slide 1: WF on IAB demod editorial

## Slide 2: Section numbering IAB-DU
8.1 IAB DU requirements
  8.1.1 General
  8.1.2 Performance requirements for PUSCH
    8.1.2.1 Performance requirmements for PUSCH with transform precoding disabled
    8.1.2.2 Performance requirmements for PUSCH with transform precoding disabled
    8.1.2.3 Performance requirements for UCI multiplexing on PUSCH
  8.1.3 Performance requirements for PUSCH
    8.1.3.1 DTX to ACK probability
    8.1.3.2 Performance requirements for PUCCH format 0
    8.1.3.3 Performance requirements for PUCCH format 1
    8.1.3.4 Performance requirements for PUCCH format 2
    8.1.3.5 Performance requirements for PUCCH format 3
    8.1.3.6 Performance requirements for PUCCH format 4
    8.1.3.7 Performance requirements for multi-slot PUCCH
  8.1.4 Performance requirements for PRACH
    8.1.4.1 PRACH false alarm probability
    8.1.4.2 PRACH detection requirements

## Slide 3: Section numbering IAB-MT
8.2 IAB MT requirements
  8.2.1 General
  8.2.2 Performance requirements for IAB-MT demodulation
    8.2.2.1 Performance requirements for PDSCH
    8.2.2.2 Performance requirements for PDCCH
  8.2.3 Performance requirements for IAB-MT CSI reporting
    8.2.3.1 CQI reporting
    8.2.3.2 PMI reporting
    8.2.3.3 RI reporting
    NOTE: The above sub-sections could be collapsed to 8.2.3 and 8.2.3 could refer to CQI, not CSI reporting in case it is agreed to do CQI only.
    Note: Do not include any sub-levels for TDD/FDD

## Slide 4: Section numbering
The previous pages are a top level order of requirements for both the core and conformance specifications
General Sub-headings for core spec:
  8.x.x.x Performance requirements for xxx
    8.x.x.x.1 General
    8.x.x.x.2 Minimum requirement
  Some extra sections required for IAB-DU PRACH for ACK to NACK, ACK missed detection etc... Follow the section ordering as in 38.104
General Sub-headings for conformance spec:
  8.x.x.x Performance requirements for xxx
    8.x.x.x.1 Definition and applicability
    8.x.x.x.2 Minimum requirement
    8.x.x.x.3 Test purpose
    8.x.x.x.4 Method of test
    8.x.x.x.4.1 Initial conditions
    8.x.x.x.4.2 Test procedure
    8.x.x.x.4.3 Test requirement

## Slide 5: Annexes
Core spec:
Annex A FRCs
Conformance spec:
Annex A FRCs
Annex [C.3] Performance test tolerances
  List both IAB-DU and IAB-MT TTs in the same table of test tolerances
Annex [D.6] Measurement set-up IAB-MT and IAB-DU performance requirements
  [D.6].1 PUSCH and PUCCH single antenna port in multipath fading
  [D.6].2 2 antenna port PUSCH, PDCCCH, PDSCH in multi-path fading
  [D,6].3 PUSCH, PRACH, CSI in static AWGN
Annex [G] Propagation conditions
  Please review R4-2104660 which attempts to merge and simplify the UE and BS annexes on this topic as a baseline structure for this annex

## Slide 6: FRC Annex guidance
The following slides indicate in detail the order and numbering of annexes for FRCs
  The slides indicates firstly the Annex number, then in which order the FRC tables are presented within the Annex
IAB-DU FRCs are named with the convention G-FRx-Ay-z
  X is the FR number (FR1 or FR2)
  Y is the Annex number
  Z increments by 1 for each new FRC in the Annex, starting from 1 for the first FRC in the annex
IAB-DU FRCs are named with the convention M-FRx-Ay-z
  X is the FR number (FR1 or FR2)
  Y is the Annex number
  Z increments by 1 for each new FRC in the Annex, starting from 1 for the first FRC in the annex
By following this guidance, the FRC ordering and naming can be co-ordinated between all core and conformance specs.

## Slide 7: FRC Annexes and ordering (1)
A.2 Fixed Reference Channels for IAB-DU performance requirements (QPSK, R=193/1024)
  The parameters for the reference measurement channels are specified in table A.2-1 and table A.3-2 for FR1 PUSCH performance requirements:
  - FRC parameters are specified in table A.2-1 for FR1 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 1 transmission layer.
  - FRC parameters are specified in table A.2-2 for FR1 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 2 transmission layers.
  - FRC parameters are specified in table A.2-3 for FR1 PUSCH with transform precoding enabled, Additional DM-RS position = pos1 and 1 transmission layer.
  The parameters for the reference measurement channels are specified in table A.3-5 to table A.3-10 for FR2 PUSCH performance requirements:
  - FRC parameters are specified in table A.2-4 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos0 and 1 transmission layer.
  - FRC parameters are specified in table A.2-5 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos0 and 2 transmission layers.
  - FRC parameters are specified in table A.2-6 for FR2 PUSCH with transform precoding enabled, Additional DM-RS position = pos0 and 1 transmission layer.
  - FRC parameters are specified in table A.2-7 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 1 transmission layer.
  - FRC parameters are specified in table A.2-8 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 2 transmission layers.
  - FRC parameters are specified in table A.2-9 for FR2 PUSCH with transform precoding enabled, Additional DM-RS position = pos1 and 1 transmission layer.
  - FRC parameters are specified in table A.2-10 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 1 transmission layer.

## Slide 8: FRC Annexes and ordering (2)
A.3 Fixed Reference Channels for IAB-DU performance requirements (16QAM, R=658/1024)
  The parameters for the reference measurement channels are specified in table A.3-1 and table A.3-2 for FR1 PUSCH performance requirements:
  - FRC parameters are specified in table A.3-1 for FR1 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 1 transmission layer.
  - FRC parameters are specified in table A.3-2 for FR1 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 2 transmission layers.
  The parameters for the reference measurement channels are specified in table A.3-3 to table A.3-6 for FR2 PUSCH performance requirements:
  - FRC parameters are specified in table A.3-3 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos0 and 1 transmission layer.
  - FRC parameters are specified in table A.3-4 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos0 and 2 transmission layers.
  - FRC parameters are specified in table A.3-5 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 1 transmission layer.
  - FRC parameters are specified in table A.3-6 for FR2 PUSCH with

## Slide 9: FRC Annexes and ordering (3)
A.4 Fixed Reference Channels for IAB-DU performance requirements (64QAM, R=567/1024)
  The parameters for the reference measurement channels are specified in table A.4-1 for FR1 PUSCH performance requirements:
  - FRC parameters are specified in table A.4-1 for FR1 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 1 transmission layer.
  The parameters for the reference measurement channels are specified in table A.4-2 to table A.4-3 for FR2 PUSCH performance requirements:
  - FRC parameters are specified in table A.4-2 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos0 and 1 transmission layer.
  - FRC parameters are specified in table A.4-3 for FR2 PUSCH with transform precoding disabled, Additional DM-RS position = pos1 and 1 transmission layer.

## Slide 10: FRC annexes and ordering (4)
A.5 IAB-DU PRACH Test preambles

## Slide 11: FRC annexes and ordering (5)
A.6 Fixed Reference Channels for IAB-DU performance requirements (16QAM, R=434/1024)
  The parameters for the reference measurement channels are specified in table A.6-1 for FR2 PUSCH performance requirements with transform precoding disabled, additional DM-RS position = pos0 and 2 transmission layers.
  The parameters for the reference measurement channels are specified in table A.6-2 for FR2 PUSCH performance requirements with transform precoding disabled, additional DM-RS position = pos1 and 2 transmission layers.

## Slide 12: FRC annexes and ordering (6)
A.7 Fixed Reference Channels for IAB-MT PDSCH performance requirements (16QAM)
  The parameters for the reference measurement channels are specified in table A.7-1 for FR1 PDSCH performance requirements.
  The parameters for the reference measurement channels are specified in table A.7-2 for FR2 PDSCH performance requirements.

## Slide 13: FRC annexes and ordering (7)
A.8 Fixed Reference Channels for IAB-MT PDSCH performance requirements (64QAM)
  The parameters for the reference measurement channels are specified in table A.8-1 for FR1 PDSCH performance requirements.
  The parameters for the reference measurement channels are specified in table A.8-2 for FR2 PDSCH performance requirements.

## Slide 14: FRC annexes and ordering (8)
A.9 Fixed Reference Channels for IAB-MT PDSCH performance requirements (256QAM)
  The parameters for the reference measurement channels are specified in table A.9-1 for FR1 PDSCH performance requirements.

## Slide 15: FRC annexes and ordering (9)
A.10 Fixed Reference Channels for IAB-MT PDCCH performance requirements
  The parameters for the reference measurement channels are specified in table A.10-1 for FR1 PDCCH performance requirements.
  The parameters for the reference measurement channels are specified in table A.10-2 for FR2 PDCCH performance requirements.

## Slide 16: FRC annexes and ordering (10)
A.11 Fixed Reference Channels for IAB-MT CSI requirements

## Slide 17: Other editorial issues
Remove all references to FDD
Do not create sub-headings for duplex mode (only TDD is used)
Do not create sub-headings for number of RX antennas; just capture using separate tables in the same sub-section.