## Slide 1: WF on Rel-16 NR IAB demodulation requirements
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic Meeting, 12th – 20th April, 2021
Agenda: 5.3.5
draftR4-2106088
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
The following WFs were approved previously
  R4-2012644, WF on Rel-16 NR IAB demodulation requirements, RAN4#96-e.
  R4-2017673, WF on Rel-16 NR IAB demodulation requirements, RAN4#97-e.
  R4-2103994, WF on Rel-16 NR IAB demodulation requirements, RAN4#98-e.
Corresponding Email summary in RAN4#98-bis-e
  R4-2106141, Email discussion summary for [98-bis-e][319] NR_IAB_Demod.

## Slide 3: IAB-DU - PUSCH
MCS/SCS applicability rule clarification
  Clarify PUSCH MCS/SCS applicability rule: If IAB-DU supports more than 1 SCS then highest modulation order is tested only with lowest supported SCS and other modulation orders only with highest supported SCS. Otherwise all modulation orders are tested on supported SCS.

## Slide 4: IAB-DU - PUCCH
Multi-slot inclusion
  Option 1: Include multi-slot PUCCH cases and keep existing BS demodulation-based test applicability rule (“multi-slot PUCCH requirement tests shall apply only if the BS supports it”).
  Option 2: Skip cases for multi-slot PUCCH.
Applicability rule on number of test cases and formats
  For each supported PUCCH format, only choose one SCS to be tested if multiple SCSs supported.
  Keep all (Rel-15) PUCCH formats’ requirements in the specification

## Slide 5: IAB-DU - PRACH
Formats to be included in IAB-DU specification
  Include all PRACH formats. Copy all requirements for all PRACH formats (excluding high speed configurations
Test applicability
  All existing requirements and applicability rules for PRACH should be re-used for IAB-DU and corresponding declaration on supporting of this feature should be defined. The following new one applicability rule should be added: “For IAB-DU declares to support more than one PRACH formats, limit the number of tests to any two cases chosen by the manufacturer. If IAB-DU declares to support more than one PRACH formats where formats for both long and short PRACH sequences are presented, require choosing formats with different sequences.
  Note: This approach only applicable for IAB-DU PRACH test cases introduced in Rel-16, and this approach should not be considered as a generic approach

## Slide 6: IAB-MT - General
Reference signals in test parameters and reference channels
  Option 7 (GtW): Baseline:
    Do not define SSB, TRS, CSI-RS configurations as a part of demodulation performance test parameters or FRC. CSI reporting is exempt from the CSI-RS configuration omission.
    Add the following notes to the FRCs:
      Note 1: PDSCH/PDCCH is transmitted only in D slots that do not contain CSI-RS, SSB and TRS.
    Remove SSB, TRS, CSI-RS configurations rows from demodulation performance test parameters and the following note in test parameter table(s):
      Note X:SSB, TRS and/or CSI-RS and other unspecified test parameters in TS 38.101-4 are left to test implementation if [transmitted/needed].
  Option 8 (Moderator): Baseline:
    Do not define SSB, TRS, CSI-RS configurations as a part of demodulation performance test parameters or FRC. CSI reporting is exempt from the CSI-RS configuration omission.
    Add the following notes to the FRCs:
      Note 1: PDSCH/PDCCH is transmitted only in D slots that do not contain CSI-RS, SSB and TRS.
    Remove SSB, TRS, CSI-RS configurations rows from demodulation performance test parameters and the following note in test parameter table(s):
      Note X: SSB, TRS, CSI-RS, and/or other unspecified test parameters with respect to TS 38.101-4, are left up to test implementation, if they are transmitted.
  Tentative agreement Baseline:
    Do not define SSB, TRS, CSI-RS configurations as a part of demodulation performance test parameters or FRC. CSI reporting is exempt from the CSI-RS configuration omission.
    Add the following notes to the FRCs:
      Note 1: PDSCH/PDCCH is transmitted only in D slots that do not contain CSI-RS, SSB and TRS.
    Remove SSB, TRS, CSI-RS configurations rows from demodulation performance test parameters and the following note in test parameter table(s):
      Note X: Transmission of SSB, TRS, CSI-RS is not mandated. SSB, TRS, CSI-RS, and/or other unspecified test parameters with respect to TS 38.101-4, are left up to test implementation, if needed.

## Slide 7: IAB-MT - General
Down scoping and changing of propagation conditions
  Replace propagation conditions (FR1: TDLC300-100 -> TDLA30-10; FR2: TDLA30-300 -> TDLA30-75) and provide simulation results for alignment.
  Tentative agreement
    If less than 3 companies provide results within a span of 2.5 dB the results are considered to be misaligned. FFS: Consequences of misalignment are:
      Option 6a): Requirements remain in square brackets.
      Option 6b): Add extra margin.
      Option 6c): Copy-paste requirements from UE specification.

## Slide 8: IAB-MT - General
OCNS model for unused REs
  FRC
    Define single slot PDSCH FRC so that symbols containing PDSCH contain only PDSCH and DM-RS and with all REs allocated.
  PDSCH
    No need for OCNS for PDSCH.
  PDCCH
    Option 1: Include OCNS/OCNG for PDCCH.
    Option 2: Do not include OCNS/OCNG for PDCCH.
    Option 3: Do not specify OCNS/OCNG for PDCCH.
    Tentative agreement: Option 3.
Test tolerances
  Option 1: TT=0.3dB for static channel, TT=0.6dB for fading channel for both conducted and radiated testing.
  Option 2: Reuse UE TT values from TS 38.521-4.

## Slide 9: IAB-MT - PDSCH
PRB bundling size
  Option 1: Keep prior agreements that only keep requirements with PRB bundling size 2. Do not re-simulate the rank 3 case.
  Option 2: Keep prior agreements that only keep requirements with PRB bundling size 2. For rank 3 case, change PRB bundling size from wideband to 2 and re-simulate that case.
  Option 3: Change prior agreement and re-use FR1 Rank 3 4Rx UE requirement (16QAM, TDLA30-10) for IAB-MT with wideband PRB bundling.
  Tentative agreement: Option 2.
PDCCH resources
  Do not to define PDCCH configuration in PDSCH test parameters.

## Slide 10: IAB-MT - PDCCH
Simulation alignment
  Option 1: Discuss if reported PDCCH results can be agreed to be consistent.
  Option 2: Other options not precluded.
  Proposed WF: Come back in next meeting.

## Slide 11: IAB-MT - CSI reporting
PMI inclusion
  Option 1: Include PMI requirements, and a declaration of PMI support.
  Option 1a: Include PMI requirements, and test them if PMI usage is declared.
  Option 2: Do not introduce PMI requirements.
PMI CSI-RS Resource type and report config
  “Adopt PMI reporting requirements as they exist in 38.101-4”, means to take the same gamma values from 38.101-4.
  FFS
    Option 1: Adopt PMI reporting requirements as they exist in 38.101-4.
    Option 2: Test parameters should be still updated to be compliant with the BS testing approach. Periodic CSI-RS resource and reporting type is preferred.

## Slide 12: IAB-MT - CSI reporting
RI inclusion
  Option 1: Include RI requirements, and a declaration of RI support.
  Option 2: Do not introduce RI requirements.
RI CSI-RS Resource type and report config
  Option 1: Adopt RI reporting requirements as they exist in 38.101-4.
  Option 2: Other options not precluded.
CSI configurations
  Define CSI-RS configurations for IAB-MT CSI reporting tests. Follow configurations from UE testing.
PDCCH configuration
  Not define PDCCH configuration for CSI reporting tests.
Reporting channel
  Do not define the physical channel for the CSI report and leave it up to the implementation.