## Slide 1: WF on FR2 HST Deployment Scenario Analysis
Samsung
3GPP TSG-RAN WG4#98-bis-e Meeting R4-2106100
Electronic Meeting, 12th – 20th April, 2021

## Slide 2: Way Forward – General Assumption (1/2)
RRH and UE Antenna Element Assumption
  For each panel in UE:
      Option-1: N=4, M=4 with 2 polarization
      Option-2: N=8, M=4 with 2 polarization
      Option-3: N=2, M=4 (or N=4, M=2) with 2 polarization
  For antenna array configuration in RRH：
      Option-1: [Mg, Ng, M, N, P]=[1, 1, 4, 8, 2]
      Option-2: [Mg, Ng, M, N, P]=[1, 1, 8, 8, 2]
      Option-3: [Mg, Ng, M, N, P]=[1, 1, 8, 16, 2]
Agreement in GTW Session (15th April, Thursday)
  RRH side:
    Option-2: [Mg, Ng, M, N, P]=[1, 1, 8, 8, 2]
  UE side:
    Option 1: N=4, M=4 with 2 polarizations as starting point, and other options not precluded pending on further discussion
    RF session can trigger relevant discussion on RF requirements taking above agreements into account.

## Slide 3: Way Forward – General Assumption (2/2)
UE antenna panel(s) for forward and backward directions
  RAN4 to consider CPE to be equipped with two panels pointed forward and backward along the track.
    Detailed boresight directions of each panel can be adjusted based on companies’ analysis.
Number of CPE devices per train/carriage
  RAN4 requirement can be defined based on the baseline of 1 CPE device per train
Necessity of JT in Scenario-A/B, for both Uni/Bi-directional RRH
  Only DPS transmission mode considered for FR2 HST
    Joint Transmission (full SFN) is precluded.
RRH/UE boresight direction of Antenna Panel and beam direction
  RAN4 may not need to specify RRH/UE boresight direction of antenna panel and beam direction for deployment scenario study, but left for companies’ choice:
    RRH/UE boresight direction of antenna panel and beam direction information can be provided by individual company to accompany their deployment scenario analysis result, which can be captured in TR.

## Slide 4: Way Forward – Scenario-A, Uni-directional (1/3)
Number of Beam for uni-directional RRH deployment, Scenario-A
  For scenario-A, uni-directional, RRH parameter:
    1 beam per RRH panel
  For scenario-A, uni-directional, UE parameter:
    Agreement in GTW Session (15th April, Thursday)
      1 beam per panel;
      2 panels assumed to be implemented in the UE side;
      Only the one active panel per UE can be used for Tx and Rx; and FFS whether another panel can be used for beam search

## Slide 5: Way Forward – Scenario-A, Uni-directional (2/3)
Beam RRH switching point for uni-directional RRH deployment, Scenario-A
  RRH switching point is where the UE switches from the source RRH beam to the target (nearest) RRH beam based on maximizing SNR among detected beams.
  Ds_offset: the relative offset distance of RRH switching point to the nearest RRH site location
    Ds_offset is in the range of [40-81]m.
    FFS the value of Ds_offset
    Ds_offset could be used to derive channel model for performance requirement.

## Slide 6: Way Forward – Scenario-A, Uni-directional (3/3)
Background: Potential Handover issue identified
  UE half cone coverage of antenna arrays on one panel is between 0 to 60 degrees on azimuthal plane, which leads to coverage hole from RRH beams when UE is passing the RRH.
  When UE pass the coverage hole region, it lack of coverage from the neighboring cell until the neighboring cell suddenly has much larger power than the serving cell, which may fail the handover procedure.
  RAN4 to study the resolution to the potential whether there is any handover issue in uni-directional model with small Ds. . In case a handover issue is confirmed, study how to resolve it.
T0
CID =1
CID =2
CID =2
HO

## Slide 7: Way Forward – Scenario-A, Bi-directional (1/2)
Background:
  Schemes for Bi-directional deployment:
    Two schemes are proposed to solve “RRH-site” coverage issue for bi-directional deployment
For Scenario-A Bi-directional RRH deployment:
  FFS the benefits with bi-directional deployment compared to uni-directional deployment;
  FFS the potential issue of coverage when close to RRH locations.
  Scheme-2 can be used as starting points for further analysis
Scheme-1: Connecting to 2nd-Nearest RRH
Scheme-2: Connecting to Nearest RRH except Coverage Hole

## Slide 8: Way Forward – Scenario-A, Bi-directional (2/2)
Number of Beam for bi-directional RRH deployment, Scenario-A:
  For scenario-A, bi-directional, RRH parameter:
    1 beam per RRH panel, two panels in opposite directions
    FFS one additional beam per RRH site needed to cover neighboring RRH site.
  For scenario-A, bi-directional, UE parameter:
    1 beam per UE panel (i.e., 2 beam per UE)
Beam dwelling time for bi-directional RRH deployment, Scenario-A:
  FFS the beam dwelling time by assuming UE maximum speed of 350kmph.

## Slide 9: Way Forward – Scenario-B, Uni-directional
Number of Beam for uni-directional RRH deployment, Scenario-B
  For scenario-B, uni-directional, RRH parameter:
    Option-1: 1 beam per RRH panel
    Option-2: 2 beam per RRH panel
    Option-3: 3 beam per RRH panel
    Option-4: 4 beam per RRH panel
    Note: uneven separation between beams can be considered
  For scenario-B, uni-directional, UE parameter:
    Number of beam(s) per UE panel
      Option 1: 1 beam per UE panel
      Option 2: 2 beams per UE panel
      Option 3: 7 beams per UE panel
    2 panels assumed to be implemented in the UE side;
    Only the one active panel per UE can be used for Tx and Rx; and FFS whether another panel can be used for beam search
RRH Beam switching point for uni-directional RRH deployment, Scenario-B
  Ds_offset: the relative offset distance of RRH switching point to the nearest RRH site location
    FFS the value of Ds_offset
    Ds_offset could be used to derive channel model for performance requirement.
  Beam dwelling time for uni-directional RRH deployment, Scenario-B:
  FFS the beam dwelling time by assuming UE maximum speed of 350kmph.

## Slide 10: Way Forward – Scenario-B, Bi-directional
FFS the benefits with bi-directional deployment compared to uni-directional deployment
Schemes for Bi-directional deployment:
  FFS how to solve coverage issue around RRH-site for bi-directional Scenario-B.
Number of Beam for bi-directional RRH deployment, Scenario-B
  For scenario-B, bi-directional, RRH parameter:
    Option-1: 1 beam per RRH panel
    Option-2: 2 beam per RRH panel
    Option-3: 3 beam per RRH panel
    Option-4: 4 beam per RRH panel
    Note: uneven separation between beams can be considered
  For scenario-B, uni-directional, UE parameter:
    Number of beam(s) per UE panel
      Option 1: 1 beam per UE panel
      Option 2: 2 beams per UE panel
      Option 3: 7 beams per UE panel
    2 panels assumed to be implemented in the UE side;
    Only the one active panel per UE can be used for Tx and Rx; and FFS whether another panel can be used for beam search
  Beam dwelling time for bi-directional RRH deployment, Scenario-B:
  FFS the beam dwelling time by assuming UE maximum speed of 350kmph.

## Slide 11: Way Forward – Necessity of Signaling
FFS the necessity of signaling for FR2 HST:
  FFS UE capability signaling to support uni-/bi-directional RRH deployment
  FFS NW signaling to indicate uni-/bi-directional RRH deployment to assistant UE RRM and/or Demod operation
  Other options are not precluded.

## Slide 12: Way Forward – Others (1/2)
Track curvature and impact on RRH separation:
  FFS its impact on performance.
  1 RRH site per BBU
  RAN4 to consider regular (non-SFN/non-DPS) deployment with 1 RRH site per BBU:
    To be considered with low priority;
    Analysis baseline is still 4 RRH site per BBU
  High difference in propagation delays
  RAN4 to elaborate further on which deployment scenarios are exposed to the very different propagation delays.
    Quantitively evaluate the implications in these scenarios both from the demodulation and RRM perspectives.
    RAN4 should study whether there is any scenario with ISI and signal power degradation, and study a scheme to alleviate if needed. RAN4 needs to study the scheme to alleviate ISI and the requirement should take signal power degradation into consideration.

## Slide 13: Way Forward – Others (2/2)
Dedicated network for roof-mounted CPE:
  RAN4 to assume that in HST FR2 Scenario A, only high-speed CPEs installed on the roof of the train can be present in the network.
  FFS Scenario B.
    RAN4 to clarify based on the operators’ input if regular (i.e., low-speed non-HST) UEs can be connected to the same cell together with a HST CPE moving at maximum speed.
  Handheld UE for FR2 HST
  RAN4 focus on roof-mounted CPE in Rel-17 WI.

## Slide 14: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2104905 | FR2 HST deployment scenario discussion | Qualcomm, Inc.
R4-2104679 | On HST deployment aspects in scenario A | Ericsson
R4-2104924 | NR support for high speed train scenario in FR2 - Deployment Scenario-A | ZTE Corporation
R4-2105023 | Discussion on FR2 HST Deployment Scenario-A | Samsung
R4-2106503 | Discussion on FR2 HST deployment aspects | Intel Corporation
R4-2106693 | On HST FR2 Deployment Scenario A | Nokia, Nokia Shanghai Bell
R4-2106826 | Discussion on NR FR2 HST deployment Scenario-A | Huawei, HiSilicon
R4-2104680 | On HST deployment aspects in Scenario B | Ericsson
R4-2104926 | NR support for high speed train scenario in FR2 - Deployment Scenario-B | ZTE Corporation
R4-2105024 | Discussion on FR2 HST Deployment Scenario-B | Samsung
R4-2106694 | On HST FR2 Deployment Scenario B | Nokia, Nokia Shanghai Bell
R4-2106827 | Discussion on NR FR2 HST deployment Scenario-B | Huawei, HiSilicon
R4-2104678 | Channel model for FR2 HST scenario | Ericsson
R4-2105025 | Channel modeling for FR2 HST and TP to TR 38.854 | Samsung
R4-2106828 | Discussion on channel modeling for NR FR2 HST | Huawei, HiSilicon
R4-2106911 | On HST FR2 Channel Modelling | Nokia, Nokia Shanghai Bell
R4-2104677 | On available capacity and the number of UE per train | Ericsson
R4-2104925 | Other considerations for HST_FR2 | ZTE Corporation

## Slide 15: Reference
[1] R4-2106146, “Email discussion summary for [98-bis-e][322] NR_HST_FR2_Scenarios_Demod”, Samsung