## Slide 1: 3GPP TSG-RAN WG4 Meeting #98bis-e R4-210xxxx Electronic Meeting, Apr. 12th – 20th, 2021
Huawei, HiSilicon
Way forward on PUSCH 256QAM performance requirements

## Slide 2
Agreements:
Applicability for PUSCH 256QAM demodulation performance requirements: Only applied for BS manufacturers declaring that uplink 256QAM is supported.
MCS: Evaluate {MCS24, MCS22} as starting point for next meeting, based on the simulation results to decide if MCS24 is feasible, otherwise to check lower MCS22 is feasible or not.
TDD pattern:
  15kHz SCS: 3D1S1U, S=10D:2G:2U
  30kHz SCS: 7D1S2U, S=6D:4G:4U
Applicability rules for TDD with different TDD patterns: Reuse the existing applicability rules defined in section 8.1.2.1.5 of TS 38.141-1
PUSCH start symbol and symbol length: S = 0, L=14.
Frequency domain allocation: Full bandwidth frequency domain resource allocation
DM-RS type: Type 1 with single-symbol DM-RS.
Additional DM-RS (dmrsAdditionalPosition): pos1, FFS pos2
  Decide based on interesting companies’ feedback for next meeting
PT-RS configuration: FFS configure PT-RS.
  Two companies would like to study the PN impact to demodulation for 256QAM, we can discuss and decide to whether to configure PT-RS or not based on interesting companies’ feedback from all companies in next meeting.
Phase Noise modelling:
  Realistic phase noise modelling is left up to the contributing entities.
  Phase noise impact can be either considered in ideal simulations or included in impairment results based on further discussion and evaluations.
  Interesting company is welcome to do investigation on the PN impact on 256QAM performance for next meeting.

## Slide 3
Agreements:
Number of HARQ transmission and RV sequence: 4 HARQ transmission with RV sequence {0,2,3,1}.
Tx EVM:
  Interesting companies are welcome to check the performance difference with and without Tx EVM (3.5% as baseline) impact considered.
  RAN4 will discuss and decide whether additional margin should be considered in alignment results if no Tx EVM modelling in next meeting as per the evaluations results.
Test metric: 70% max throughput.
Other test parameters:
  CP: Normal
  SRS: Not configured
  Number of DM-RS CDM groups with data: 2
  Ratio of PUSCH EPRE to DM-RS EPRE: -3dB
  DM-RS sequence generation: NID=0, nSCID=0
  Frequency hopping: Disabled
  CBG-based PUSCH transmission: Disabled
  Timing offset: 0
  Frequency offset: 0
  Limited buffer rate matching: Disabled.

## Slide 4
Agreements:
Waveform:
  CP-OFDM only.
Propagation condition:
  TDLA30-10 Low
  PUSCH mapping type
  Type A and Type B with reusing the existing applicability rule defined in section 8.1.2.1.3 of TS 38.141-1
FRC: Discuss the FRC after MCS, DM-RS pattern, BW and Rank are finalized.

## Slide 5
Open issues:
Number of Tx:
  Option 1: Only 1Tx
  Option 2: Both 1Tx and 2Tx
Number of Rx:
  Option 1: 2/8 Rx
  Option 2: 2/4/8 Rx
Number of layers:
  Option 1: Only 1 layer
  Option 2: Both of 1 and 2 layers
  SCS and bandwidth
  15kHz SCS:
    - Option 1:5MHz and 10MHz
    - Option 2: 5MHz, 10MHz and 20MHz.
  30kHz SCS
    - Option 1:10MHz and 40MHz
    - Option 2:10MHz, 20MHz, 40MHz and 100MHz.
  Applicability rule for different antenna configurations
  Option 1: Reuse the existing test applicability rule defined in clause 8.1.2.0 of TS38.141-1
  Other options
  Applicability rules for different SCS and CBW
  Option 1: Reuse the existing applicability rules defined in sections 8.1.2.1.1 and 8.1.2.1.2 of TS 38.141-1
  Other options.