## Slide 1: WF on agreements and remaining issues with FR2 test method enhancements
Apple
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic Meeting, April 12th – 20th, 2021
Agenda Item: 9.1.1
R4-2106127

## Slide 2: Background (1)
The following issues related to FR2 test method enhancements were identified in the email discussion [28]:
  Issue 1-1-1: Determining the unknown antenna location in CFFNF setup
  Issue 1-1-2: CFFNF test procedure and rationale
  Issue 1-1-3: CFFNF MU elements
  Issue 1-1-4: Preliminary assessment of CFFNF MU
  Issue 1-2-1: CFFDNF MU elements
  Issue 1-2-2: Preliminary assessment of CFFDNF MU (EIRP/EIS test cases)
  Issue 1-2-3: Preliminary assessment of CFFDNF MU (TRP test cases)
  Issue 1-3-1: Applicability of the DNF setup
  Issue 1-4-1: Clear summary of applicable enhancements

## Slide 3: Background (2)
List of issues continued from last slide:
  Issue 2-1-1: TPMI method
  Issue 2-1-2: 2-port CSI-RS
  Issue 2-1-3: Other methods
  Issue 2-2-1: EVM measurement setup (2L MIMO)
  Issue 2-2-2: EVM measurement setup (1L MIMO)
  Issue 2-2-3: EVM measurement parameters
  Issue 4-1-1: Applicability of ETC
  Issue 4-1-2: ETC MU
  Issue 5-1-1: New measurement grid (1-MG)
  Issue 5-1-2: RSRP(B) based RX beam peak search (2-RSRP)
  Issue 5-1-3: 3-Single Pollink
  Issue 5-1-4: Fast Spherical Coverage Method
  Issue 6-1-1: Band-dependent parameters for the demodulation setup

## Slide 4: (Obj 1) Antenna location and rationale of the CFFNF setup
NOTE: outcome of Issues 1-1-1 and 1-1-2
Tentative agreement
  Antenna location for the black&white box approach can be based on manufacturer declaration as a baseline
    To be captured in the TR as part of the detailed test procedure and rationale of the CFFNF system (see Issue 1-1-2): a TP is needed for RAN4 #99-e
    For this method the contribution to MU is:
      Option 1: covered by estimation of DUT antenna location (Issue 1-1-3, Alt 1-1-3-4)
      Option 2: FFS
  Antenna location for the black box approach can be based on the three radii method
    Approach to determine the unknown phase center of the antenna array to be finalized by RAN4 #99-e
    For this method the contribution to MU and impact on measurement time are FFS
  OEMs to provide maximum expected offset between geometric centre of the antenna array with respect to the phase centre
  Whether antenna location for the black box approach can be determined using a scan of the field or power distribution close to the device surface is FFS pending an understanding of the impact on MU, measurement time, test range, and system complexity.

## Slide 5: (Obj 1) CFFNF MU
NOTE: outcome of Issues 1-1-3 and 1-1-4
Tentative agreement
  New MU elements and uncertainty mechanisms related to the CFFNF setup include the following:
    Estimation of DUT antenna location, including compensation of the path loss with respect to the active array, and is applicable to CFFNF using the black and black&white box approach
    Compensation of the probe antenna pattern
    EIRP measurement error
    Whether interaction between probe antenna and DUT antenna at the near distances from the DUT can be introduced is FFS
  Preliminary assessment of EIRP measurement error
    A detailed impact of the SNR on EIRP measurement error is needed
    Simulation assumptions on SNR:
      Option 1: Noise is injected at the output of the UE
      Option 2: Influence of noise for testability analysis is a function of the measurement equipment (e.g. power sensor or spectrum analyzer for Tx measurements)

## Slide 6: (Obj 1) CFFDNF setup
NOTE: outcome of Issue 1-2-1
Tentative agreement
  New MU elements and uncertainty mechanisms related to the CFFDNF setup include the following:
    Whether compensation of the path loss (w.r.t. to the active antenna array) is applicable is FFS
    Compensation of the probe antenna pattern
    EIRP measurement error
    TRP measurement error
    Whether interaction between probe antenna and DUT antenna at the near distances from the DUT can be introduced is FFS
    Estimation of DUT antenna location, including compensation of the path loss with respect to the active array

## Slide 7: (Obj 1) CFFDNF MU (EIRP and TRP measurement errors)
NOTE: outcome of Issues 1-2-2 and 1-2-3
Tentative agreement
  The tables below as the baseline and finalize the MU element description and preliminary assessment of the value next meeting
Antenna Configuration | Range Length [m] | ¦Mean EIRP Error¦ w.r.t. FF [dB] | Std. Dev of EIRP at NF BP [dB]
4x1 | 0.2 | 0.04 | 0.02
 | 0.25 | 0.02 | 0.01
 | 0.3 | 0.01 | 0.00
 | 0.35 | 0.01 | 0.00
 | 0.4 | 0.01 | 0.00
 | 0.45 | 0.00 | 0.00
 | 20 | 0.00 | 0.00
8x2 | 0.2 | 0.48 | 0.22
 | 0.25 | 0.23 | 0.08
 | 0.3 | 0.14 | 0.04
 | 0.35 | 0.09 | 0.02
 | 0.4 | 0.07 | 0.01
 | 0.45 | 0.05 | 0.01
 | 20 | 0.00 | 0.00
12x12 | 0.2 | 3.41 | 1.09
 | 0.25 | 1.84 | 0.44
 | 0.3 | 1.16 | 0.22
 | 0.35 | 0.80 | 0.13
 | 0.4 | 0.59 | 0.08
 | 0.45 | 0.45 | 0.05
 | 20 | 0.00 | 0.00
Antenna Configuration | Range Length [cm] | Constant Density Grid Step Size Dq=Df [o] | With Path Loss Correction |  | Without Path Loss Correction | 
 |  |  | ¦Mean TRP Error¦ [dB] | TRP Std. Dev. [dB] | ¦Mean TRP Error¦ [dB] | TRP Std. Dev. [dB]
8x2 | 20 | 5 | 0.01 | 0.04 | 0.39 | 0.24
 |  | 7.5 | 0.02 | 0.13 | 0.39 | 0.25
 |  | 10 | 0.03 | 0.17 | 0.39 | 0.29
 | 32 | 5 | 0.02 | 0.01 | 0.14 | 0.08
 |  | 10 | 0.04 | 0.03 | 0.14 | 0.09
 | 43 | 5 | 0.02 | 0.01 | 0.08 | 0.04
 |  | 10 | 0.04 | 0.03 | 0.08 | 0.04
12x12 | 20 | 5 | 0.02 | 0.07 | 0.29 | 0.17
 |  | 7.5 | 0.01 | 0.24 | 0.29 | 0.21
 |  | 10 | 0.01 | 0.36 | 0.27 | 0.39
 | 32 | 5 | 0.04 | 0.13 | 0.11 | 0.06
 |  | 10 | 0.09 | 0.63 | 0.07 | 0.64
 | 43 | 5 | 0.06 | 0.13 | 0.06 | 0.03
 |  | 10 | 0.12 | 0.65 | 0.01 | 0.66

## Slide 8: (Obj 2) TPMI method
NOTE: outcome of Issue 2-1-1
Tentative agreement
  TPMI method is applicable for clause 6.2 of TS 38.101-2 for Rel-15 and Rel-16 coherent UEs and is applicable for clause 6.2D for Rel-16 nonCoherent UEs with uplink full power transmission.
    2TX TPMI 2-port transmission shall be configured for coherent UEs and nonCoherent UEs supporting full power transmission (mode-1, mode-full power).
    When 2-port transmission is configured for EIRP measurement for test cases in clause 6.2 and 6.2D of TS38.101-2, fixed TPMI index=2 shall be configured.
  TPMI method is applicable for clause 6.2 of TS38.101-2 and other transmitter test cases. and 2TX TPMI shall be configured for coherent UEs and nonCoherent UEs supporting full power transmission (mode-1, mode-full power). For Non-coherent UEs which do not support full power transmission (mode-1, mode-full power), 2-port transmission shall be not configured with nrofSRS-ports=1.
  When 2-port transmission is configured for EIRP measurement for test cases in clause 6.2 of TS38.101-2, fixed TPMI index=2 shall be configured.

## Slide 9: (Obj 2) EVM measurement setup
NOTE: outcome of Issues 2-2-1, 2-2-2
Tentative agreement
  Outcome of obj 2 only applies for FR2 test application
  FFS 2L and 1L setups should be agreed as a package
    There is no inter-layer interference for 1L , no need to enhance 1L EVM measurement setup
  Two alternative methods, proposed in [9] and [15], can be included in the TR with the understanding that tThe study item outcome will capture a single setup as clear guidance related to this enhancement
  Companies are encouraged to provide further analysis of the following:
    How to handle the probability of having a non-invertible matrix in the demodulation paths of both proposed schemes
    Potential differences in calculated EVM of both proposed schemes
    Whether TE is mandated to implemented with ‘ZF’ for FR2 EVM measurement
  Whether different polarization angles shall be used in the EVM and spectrum flatness tests is FFS
    A potential rationale is to avoid test results being impacted by polarization basis mismatch before new MIMO demodulation scheme is applied to address the polarization basis mismatch issue.
  TP drafting: it is proposed to postpone the TP related to this setup until the next meeting, with the understanding that companies will seek ways to converge on the above aspects in the interim

## Slide 10: (Obj 4) ETC
NOTE: outcome of Issue 4-1-2
Tentative agreement
  Given that ETC MU assessment (23.45GHz - 40.8GHz) of EIRP and EIS has been finalized in RAN5, the additional 0.28dB MU induced by ETC system can be considered as an example conclusion added to TR38.884.
  Given the MU assessment in RAN5 is only up to 40.8GHz, it is still valuable to perform the preliminary MU assessment of ETC to 49GHz in this SI, to cover the new n262 band, and conclude the ETC feasibility of this band.
  UE vendors to provide feedback whether +/-4 degrees of temperature tolerance (compared to +/-2 for FR1) introduces additional MU, TT or core requirement relaxation
  FFS whether max difference of path loss between the NTC and ETC environment should be taken into account in the ETC MU

## Slide 11: (Obj 5) Enhancements to reduce test time
NOTE: outcome of Issues 5-1-1, 5-1-2, 5-1-3, and 5-1-4
Tentative agreement
  New measurement grid (1-MG)
    Simulation assumptions to derive MU contribution of the 4x2 measurement grid need to be further aligned based on the following assumption: reuse the antenna array location defined in TR38.810 for Rel-15 spherical coverage measurement grid to keep the simulation parameters consistency (front and back, in the centre)
    The spherical coverage and TRP measurement grid based on 4x2 antenna array should also be defined in this SI. The analysis of reduced test time could be captured as the outcome in TR38.884.
  RSRP(B) based RX beam peak search (2-RSRP)
    RAN4 should confirm that RSRP is available to find the beam peak direction
    Further discuss RSRP or RSRP&EIS based beam peak searching procedure
      If RSRP is selected, further discuss whether an additional MU element is needed.
    Whether the test procedure of Rx beam peak search based on RSRPB for demodulation and CSI testing can be applicable is FFS
  3-Single Pollink
    For EIRP test of UL MIMO and Tx diversity, by default whether single Pollink can be is randomly selected (from either theta Pollink or phi Pollink) or test under 2 link directions , depends on UE declaration
  Agree that FFS whether the Fast Spherical Coverage Method can be introduced
    Keep the maximum elevation between [112.5º] of 90o for DUT Orientation 1and further discuss next meeting

## Slide 12: (Obj 6) Band-dependent parameters for the demodulation setup
NOTE: outcome of Issue 6-1-1
Tentative agreement
  Take the proposed calculations as a preliminary assessment and share with RAN5 for their comment
  Ask RAN5 to share any updates related to FR2b, so that these can be applied to the SNR calculations for n262

## Slide 13: TR 38.884 MU annex drafting
A dedicated sub-agenda item for MU analysis and text proposals discussion is helpful to finalize all the MU related work next meeting.
The MU assessment is related to all the objectives

## Slide 14: References
Ref | T-doc | Company | Title
[1] | R4-2104523 | vivo | TP to TR38.884 v0.2.0 on MU Annex
[2] | R4-2104897 | Apple, vivo | Rapporteur input to TR38.884
[3] | R4-2104898 | Apple, vivo | TR38.884 work split
[4] | R4-2104522 | vivo | Discussions on test procedure of FR2 enhanced test methods
[5] | R4-2104684 | Huawei, HiSilicon | On black box test
[6] | R4-2106695 | MVG Industries, Sony | DNF Method
[7] | R4-2107130 | Keysight Technologies | On CFFNF and CFFDNF test methodologies for high DL power and low UL power test cases
[8] | R4-2107187 | Rohde & Schwarz | Analysis of NF based solutions
[9] | R4-2104489 | Qualcomm Incorporated | Transmit signal quality measurements by TE with dual pol Rx
[10] | R4-2104558 | MediaTek Inc. | TPMI, 2-port CSI-RS, and EVM issues about polarization basis mismatch
[11] | R4-2104569 | Anritsu Corporation | Considerations on test with TPMI method
[12] | R4-2104701 | Sony, Ericsson | Views on solutions to minimize the impact of polarization basis mismatch
[13] | R4-2105043 | Samsung | Discussion on TPMI configuration in EIRP measurement
[14] | R4-2106570 | OPPO | Solution to minimize the impact of polarization basis mismatch
[15] | R4-2107111 | Rohde & Schwarz | Text proposal to TR38.884: FR2 UL EVM measurements
[16] | R4-2104958 | Anritsu Corporation | TP to TR 38.884 on Inter-band DL CA in FR2
[17] | R4-2104521 | vivo | TP to TR38.884 v0.2.0 on ETC system
[18] | R4-2104570 | Anritsu Corporation | Considerations on ETC MUs and a testability
[19] | R4-2107128 | Keysight Technologies | On extreme temperature condition testing
[20] | R4-2104518 | vivo | (draft) LS on antenna assumption and measurement grids for FR2 PC3 UE
[21] | R4-2104519 | vivo | Discussion and TP to TR38.884 on FR2 test time reduction
[22] | R4-2105001 | LG Electronics | Discussion on test time reduction for FR2 OTA test time
[23] | R4-2105044 | Samsung | Discussion on prioritized methods for test time reduction
[24] | R4-2107110 | Rohde & Schwarz | Text proposal to TR38.884: Fast Spherical Coverage Method
[25] | R4-2107129 | Keysight Technologies UK Ltd | Draft LS to RAN5 on Test Time Reduction
[26] | R4-2107296 | Huawei, HiSilicon | Discussion on enhance test method to reduce FR2 OTA test time
[27] | R4-2104896 | Apple | On permitted test methods for demodulation in band n262
[28] | R4-2105998 | Moderator (Apple) | Email discussion summary for [98-bis-e][327] FR2_enhTestMethods