## Slide 1: WF on UE RF UL RMC
Qualcomm Inc., …
R4-1809333
3GPP TSG-RAN WG4 Meeting #AH1807
Montreal, Canada, 2-6 July 2018
Agenda Item: 5.5

## Slide 2: Background
R5-183950 recommends possible modulations, waveforms and RB allocation for REFSENS, MOP and frequency error tests for defining UL RMC at RAN4
This document summarizes the parameters for defining UL RMC for different UE RF tests.

## Slide 3: MCS and Target Code Rate
Use following MCS and code rate for different modulations:
  Pi/2 BPSK: MCS 0, Target Code Rate = 1/4
  QPSK: MCS 2, Target Code Rate = 1/6

## Slide 4: Parameters for REFSENS FR1
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | DFT-S-OFDM | 20 | 2 | QPSK | 1/6
5 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
10 | 15 | DFT-S-OFDM | 20 | 2 | QPSK | 1/6
10 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 20 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 75 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 20 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 100 | 2 | QPSK | 1/6
25 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
30 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
40 | 15 | DFT-S-OFDM | 216 | 2 | QPSK | 1/6
50 | 15 | DFT-S-OFDM | 270 | 2 | QPSK | 1/6
60 | 30 | DFT-S-OFDM | 162 | 2 | QPSK | 1/6
100 | 30 | DFT-S-OFDM | 270 | 2 | QPSK | 1/6

## Slide 5: Parameters for REFSENS FR2
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50 | 120 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
200 | 120 | DFT-S-OFDM | 132 | 2 | QPSK | 1/6
400 | 120 | DFT-S-OFDM | 264 | 2 | QPSK | 1/6

## Slide 6: Parameters for FR1 MOP: Pi/2 BPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5, 10, 15, 20, 25, 30, 40, 50 | 15 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
5 | 15 | DFT-S-OFDM | 12 | 0 | PI/2 BPSK | 1/4
10 | 15 | DFT-S-OFDM | 25 | 0 | PI/2 BPSK | 1/4
15 | 15 | DFT-S-OFDM | 36 | 0 | PI/2 BPSK | 1/4
20 | 15 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
25 | 15 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
30 | 15 | DFT-S-OFDM | 80 | 0 | PI/2 BPSK | 1/4
40 | 15 | DFT-S-OFDM | 108 | 0 | PI/2 BPSK | 1/4
50 | 15 | DFT-S-OFDM | 135 | 0 | PI/2 BPSK | 1/4
5, 10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 | 30 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
5 | 30 | DFT-S-OFDM | 5 | 0 | PI/2 BPSK | 1/4
10 | 30 | DFT-S-OFDM | 12 | 0 | PI/2 BPSK | 1/4
15 | 30 | DFT-S-OFDM | 18 | 0 | PI/2 BPSK | 1/4
20 | 30 | DFT-S-OFDM | 25 | 0 | PI/2 BPSK | 1/4
25 | 30 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
30 | 30 | DFT-S-OFDM | 36 | 0 | PI/2 BPSK | 1/4
40 | 30 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
50 | 30 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
60 | 30 | DFT-S-OFDM | 81 | 0 | PI/2 BPSK | 1/4
80 | 30 | DFT-S-OFDM | 108 | 0 | PI/2 BPSK | 1/4
90 | 30 | DFT-S-OFDM | 120 | 0 | PI/2 BPSK | 1/4
100 | 30 | DFT-S-OFDM | 135 | 0 | PI/2 BPSK | 1/4
10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 | 60 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
10 | 60 | DFT-S-OFDM | 5 | 0 | PI/2 BPSK | 1/4
15 | 60 | DFT-S-OFDM | 9 | 0 | PI/2 BPSK | 1/4
20 | 60 | DFT-S-OFDM | 12 | 0 | PI/2 BPSK | 1/4
25 | 60 | DFT-S-OFDM | 15 | 0 | PI/2 BPSK | 1/4
30 | 60 | DFT-S-OFDM | 18 | 0 | PI/2 BPSK | 1/4
40 | 60 | DFT-S-OFDM | 25 | 0 | PI/2 BPSK | 1/4
50 | 60 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
60 | 60 | DFT-S-OFDM | 36 | 0 | PI/2 BPSK | 1/4
80 | 60 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
90 | 60 | DFT-S-OFDM | 60 | 0 | PI/2 BPSK | 1/4
100 | 60 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4

## Slide 7: Parameters for FR1 MOP: QPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modul2ation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5, 10, 15, 20, 25, 30, 40, 50 | 15 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
5 | 15 | DFT-S-OFDM | 12 | 2 | QPSK | 1/6
10 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 36 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
25 | 15 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
30 | 15 | DFT-S-OFDM | 80 | 2 | QPSK | 1/6
40 | 15 | DFT-S-OFDM | 108 | 2 | QPSK | 1/6
50 | 15 | DFT-S-OFDM | 135 | 2 | QPSK | 1/6
5, 10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 | 30 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
5 | 30 | DFT-S-OFDM | 5 | 2 | QPSK | 1/6
10 | 30 | DFT-S-OFDM | 12 | 2 | QPSK | 1/6
15 | 30 | DFT-S-OFDM | 18 | 2 | QPSK | 1/6
20 | 30 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
25 | 30 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
30 | 30 | DFT-S-OFDM | 36 | 2 | QPSK | 1/6
40 | 30 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
50 | 30 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
60 | 30 | DFT-S-OFDM | 81 | 2 | QPSK | 1/6
80 | 30 | DFT-S-OFDM | 108 | 2 | QPSK | 1/6
90 | 30 | DFT-S-OFDM | 120 | 2 | QPSK | 1/6
100 | 30 | DFT-S-OFDM | 135 | 2 | QPSK | 1/6
10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 | 60 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
10 | 60 | DFT-S-OFDM | 5 | 2 | QPSK | 1/6
15 | 60 | DFT-S-OFDM | 9 | 2 | QPSK | 1/6
20 | 60 | DFT-S-OFDM | 12 | 2 | QPSK | 1/6
25 | 60 | DFT-S-OFDM | 15 | 2 | QPSK | 1/6
30 | 60 | DFT-S-OFDM | 18 | 2 | QPSK | 1/6
40 | 60 | DFT-S-OFDM | 25 |  | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
60 | 60 | DFT-S-OFDM | 36 | 2 | QPSK | 1/6
80 | 60 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
90 | 60 | DFT-S-OFDM | 60 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6

## Slide 8: Parameters for FR2 MOP: Pi/2 BPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
50 | 60 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
50 | 60 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
100 | 60 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
100 | 60 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
200 | 60 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
200 | 60 | DFT-S-OFDM | 256 | 0 | PI/2 BPSK | 1/4
50,100,200,400 | 120 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
50 | 120 | DFT-S-OFDM | 16 | 0 | PI/2 BPSK | 1/4
50 | 120 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
100 | 120 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
100 | 120 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
200 | 120 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
200 | 120 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
400 | 120 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
400 | 120 | DFT-S-OFDM | 256 | 0 | PI/2 BPSK | 1/4

## Slide 9: Parameters for FR2 MOP: DFT-s-OFDM QPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
200 | 60 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
200 | 60 | DFT-S-OFDM | 256 | 2 | QPSK | 1/6
50,100,200,400 | 120 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
50 | 120 | DFT-S-OFDM | 16 | 2 | QPSK | 1/6
50 | 120 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
200 | 120 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
200 | 120 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
400 | 120 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
400 | 120 | DFT-S-OFDM | 256 | 2 | QPSK | 1/6

## Slide 10: Parameters for FR2 MOP: CP-OFDM QPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | CP-OFDM | 1 | 2 | QPSK | 1/6
50 | 60 | CP-OFDM | 33 | 2 | QPSK | 1/6
50 | 60 | CP-OFDM | 66 | 2 | QPSK | 1/6
100 | 60 | CP-OFDM | 66 | 2 | QPSK | 1/6
100 | 60 | CP-OFDM | 132 | 2 | QPSK | 1/6
200 | 60 | CP-OFDM | 264 | 2 | QPSK | 1/6
200 | 60 | CP-OFDM | 264 | 2 | QPSK | 1/6
50,100,200,400 | 120 | CP-OFDM | 1 | 2 | QPSK | 1/6
50 | 120 | CP-OFDM | 16 | 2 | QPSK | 1/6
50 | 120 | CP-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | CP-OFDM | 33 | 2 | QPSK | 1/6
100 | 120 | CP-OFDM | 66 | 2 | QPSK | 1/6
200 | 120 | CP-OFDM | 66 | 2 | QPSK | 1/6
200 | 120 | CP-OFDM | 132 | 2 | QPSK | 1/6
400 | 120 | CP-OFDM | 132 | 2 | QPSK | 1/6
400 | 120 | CP-OFDM | 264 | 2 | QPSK | 1/6