## Slide 1: Summary of operators input on the TDD patterns for NR UE performance tests in Rel-15
Ericsson, Verizon, AT&T, CMCC, NTT Docomo, KDDI
3GPP TSG-RAN WG4 Meeting #AH201807 Montreal, Canada, 27 Nov - 1 Dec 2017
Agenda Item: 5.4.1.3
R4-1809394

## Slide 2: Agreed work plan
The work plan for UE performance WI was agreed in R4-1808029.
  Phase 0: Overall test scope, generic common test set-up and channel modelling, specification skeleton
  Phase 1: Completion 1st bullet of test cases (RAN4 July Ad-hoc, RAN4#88)
    Demod:
      PDSCH: Normal test cases with single carrier
      PDCCH
    CSI: CQI (static), PMI, RI test cases
  Phase 2: Completion 2nd bullet of test cases (RAN4#88bis, RAN4#89)
    Demod:
      PDSCH: SDR test, CA/DC/SUL test cases if any
      PBCH if any
    CSI: CQI (fading), L1-RSRP, CRI test cases if any

## Slide 3: Background
Different operators/countries/regions have different planning and considerations on TDD patterns for different frequency bands.
The TDD config for the test set-up is still open for UE performance tests except the FR1 15kHz was agreed as following with the purpose to align the LTE config#2
  FR1:
    15 kHz: DDDSU(aligned with LTE config#2 with 5ms periodicity)
      S = 12D+1Gp+1U
The purpose of UE performance tests should reflect the practical networks based on actual deployment from operators.
In this document summarizes the preference from different operators for different SCS and FR with represents present in this AH meeting.

## Slide 4: FR1
30kHz
Operators | First prior | Second prior
DCM | 7D1S2U, S = 6D:4G:4U | SU, S=12D:2G
CMCC | DDDSUDDSUU, [S1=10D:4G], [S2= 10D:4G] | DDSU, [S = 10D:4G]
Orange | DDDSU, S=10D:2G:2U | 7D1S2U, S = TBD

## Slide 5: FR2
60kHz
120kHz
Operators | First prior | Second prior
DCM | DDDSU, S=10D:2G:2U | DSUU, S=12D:2G
AT&T, Verizon | DDSU, S=11D+3G | 
Operators | First prior
AT&T, Verizon | DDSU, S=11D+3G

## Slide 6: WF for TDD patterns for NR UE performance tests in Rel-15
The UE performance tests should be defined based on the operators actual deployment plan to reflect the practical network condition
The total number of tests for PDSCH alignment should be considered as manageable for first round alignment in Aug meeting.
The TDD patterns from first prior have the same level of priority for test setup
  Similar test scope should be covered for each TDD pattern as first prior e.g. MIMO config, channel model with doppler, MCS, etc.
  First prior should be considered for Phase 1 and collected with alignment results in Aug meeting
The second prior test will be defined with UE performance tests after first prior test set is completed in Rel-15.
The TDD patterns from first prior are considered frozen in this AH meeting, in order to have alignment results in Aug meeting.
The TDD patterns from second prior will be finalized and frozen in Aug meeting, and some limited test cases for second prior should be defined within Rel-15.
For test cases introduced in future releases after Rel-15 the TDD patterns will be FFS.

## Slide 7: Proposal on how to limit test number
Step 1: Based on the WF from R4-1809392 with the simulation assumptions defined for PDSCH demodulation tests, a total number of test cases is calculated/proposed per FR1 30kHz, and FR2 120kHz. (FR2 60kHz is only one TDD pattern proposed)
Step 2: This total number of test cases per FR1 30kHz and FR2 120kHz will be divided equally by the number of first prior TDD patterns proposed by operators as 3 for FR1 30kHz and 2 for FR2 120kHz. Each different TDD pattern has same number of test cases based on the above and the total number of tests remains the same as proposed from Step 1.
Detailed test list will be defined in separated document for simulation assumptions.