## Slide 1: IETF Status Report to TSG CT/SA#100
Lionel Morand, Orange

## Slide 2: Contents
3GPP-IETF Coordination
Liaison statements exchanged between IETF and 3GPP
Tracking IANA requests
Published RFCs (1)
RFC Editors Queue (2)
IESG review (3)
Active WG document (1)
Individual drafts (1)

## Slide 3: 3GPP-IETF Coordination

## Slide 4: IETF-3GPP Coordination meeting
Last: @IETF#116 (Yokohama)
  2023, March 28, 2.30am UTC (remote access provided)
  With CT chair, IETF liaison, IESG members, IAB members, WG chairs and delegates. About 40 attendees
  Some issues with the LS sent by IETF.
    Reminder to IETF: LS from IETF have to be sent in a formatted document attached to the email sent to the 3GPP Liaison coordinator
  Remaining dependencies (about 7) under control
Next: @IETF#117 (San Francisco)
  Will be held on 2023, July 24 (TBC)
  Remote access will be provided

## Slide 5: New (formal) IETF - 3GPP IAB group
Created in April 2023, similar to the IETF-IEEE IAB group
Group description
  The purpose of this group is to support coordination activities between IETF and 3GPP as documented in RFC 3113.
  led jointly by the 3GPP and IETF liaison managers
  No fixed membership but participation from relevant IETF Area Directors, IETF WG Chairs, 3GPP WG Chairs, and document authors/editors is encouraged.
  See: https://datatracker.ietf.org/group/ietf3gpp/about/
Action Points:
  Update the dependency list tool or create a new one (with IETF support)
  Update RFC 3113: "3GPP-IETF Standardization Collaboration" (2001)

## Slide 6: For information
A new IETF non-working group email list has been created.
  List address: sat-int@ietf.org
  Archive: https://mailarchive.ietf.org/arch/browse/sat-int/
Purpose:
  To discuss the networking issues and solutions involved in NTN integration with 5G and Internet
  The mail list will only focus on the technical topics related to IETF technologies, more specifically in L3 layer such as addressing, routing and switching, traffic engineering, integration with Internet, etc.
  IMPORTANT: It is not intended to be a platform for 3GPP discussions except the requirements to IETF, thus all 3GPP solutions in RAN, SA, etc. will be excluded in the discussion.

## Slide 7: IETF-3GPP Liaison Statements

## Slide 8: 3GPP->IETF Reply LS on SCTP-AUTH and DTLS
In response to LS on SCTP-AUTH and DTLS from IETF TSWG
  inform RAN3/SA3 of discovered security issues delaying RFC 6083-bis work
Feedback from SA3:
  SA3 agrees that the discovered security issues are serious and need to be solved
  SA3’s understanding is that the solution should be based on DTLS
  SA3 kindly asks TSVWG to work on and publish a solution as soon as possible

## Slide 9: 3GPP->IETF: isInvariant and SystemCreated in YANG
LS on need for modeling isInvariant and SystemCreated in YANG to Netmod (03/23)
3GPP Requirements
  A solution to represent the isInvariant and SystemCreated properties in IETF defined YANG statements is needed to support 3GPP stage3 YANG data model.
  3GPP SA5 sees draft-ma-netmod-immutable-flag as a potential solution
Discussed in the IETF-3GPP coordination meeting
WG adoption currently discussed on netmod mailing list
  Interested companies should express their support for this draft

## Slide 10: IETF->3GPP
None

## Slide 11: Tracking requests to IANA

## Slide 12: IANA assignment request handling
Review of Rel-17 specifications has revealed that:
  A lot of IANA assignment requests have still to be done
  There is no easy way to track the need for IANA assignment requests from 3GPP
Actions (3GPP wide):
  LS sent to all the 3GPP WGs
    Specification rapporteurs needs to review Rel-17/Rel-18 specs and collect the request for IANA assignment
    Any IANA assignment request must be indicated to the CT Chair
  ETSI has created an IANA Pending Request Registry accessible today on CT1 WG webpage (trial phase) but should be accessible via the delegate corner.

## Slide 13: 3GPP allocated port numbers
Alternative solutions to avoid the need for port assignment for (private) 3GPP interfaces
  TR 29.941: Guidelines on Port Allocation for New 3GPP Interfaces
  TS 29.641: 3GPP Registry for Service Names and Port Numbers
Assigned port number in TS 29.641:
  Port 65400: Assigned to SLMP (SEAL Off- Location Management protocol)
  Port 65401: Assigned to MSGin5G service

## Slide 14: IETF Dependencies

## Slide 15: New Published RFCs

## Slide 16: IETF reference updates
None

## Slide 17: Drafts in RFC Editor queue

## Slide 18: Drafts in RFC Editor queue
draft-ietf-stir-identity-header-errors-handling-08
  Title: Identity Header Errors Handling for STIR
  Next step:
    Published as Proposed Standard RFC
    CRs to 24.229 and 29.165
draft-ietf-ace-extend-dtls-authorize-07
  Title: Extension of the DTLS Profile for ACE to TLS
  Next step:
    Published as Proposed Standard RFC
    CRs to 33.434

## Slide 19: Drafts under IESG review

## Slide 20: Drafts under IESG review
draft-ietf-stir-passport-rcd-26
  Title: PASSporT Extension for Rich Call Data
  Published: 06/2023
  Next step: Published as Proposed Standard RFC, CRs to 33.127 and 33.128
draft-ietf-stir-messaging-07
  Title: Messaging Use Cases and Extensions for STIR
  Published: 03/2023
  Next step: Published as Proposed Standard RFC, CRs to 33.127
  !!! WARNING !!! Wrong draft reference in 33.127
    IETF draft-ietf-stir-passport-messaging-00, "Messaging Use Cases and Extensions for STIR".

## Slide 21: Drafts under IESG review
draft-ietf-detnet-yang-17
  Title: Deterministic Networking (DetNet) YANG Model
  Published: 04/2023
  Next step:
    Published as Proposed Standard RFC
    CRs to 23.501, 23.503 and 29.565

## Slide 22: Active WG document

## Slide 23: Active WG document
draft-jesske-update-p-visited-network-04
  Title: Update to P-Visited-Network-ID in SIP Requests and Responses
  Last update: dec 2022.
  Status:
    Pushed forward by Brian Rosen (sipcore chair) after the last IETF-3GPP coordination
    In WG Last Call
  Next step: draft update, IESG review, RFC publication, CT1 CR to 24.229

## Slide 24: Individual submission

## Slide 25: Individual submission
draft-schwarz-mmusic-sdp-for-gw
  Next step: Still to be reactivated, published RFC, CT4 CR to 23.334 and 29.334
  Last version May 2016
  Action Point: contact an ITU expert that could help us.

## Slide 26: Potential future IETF dependencies

## Slide 27: Rel-18 Studies
TR 23.700-53: Study on ATSSS support in the 5G system architecture; Phase 3
  draft-ietf-quic-multipath-04
  draft-ietf-tsvwg-multipath-dccp-07
  draft-ietf-masque-connect-ip-08
TR 23.700-60: Study on XR (Extended Reality) and media services
  draft-ietf-avtext-framemarking-13
  draft-ietf-quic-http-34
  draft-ietf-tsvwg-udp-options-18
  draft-ietf-avtcore-rtp-vvc-14
  draft-ietf-masque-connect-udp
  draft-ietf-quic-http
  draft-ietf-masque-h3-datagram
  draft-ietf-httpbis-h3-websockets

## Slide 28: Rel-18 Studies
TR 33.876: Study on automated certificate management in Service-Based Architecture (SBA)
  Certificate Management Protocol (CMP) Updates, draft-ietf-lamps-cmp-updates
  Certificate Management Protocol (CMP) Algorithms, draft-ietf-lamps-cmp-algorithms
  X.509 Certificate Extended Key Usage (EKU) for (JOSE) and CBOR Object Signing and Encryption (COSE), draft-ietf-lamps-nf-eku
  TNAuthList profile of ACME Authority Token, draft-ietf-acme-authority-token-tnauthlist

## Slide 29: Thank You!
Peter Schmitt
TSG CT Chair
IETF Liaison
Peter.Schmitt@huawei.com