## Slide 1: Summary for RAN Rel-19 Package: RAN1/2/3-led
Source: RAN Chair
3GPP RAN#102
December 11th – 15th, 2023
RP-232745
AI: 9.1

## Slide 2: Outline
References
Overall RAN Rel-19 package: RAN1/2/3-led
  General thoughts
  RAN1-led
  RAN2-led
  RAN3-led
Appendix:
  Baseline TU arrangement
  Baseline objectives

## Slide 3: References

## Slide 4: References
RAN#98-e: Steps towards RAN Rel-19 package approval, as endorsed in RP-222730
RAN#99: Rel-19 timeline, as endorsed in RP-230050
RWS: Rel-19 workshop summary, as endorsed in RWS-230488
RAN#101: RAN Chair’s Guidance for RAN Release 19 in RP-231540
RAN#101: summary of various potential Release 19 topics
  See the table on the right
 | Topic | Moderator's summary
RAN1 | AI (Artificial Intelligence)/ML (Machine Learning) for Air interface | RP-232611
 | MIMO Evolution | RP-232612
 | Duplex Evolution | RP-232613
 | Ambient IoT | RP-232614
 | Network Energy Savings | RP-232615
 | LP-WUS/WUR | RP-232616
 | ISAC & Exploring Study in New spectrum (7-24GHz) | RP-232617
RAN2 | Mobility Enhancements | RP-232618
 | Enhancements for XR | RP-232619
 | NTN for NR | RP-232610
 | NTN for IoT | RP-232621
 | AI/ML for Air Interface SI (Mobility) | RP-232622
RAN3 | AI/ML for NG-RAN | RP-232623
 | SON/MDT Enhancements | RP-232624
 | Additional Topological Enhancements | RP-232625
Additional RAN1 | Multi-carrier Enhancements, Coverage Enhancements, Positioning Enhancements, SL Evolution, Others | RP-232626
Additional RAN2 | NCR, SL Relay Enhancements, UAV/UAM, MU-SIM, Broadcast/multicast, UE aggregation, collaboration, and backup, Lean protocol stack/High speed packetization/Layer 2 UP enhancements, Others | RP-232627
Additional RAN3 | QoE, Others | RP-232628

## Slide 5: Overall RAN Rel-19 Package: RAN1/2/3-led

## Slide 6: General Guidance 1/2
As endorsed in RWS-230488 and RP-231540
  It is critical to ensure all WGs’s load in Rel-19 is reasonable, and lower than that of Rel-18!
  Details of the first-order TU estimate can be found in RP-231540
  Note: as usual, the TUs for Rel-18 maintenance will need to start with a large # of TUs, then slowly back to “normal”
To ensure reasonable Rel-19 workload, it is critical to make sure that:
  The number of projects is reasonable, and
  Probably even more importantly, the amount and the clarity of scope for each project
    Shall avoid “generic enhancements”-like scope!
  Based on the RWS and RAN#101 outcome, a set of RAN1/2/3-led projects for Rel-19 are proposed in the subsequent slides
    The corresponding objectives are also listed in the Appendix as a baseline for further discussion in RAN#102 for final SID/WID approval, including identifying the impacted RAN WGs and the interaction with other TSG WGs

## Slide 7: General Guidance 2/2
Based on commercial needs, and Rel-19 progress, additional new but smaller RAN1/2/3-led projects or scope expansion of the RAN#102 approved RAN1/2/3-led projects may be further discussed and approved at a later stage of Rel-19
  The earliest time of such opportunity is September 2024
  Similar to Rel-18, this will be carefully managed
Notes:
  The RAN Rel-19 project names listed in the sequel are abbreviated/simplified, and are subject to further discussion/refinement
  The TUs for the follow-up WIs (after the expected completion of the corresponding SIs) are based on current expectation and may need to be adjusted based on the corresponding SI outcome
In the TU spreadsheet, a first-order estimate of RAN4 TUs is also provided for each RAN1/2/3-led project

## Slide 8: RAN R19 Package: RAN1-led Projects
Project | TU estimate
AI/ML - Air Interface | ~4 TUs
NR-MIMO Evolution | ~2.5 TUs in 1st half, ~2TUs in the 2nd half
Evolution of duplex operation | ~2 TUs
Ambient IoT | ~3.5 TUs (TUs budgeted for the entire release, target 12-month for SI completion, check in Dec’24 for conversion to WI or if necessary, continuation of SI)
Network energy savings | ~2 TUs
Low power WUS/WUR | ~1.5 TUs
ISAC | SI only, starting from 2Q’24, ~1 TU for 15 months. Focusing on channel model; check in Sept’24 for possibly additional study beyond channel model
Exploring study in new spectrum (7-24GHz) | SI only, starting from 2Q’24, ~1 TU for 15 months for channel model
Legend - XX: WI; XX: SI only; XX: SI followed by WI or if necessary, continuation

## Slide 9: RAN R19 Package: RAN2-led Projects
Project | TU estimate
Mobility Enhancements | ~2 TUs
Enhancements for XR | ~2 TUs
NTN (Non-Terrestrial Networks) evolution - NR | ~2 TUs
NTN (Non-Terrestrial Networks) evolution - IoT | ~1 TU
AI/ML for Air Interface (Mobility) | ~2 TUs
Legend - XX: WI; XX: SI only; XX: SI followed by WI

## Slide 10: RAN R19 Package: RAN3-led Projects
Project | TU estimate
AI/ML for NG-RAN | 6 months SI, followed by 12-month WI, ~2 TUs
SON/MDT Enhancements | ~1.5 TUs
Additional topological improvements | 6 months SI, followed by 12-month WI, ~2TUs for SI, and ~1.5TUs for WI
Legend - XX: WI; XX: SI only; XX: SI followed by WI

## Slide 11: Proposal
RAN R19 package for RAN1/2/3 as detailed in slides 6 to 10 is endorsed
  The detailed TU spreadsheet for RAN1/2/3/4 as detailed in slides 13 to 16 is endorsed as the baseline for further discussion during RAN#102 for final RAN Rel-19 SID/WID approvals
    RAN4 TU spreadsheet is expected to be further refined/updated in RAN#103
  The proposed detailed scope in slides 18 to 33 is endorsed as the baseline for further discussion in RAN#102 for final RAN Rel-19 SID/WID approvals

## Slide 12: Appendix: Baseline TUs

## Slide 13: TU Spreadsheet for RAN1

## Slide 14: TU Spreadsheet for RAN2

## Slide 15: TU Spreadsheet for RAN3

## Slide 16: TU Spreadsheet for RAN4

## Slide 17: Appendix: Baseline Objectives

## Slide 18: AI/ML – Air Interface WI
References: RWS-230488, RP-231540, RP-232611
Potential objectives:
  Consider support single sided models for,
    Positioning, further discuss whether to support all 5 sub use cases.
    Beam management for DL Tx prediction in both UE-sided and NW sided model,
    Consider support of single sided model for CSI prediction, if it is recommended to proceed with normative work taken all WG’s outcome in Q4-23 into account
  Consider support two-sided model for CSI compression, if it is recommended to proceed with normative work taken all WG’s outcome in Q4-23 into account
  Consider support the necessary/recommended LCM components for selected sub use cases
  RAN4 requirements and test cases for AI/ML enabled features
Taking into account the progress in RAN WGs in 4Q’2023

## Slide 19: NR-MIMO Evolution WI
References: RWS-230488, RP-231540, RP-232612
Potential objectives:
[To discuss in RAN#102 according to the TU budget, particularly the necessary down-scoping of the yellow part]
  Topic 1: Beam management enhancements to reduce overhead/latency through UE-initiated/event-driven beam management
  Objective 1. Signalling/mechanism to facilitate UE-initiated beam management procedure including UE-initiated beam reporting/[switch]
  Topic 2: Enhancements to CSI framework to support > 32 (64/128) CSI-RS ports
  Objective 1: Type I codebook enhancements to support > 32 CSI-RS ports
  Objective 2: Type II codebook enhancements to support > 32 CSI-RS ports
  Objective 3: Hybrid beamforming enhancements (CRI based reporting enhancements)
  Note 1: Extension of legacy codebooks and legacy CSI-RS resources
  Note 2: Objective 3 may require further study or clarification.
  Topic 3: CJT/DL multi-TRP enhancements
  Objective 1: UE-assisted calibration reporting of delay and frequency/phase offsets for CJT with non-ideal synchronization and backhaul
  Note: Assume legacy CSI-RS design and standalone aperiodic reporting on PUSCH.
  Topic 4: UL enhancements
  Objective 1: STxMP enhancements (e.g. Simultaneous TX of PUCCH and PUSCH, Asymmetric panel implementations, mDCI PUCCH + PUCCH, STxMP with up to rank 8, Coherent SFN STxMP)
  Objective 2: Enhancements for UL 3Tx including 3Tx for UL codebook and non-codebook based transmission
  Topic 5: Enhancement for asymmetric downlink S-TRP/UL M-TRP scenario assuming intra-band intra-cell non-co-located M-TRP scenarios without changing existing cell definition or defining a new cell
  Objective 1: Extension of Rel-18 2TA mDCI to sDCI assuming legacy PRACH resources
  Objective 2: Separate UL power control for SRS only to downlink S-TRP from SRS to UL M-TRP and introduce path loss measurement to uplink M-TRP
  Topic 6: 6Rx/8Rx UE enhancements with lower complexity utilizing two segments of 3/4 Rx antenna units up to 8-layer DL Tx based on legacy codebook and legacy codeword to layer mapping
  Objective 1: SRS antenna port grouping, CSI and codeword association to the segments of receive antenna.

## Slide 20: Evolution of duplex operation WI
References: RWS-230488, RP-231540, RP-232613
Potential objectives:
  For subband non-overlapping full duplex (SBFD) operation at gNB side within a TDD carrier
    [Semi-static/dynamic] indication of time location of SBFD subbands to UEs [in RRC_CONNECTED mode]
    Semi-static indication of frequency domain location of SBFD subbands to UEs [in RRC_CONNECTED mode]
    UE transmission and reception behavior and procedures in SBFD symbols and/or non-SBFD symbols
    Note: followings are assumed based on TR 38.858
      SBFD operation Option 4
      Coexistence between legacy UEs and SBFD aware UEs in the cell operating SBFD at gNB side
      SBFD scheme within a single configured DL and UL BWP pair with aligned center frequencies
      Up to one UL subband for SBFD operation in an SBFD symbol (excluding legacy UL symbol/slot) within a TDD carrier
    At least adjacent channel coexistence between two operators should be considered as a minimum.
  Specify enhancements for CLI handling:
    Support both the gNB-to-gNB co-channel CLI handling scheme(s) and UE-to-UE co-channel CLI handling scheme(s) (the detailed schemes are to be down-selected from those in TR38.858)
    The SBFD operation drives the CLI enhancements, which are expected to be applicable to the dynamic/flexible TDD operation but without dedicated optimization
  RF requirements for SBFD operation at gNB

## Slide 21: Ambient IoT SI
References: RWS-230488, RP-231540, RP-232614
Potential objectives:
  Consider all Devices A, B and C in the SI?
  Down-selection among:
    Deployment scenario 1 with Topology 1
    Deployment scenario 2 with Topology 1
    Deployment scenario 2 with Topology 2
    Deployment scenario 4 with Topology 1
    Deployment scenario 4 with Topology 3
  FR1 licensed spectrum, focusing on FDD only
    Downselection Spectrum in-band to NR, in guard-band to LTE/NR, and in standalone band(s)
      Evaluations and remaining feasibility assessments
          Device architecture and characteristics
        Evaluation methodology and assumptions
        Design target evaluations
        Coexistence evaluations
      Physical layer study on:
        Waveform and multiple access
        Frame structure and numerology
        Modulation and channel coding
        Physical layer signals/channels
        Physical layer procedures including initial access and mobility, scheduling, (H)ARQ, power control, etc
      Higher layers study on:
        Compact protocol stack and lightweight signaling procedure, including mobility aspects
          Control plane functionalities, including CN connectivity
          User plane functionalities
          Security aspects (*Note: This does not necessarily mean security has RAN impact)
      RAN3 aspects for study:
        Enabling necessary CN-RAN signalling
        RAN architecture aspects, if any
      RAN4 aspects for study:
        Feasibility study of BS/UE/device architectures
        Link budget study
        Coexistence analysis
        RRM

## Slide 22: Network Energy Savings WI
References: RWS-230488, RP-231540, RP-232615
Potential objectives:
  On-demand SSB transmission ([and possibly other DL signals]) for Scell for connected UEs
    Possible triggering methods (e.g., UE uplink wake-up-signal using an existing signal/channel, cell on/off indication via backhaul, Scell activation/deactivation signaling, etc.)
    Whether to target the design of a simplified SSB
  On-demand SIB1/[SSB] transmission for idle UEs
    Possible triggering methods (e.g., UE uplink wake-up-signal using an existing signal/channel, cell on/off indication via backhaul, Scell activation/deactivation signaling, etc.)
    Whether to target the design of a simplified SSB
  Other topics?
  [SSB]/SIB1-less operation in multi-carrier scenario for (documented in TR38.864)
    [SSB]/SIB1-less for non-anchor NES cell for UEs in IDLE/INACTIVE state, where it is assumed that another carrier (an anchor cell) is available for the UE
  Adaptation of common signal/channel transmissions (documented in TR38.864)
  Specify Cell DRX/DTX for UEs in idle/inactive modes (as an extension of Rel-18 cell DRX/DTX)
  Multi-TRP adaptation mechanisms
  UE group-common or cell-specific BWP configuration, adaptation and/or switching.
  Group cell switch
  Power domains studied in R18 (techniques D-2 ~ D-5)
  Low-power SSB/SIB1/Paging
  Extension of spatial and power domain techniques in 1) high load scenarios 2) Type-II codebook types
  Semi-static beam-specific broadcast channel configuration
  Scenario 2a for SSB-less
  It was also mentioned that some proposals for multi-carrier enhancements may be beneficial for network energy savings (e.g. cross-carrier HARQ, fast DL carrier switch, multi-carrier CSI)
  Extensions to network-controlled repeaters (NCR), e.g. backhaul/control link behavior for efficient interaction between NES-capable gNB and associated NCR, to consider the case where the gNB would operate with S/P-domain adaptation or cell DTX/DRX adaptation for NW energy saving

## Slide 23: LP-WUS/WUR WI
References: RWS-230488, RP-231540, RP-232616
Potential objectives:
  Waveform & LP-SS support
    Waveform-option-1 + waveform-point-3, or waveform-point-3 only  Further downselection
      Waveform-option-1: OOK-1 and/or OOK-4, as described in section 7.2.1.1 (A)(D) in TR38.869.
      Waveform-option-3: Harmonized design that accommodates OOK-1/OOK-4 and OFDM waveform, i.e., specified overlayed OFDM sequences over OOK symbol
    For RRC IDLE/INACTIVE, in addition to existing PSS/SSS, LP-SS (, i.e., OOK-1 and/or OOK-4 waveform with/without overlayed OFDM sequences with potential further down selection in WI phase) for LP-WUR that cannot receive existing PSS/SSS, is supported for synchronization and/or RRM for serving cell.
For IDLE/INACTIVE operation, specify
  UE serving cell RRM measurement offloaded from MR to LR
  Further time domain relaxation (at least X times) of UE MR RRM measurement for both serving and neighbor cell measurement
    X to be determined in the WI phase
Note: For CONNECTED mode, UE RRM/RLM/BFD/CSI measurements are performed by MR
To specify an LP-WUS design commonly applicable to both IDLE/INACTIVE and CONNECTED modes
For IDLE/INACTIVE mode, to specify procedures to allow UE MR paging monitoring triggered by LP-WUS
For CONNECTED mode, to specify procedures to allow UE MR PDCCH monitoring triggered by LP-WUS
At least duty-cycled monitoring for LP-WUS is supported
Note: LP-WUS shall be able to reach at least the coverage of PUSCH for message3

## Slide 24: ISAC SI
References: RWS-230488, RP-231540, RP-232617
RAN to select a small number of ISAC use cases from TR22.837, and to identify appropriate corresponding information needed for the point below, i.e. scenarios, frequency ranges and sensing modes.
  Also consider the ongoing SA1 TS22.137
Potential objectives:
  A RAN1-led study objective to define channel modelling details for sensing using 38.901 (if applicable to the selected use cases) as a starting point, and taking into account relevant measurements, including:
    a. modelling of sensing targets and background environment, including, for example (if needed by the selected use cases), radar cross-section (RCS), mobility and clutter/scattering patterns;
    b. spatial consistency.
  This objective to start after completion of the first (RAN-led) objective if not already done in SID.
  Anything else?

## Slide 25: Exploring study in new spectrum (7-24GHz) SI
References: RWS-230488, RP-231540, RP-232617
Potential objectives (starting from Q2’2024):
  Validate using measurements the channel model of TR38.901 for 7-24 GHz, and
  As necessary: To adapt/extend as necessary the channel model of 38.901 for at least 7-24 GHz, additionally including at least the following aspects for applicable scenarios:
    Near-field propagation;
    Spatial non-stationarity.
Note that continuity of the channel model in the frequency domain shall be ensured.
Note that mathematical and/or theoretical aspects (if any) may be studied before results of measurement campaigns are available. Study of measurement results is likely to be able to start in Q3 2024 (Note: measurement results may be available and submitted earlier).
anything else?

## Slide 26: Mobility Enhancements WI
References: RWS-230488, RP-231540, RP-232618
Potential objectives:
  Specify support for inter-CU Layer 2 Mobility (LTM)
    Prioritize the case when CU is acting as MN when DC is not configured
    Whether to additionally support e.g. when CU is acting SN? (focus on practical deployments)
      In this case, whether it is supported for EN-DC and/or NR-DC only?
  Measurements related enhancements for purpose of supporting LTM:
    Specify event triggered L1 measurement reporting for triggering LTM  depending on the detailed discussion in RAN#102, resolve how to avoid overlapping with similar objective in MIMO WI
    Specify support for CSI-RS measurements for LTM procedures and enable CSI-RS based beam management and/or other physical layer operations on candidate cells before LTM
  Support of conditional mobility (including set of candidate cells, UE evaluated mobility conditions, ability for UE to perform subsequent mobility procedures without need for RRC configuration) along with short mobility interruption time (similar to that achievable with LTM).
    Next Step question to consider the most appropriate approach to achieve this aim. For example, by specifying conditional triggering of LTM, or specifying support of Early TA or RACHless (as defined for LTM) to be used as part of layer 3 CHO, or possibly other approaches. If this questions cannot be concluded during the Rel-19 scoping discussion then it may be possible to start with a RAN2 study phase.
  Anything else (e.g., RAN4 related)?

## Slide 27: Enhancements for XR WI
References: RWS-230488, RP-231540, RP-232619
Potential objectives:
  Study and if justified, specify aspects related to multi-modality(intra-UE)/multi-QoS flow (intra-UE) (with coordination with SA2/SA4), and other aspects requiring coordination w/ SA initiated work as necessary (e.g., SA2/SA4 task list which may potential have RAN impact)
    Check in RAN#105
  Measurement Gaps / Scheduling restrictions: Specify enhancements for reducing the impact to capacity and impact to individual UEs with respect to scheduling restrictions for FR1 and FR2 inter-frequency RRM measurements with measurement gaps and FR2 intra-frequency measurements w/o measurement gaps. [RAN1, RAN2, RAN4].
  UTO-UCI: support multiple CG config
  CQI/CSI link adaption enhancement
    FFS exact scope: PDSCH reception based, Traffic related, Soft-HARQ
    FFS CBG enh.
  Delay aware / Delay adaptive (remaining time) scheduling
  PDCP Discard enhancements for PDU set discard enhancements for inter-PDU Set dependencies
    Coordination with SA2
  Power saving, DRX and PDCCH skip (excluding power saving for Multi-modal)

## Slide 28: NTN (Non-Terrestrial Networks) evolution - NR WI
References: RWS-230488, RP-231540, RP-232610
Potential objectives:
  RAN1-centric
    Coverage enhancements for Downlink focusing on which channels & signals (e.g., paging, DL control, etc.) and target (link level), and assess Satellite Beamhopping optimisations (system level)
      Do we need to study first?
      Including potential consideration for “Robust Notification/Alert for paging with no modification to SSB, with close coordination with SA2”
    Uplink capacity / throughput enhancement?  Need to be specific of what to be done (e.g., increasing multiplexing capacity beyond the means of spatial-multiplexing?)
  RAN2-centric
    Mobility enhancements, depending on R18 progress (e.g., Cell reselection enhancements from TN to NTN, Handover enhancements, Soft unchanged PCI switch)  all completed?
    Enhanced GNSS Operation for a UE with GNSS capability in RRC_CONNECTED mode when it’s out of GNSS coverage
  RAN3-centric
    Regenerative payload with full gNB
  RAN4-centric
    Coverage enhancements for Uplink focusing on HPUE. Msg5?
      Should HPUE for NTN be a separate project (led by RAN4)?  to be handled in RAN#103
    (RAN4 only) REDCAP
      Focusing on 1Rx only?
      Should REDCAP for NTN be a separate project (led by RAN4)?
  MBS via NTN (->) Broadcast only for NGSO

## Slide 29: NTN (Non-Terrestrial Networks) evolution - IoT WI
References: RWS-230488, RP-231540, RP-232621
Potential objectives:
  Store & Forward (requiring regenerative payload), with close coordination with SA2
  Capacity enhancements for Uplink???, similar to NR NTN (need to be specific)
  Mobility enhancements (depending on R18 progress. All completed in Rel-18?)
  Others?
    “Coarse Location Reporting” in case….(SA2/CT1 discussion?)

## Slide 30: AI/ML for Air Interface (Mobility) SI
References: RWS-230488, RP-231540, RP-232622
Potential objectives: possible down-scoping in RAN#102
  Type of mobility
    L3-based mobility and L1/L2-triggered mobility (LTM) are both considered
  HO optimization in Network side [/UE side], including
    Candidate/target cell prediction in L3-based mobility, or, candidate/target beam(s) and cell(s) prediction in LTM
  RRM measurement and event prediction, including
    Beam-level measurement prediction
    Cell-level measurement prediction, e.g., using intra-frequency measurement results to forecast the RRM measurement of inter-frequency/inter-RAT cells
    HO failure/RLF prediction
    Measurement events prediction
  LCM framework and others
    The conclusions in Rel-18 AI/ML study should be used as baseline
    Other impacts are further studied
  [UE RRM enhancement, RAN4]
  Note 1: no intention to change the existing framework for the mobility under connected mode
  Note 2: In the SID, target performance metrics and impacts should be clarified
  Note 3: Avoid overlap work with RAN3

## Slide 31: AI/ML for NG-RAN SI  WI
References: RWS-230488, RP-231540, RP-232623
Potential objectives:
  6 months SI + 12 months WI
  Rel-18 leftovers (depends on Rel-18 outcome), e.g.:
    Mobility optimization
      NR-DC
      UE Trajectory prediction
    Energy saving
      Prediction for energy cost
    Continuous MDT
  At least 1 At most 2 potential new use case/scenario which benefits from inference-based techniques
    Coverage and Capacity Optimization
    Potential Rel-18 use case enhancements (e.g. new scenarios for ES)
    QoE
    Slicing
    Note: Model training/inference at the DU and/or F1 enhancements must be justified by the use case
  Study: Consider available functionality specified in 5GC (NWDAF, MDAS) in order to align AI/ML framework between RAN and CN

## Slide 32: SON/MDT Enhancements WI
References: RWS-230488, RP-231540, RP-232624
Potential objectives:
  MRO enhancement for R18 mobility mechanisms, Lower layer triggered mobility (LTM), CHO with candidate SCGs, subsequent CPAC [RAN3, RAN2]:
    Specification of the inter-node information exchange, including possible enhancements to interfaces[RAN3];
    Identify and specify necessary UE reporting to enhance the mobility parameter tuning [RAN2]
  Only SON/MDT enhancements for intra NTN mobility, Network slicing and NW energy saving are for further consideration.
    Details of these aspects (e.g., spec changes, assessment of workload).
    No other new features are to be added
  For NW energy saving, Note: avoid duplication with AI for NG-RAN.
  R18 leftovers, FFS details, which can be decided based on further progress in RAN2/3 [RAN3, RAN2]

## Slide 33: Additional topological improvements SI  WI
References: RWS-230488, RP-231540, RP-232625
Potential objectives:
  6 months SI + 12 months WI
Study enhancements for the support of WAB including (RAN3-led, RAN2):
  Study impact of gNB mobility within a stationary RAN and in proximity to other mobile gNBs:
    Identify the issues of dynamic inter-gNB neighbor relations resulting from gNB mobility, e.g., ANR, inter-gNB HO/DC and SON.
    Identify potential RAN-related issues when collocating a UPF with the gNB for MEC, local services and/or local inter-UE communications.
    Identify necessary inter-gNB- and gNB-to-CN signaling to address these issues.
  Study the signaling enhancements for the authorization of WAB nodes.
  Study signaling enhancements to extend the IAB resource multiplexing framework to WAB, as necessary.
  Study enhancements to QoS support on WAB backhaul, as necessary (subject to interaction w/ SA2)
Study enhancements for the support of single-donor IAB topology, including (RAN2-led, RAN3):
  Study enhancements to the robustness of multi-hop routing within the IAB topology in presence of local IAB-node mobility.
Note: Access link for WAB backhaul can be TN or NTN.
Femto
Study the overall RAN architecture and required functional and procedural impacts for supporting 5G Femto deployments.
Study how to define the 5G access control mechanism by (re-)using the existing CAG functionality and identify needed enhancements (if any).
Study how to enable access to local services from the 5G Femto via collocated local UPF.
Note: The study involves a gap analysis of existing 5G functionality with HomeNB functionality.