## Slide 1: Way forward for FS_EnergySys
Qualcomm Incorporated, Nokia, Verizon, Lenovo, KDDI

## Slide 2: SA2 status
Two different directions were discussed (again) in SA2#164 for conclusion of KI#1 (“Network energy related information exposure”)
  OAM/CHF based solution to be defined by SA5
  New network function to be defined by SA2
Based on SoH in SA2#164 meeting, the New Network Function to be defined by SA2 was approved as a conclusion with working agreement (see WA#64), which is challenged in SA#105 meeting.
We propose a (possible) compromise solution
  Do not introduce new NF, use as much as possible existing features
  NWDAF would be responsible for estimating EC in different granularities

## Slide 3: Architecture
Estimation/Calculation formulas are the same as other solutions
  Based on ratio of data volume for each NF
NWDAF collects
  NF/NS/gNB level EC information OAM
    Already supported, no further enhancement is needed
  Data volume information directly from UPF (via SMF)
    In different level of granularities (UE, PDU, QoS Flow)
NWDAF estimates/calculates EC in UE, PDU, QoS Flow levels
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
NWDAF
UE
NEF
UE
AF
UE
OAM
UE
5GCNF

## Slide 4: Advantages
No (significant) architectural impact
  No new function
  No new interfaces
NWDAF already collects a wide range of data from various entities
  Collecting data volume in different levels is supported / is feasible without significant changes
  Collecting data from OAM is already supported
Other NFs (PCF/AF) already gets analytics from NWDAF for optimization
  Getting EC information from NWDAF is not a significant changes in other NFs
NWDAF already supports storing long-term data in ADRF
  EC information can also be stored in the same way, no need to introduce new capability

## Slide 5: Proposal
Agree WID version in SP-241302
Avoid technical vote in SA#105
Discuss further details in SA2 during normative work in Q4 2024