## Slide 1: Brief Introduction of R19 Energysys SID
China Mobile
SP-241313
3GPP TSG SA Meeting #105
Melbourne, Australia, September 10 – 13, 2024

## Slide 2: Brief Motivation——Benefits to the Community
Energy saving and sustainability are the topic for years that companies pursuit hard for, especially in 5G and afterwards.
“Energy saving as a service” is developed in SA1 when energy consuption info can be exposed and green energy usage can be steerred.
Many potential benefits operators can expect (e.g., listed 9 in RP-241529).
Currently, the energy saving are mainly for NF/Node level or Network Slice.
There is lack of mechanism to measure/monitor/exposure the E2E energy consumption info with finer granularity, e.g., per UE, per App.
There is lack of mechanism that the network can control/optimize the NF/Node/UE behavior based on energy consumption information

## Slide 3: FS_EnergyServ in SA1
R19 FS_EnergyServ (TR22.882) start August 2022(SP-220446,20 supports),scope includes:
  Defining and supporting energy efficiency criteria as part of communication service to user and application services;
  Supporting information exposure of systematic energy consumption or level of energy efficiency to vertical customers;
R19 EnergyServ WID (SP-230520 ,25 supports) objective:
  Energy related information as Service Criteria. Support of different energy states of network elements and network functions. Optimization of 5G network functions based on energy related information. Temporary pooling of coverage layer for energy saving. Monitoring and measurement related to energy efficiency.Energy related information exposure. Security, charging and privacy.
R20 FS_EnergyServ_Ph2 (TR22.883) start at March 2024(SP-240494,29 supports, 16 operators). Objectives:
  Information exposure of energy-related characteristics of the network for the communication service (i.e. energy consumption, energy supply mix, carbon footprint, energy capacity and availability conditions) to authorized users or authorized 3rd parties.
  Potential dynamic adjustments of the delivered communication service from 5G system perspective (including service performance adjustments) resulting from the changes of energy-related characteristics of this service....
SA1 has 3 R20 SIDs, FS_EnergyServ_Ph2 consumes nearly 50% of SA1 R20 SID TUs.

## Slide 4: SA2 R19 FS_EnergySys (1/2)
September 2023
FS_Energysys is the first high prioritized SA2 SID approved in SA#101, 33 supports (14 operators)(SP-231192).
The total TU until now is 8.5 TUs
May 2024
Companies proposed 39 solutions in TR23.700-66 (11 for KI#1, 18 for KI#2, and 17 for KI#3).
    KI#1:the architecture of Energy Consumption information calculation, and the basis for KI#2&KI#3.
    KI#2: the subscription and policy control to support energy efficiency.
    KI#3: existing feature enhancement including NF selection and analytics.
KI#1 is the basis for KI#2 & 3 and for future work. It addresses how to monitor and calculate the energy consumption information for specific UE(or e. g. per UE per application).
Four SoHs on KI#1 conducted, majority companies support a new NF(defined by SA2) and per UE granularity energy consumption information exposure. (see Annex.1). Three companies proposed to reuse CHF.
The SID conclusions on KI#1, 2, 3 are reached at the last minutes of the meeting.
The WID is left for email approval and NOTED.

## Slide 5: SA2 R19 FS_EnergySys (2/2)
June 2024
SA#104 approved 13 SA2 R19 WIDs without EnergySys which got the most number of company interest.
Extensive discussion in SA and SA tasks SA2 and SA5 leaderships to work together to work out a way forward
  SA2&SA5 leadership have CCs
  SA2 and SA5 delegates have CC to clarifies what has been discussed in SA2
  NWM opinion collects all company views.
August 2024
SA2 further clarifies three solutions new NF (S2-2408985), OAM based (S2-2407887), CHF based(S2-2408986)
The companies’s position are not changed as compared with SA2 may meeting
The energy consumption calculation reach common understanding. OAM is first ruled out.
Show hands shows clear majority still for new NF: new functionality(Y:15, N:3), CHF(Y:4, N:16)
SA2 achieves Working Agreement (show hands:23 vs 3) as in S2-2409296 and the WID S2-2409559.

## Slide 6: Proposal
It is proposed the WA be confirmed in SA#105 to approve the WID.
  The solution may not be perfect (i.e., more precise with RAN reporting) but it set a basis for future work in 5G-A outwards
In case WA not confirmed
  No SA2 futher R19 study. No normative work for EnergySys Phase 1.
  SA1 may clean up R19 requirements and reconsider the on-going R20 Phase 2 study.

## Slide 7: Annex- General on calculations
Per UE EC= ECRAN,UE +∑ECupf,UE
EECF, CHF or OAM do the calculation.
Approach 1: data volume and NF EC information ECupf,ue=*ECupf， ECran,ue= *ECran
  ECupf , DVran, ECran are from OAM,
  DVupf, ue=DVran,ue are from UPF
  Approach 2:data volume, UPF EC information, and RAN reporting
  ECupf,ue=*ECupf, ECran,ue=RAN reporting
  ECupf is from OAM.
  DVupf, ueare from UPF

## Slide 8: Annex- 5GC functionality-determined by SA2
New NF EECF
New NEF exposure services
EECF do the calculation.
Approach 1: data volume and NF EC information ECupf,ue=*Ecupf， ECran,ue= *ECran
  ECupf , DVran, ECran are from OAM, and the SMF ID is provided from UDM to EECF. RAN ID is provided from AMF to EECF.
  DVupf, ue=DVran,ue are from UPF(I-UPF and PSA UPF)
  Approach 2:data volume, UPF EC information, and RAN reporting
  ECupf,ue=*ECupf, ECran,ue=RAN reporting
  ECupf is from OAM, and the SMF ID is provided from UDM to EECF(SMF knows the UPF/I-UPF which supporting the UE). RAN ID is provided from AMF to EECF.
  DVupf, ueare from UPF(I-UPF and PSA UPF)
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
EECF
UE
NEF
UE
AF
UE
OAM
UE
UDM
UE
5GCNF
Architecture of 5GC supporting EnergySys

## Slide 9: Annex-- CHF based solution
No new NF, enhancements to existing NFs
CHF to calculate the EC information per UE
  The CHF provides the DVupf,UE=DVran,ue
  OAM provides ECupf, ECran, DVupf, DVran
  SMF provides UPF IDs to CHF
  ULI reporting is used to provide RAN IDs
Significant OAM capacity needed to provide ECupf and ECran (approach 1) measurement/estimations to CHF
  Same for all solution in these slides
CHF is enhanced to support to UE EC exposure to NEF/NF.
Problem: CHF does not have I-UPF information. Therefore the CHF cannot generate the I-UPF EC of the UE.
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
NEF
UE
AF
UE
CHF
UE
5GCNF
CHF expose the EC of UE to NEF/NF
UE
OAM

## Slide 10: Annex-Comparison
Solution# | Per UE EC calculation | Evaluation
5GC New functionality | Approach 1 RAN, I-UPF, PSA-UPF Node level EC from OAM; RAN node level DV from OAM DVupf,ue=DVran,ue Approach 2 ECran,ue reporting from RAN | EC ran, EC-upf, DV-ran from OAM New NF Corresponding exposure service, Decided by SA2.
CHF | Formula the same as the Sol#1 approach 1, except the CHF provides the DVupf,UE=DVran,ue CHF needs to get the ECupf, ECran, DVupf, DVran from OAM DV from CHF but without I-UPF related information | Enhancement in SA5 to support the I-UPF EC information calculation New exposure service to support CHF information exposure Interface between CHF and OAM to support CHF getting the ECupf, ECran, DVupf, DVran from OAM Decided by SA5.