## Slide 1: Views on SA Rel-20 5G-A
ETRI, SK Telecom, KT, LG Uplus

## Slide 2: General Views on Rel-20
Rel-20 roles & general considerations
  Rel-20 should be prepared for and be linked to 6G, to ensure a smooth transition and continuity of network services.
  The number of items should be limited based on the maximum TU budget for WGs.
Expected to be considered in 6G and expanding the network portfolio
  Supporting new services and verticals (e.g., AI and Communication, ISAC, Ambient IoT, etc.)
  Expanding the network to include TN/NTN, 3GPP/Non-3GPP, etc.
  Supporting new network requirements, such as energy efficiency, softwarization, cloud-native, etc.
Commercial deployment issues and consideration for 5GS enhancements
  Network/service openness (Open network APIs - CAPIF, CAMARA (GSMA), Open gateway (GSMA), etc.)
  Network management for CAPEX/OPEX efficiency (e.g., network optimization, failure recovery, energy efficiency, etc.)

## Slide 3: Focus Items and Prioritization
AI/ML_CN - Phase 2
EnergySys - Phase 2
Satellite access enhancement
Integrated Sensing and Communications (ISAC)
Ambient IoT
Net Sharing - Phase 2
UIA_ARC - Phase 2*
** These items are not in order of priority or ranked in any specific order.
* This item is selected and supported only by ETRI.

## Slide 4: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1. | AIML_CN – Phase 2 (See slide 7 for more details) | 5G system currently provides assistance functions for data insights (analysis and prediction) and policy assistance based on AI/ML technologies. However, further research is required in terms of evolving policy automation and managing data and models in conjunction with UE and RAN Key Work Tasks includes defining - Reinforcement learning-based policy determination enhancements Cross-domain collaborative AI/ML operation involving UE, 5GC, and OTT Model transfer architecture and procedure based on ML model ID for managing ML models of UE and RAN Extension of ADRF dataset profiles and model request procedures | - | SA2 | Yes, Major | SA3 for security, SA5 for charging
2. | EnergySys – Phase 2 (See slide 8 for more details) | Advancing 5G network energy efficiency with enhanced KPI frameworks, secure energy data exchange, and dynamic NF optimization mechanisms. This proposal emphasizes refining energy consumption metrics, enabling real-time monitoring tools, and implementing traffic and resource management strategies to achieve sustainability goals while maintaining high-quality service delivery. Key Work Tasks includes defining - Expanding KPIs to include traffic-based energy efficiency and carbon metrics. Developing APIs for seamless energy consumption data exchange between UDR, PCF. Implementing NF scaling and dynamic traffic routing for real-time energy optimization. Supporting UE-based energy-saving with battery status reporting and QoS adjustments. | Yes, TR 22.882 (Phase 1), TR 22.883 (Phase 2), TS 22.261 | SA2 | No | SA5 for monitoring, Charing , CT4 for API design and security,

## Slide 5: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | Satellite access enhancement (See slide 9 for more details) | 5G system support for integrating of satellite components in the 5G architecture Key Work Tasks includes defining - Enhancements for multi-orbit satellite access in terms of service continuity, network selection, traffic switching/steering, QoS policies, charging Support for UE-Sat-UE communications within 5G-LAN via satellite access GNSS independent operation & positioning enhancements for satellite access Support for IMS voice calls using GEO satellite access | Yes, TR 22.865, TR 22.887, TS 22.261, | SA2 | Yes, Alignment | SA3 for the security, SA5 for charging, SA6 for application enlaber
4 | Integrated Sensing and Communications (See slide 10 for more details) | 5G system support for NR-based sensing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g., shape, size, orientation, speed, location, distances or relative motion between objects, etc.) using NR RF signals. Key Work Tasks includes defining - Overall architecture and function enhancement to support new sensing service. Basic functionality and E2E procedure for Sensing service exposure, Discovery and selection of the sensing entities, Authorization, Sensing control parameter generation and provisioning, related QoS/Policy enhancement. Enhancements for Non-3GPP sensing, sensing data transport/storage, sensing data processing with AI/ML support | Yes, TR 22.837, TS 22.137 | SA2 | Yes, Major | SA3 for security, SA5 for charging, SA6 for application enlaber

## Slide 6: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5 | Ambient IoT (See slide 11 for more details) | 5G system supports Ambient IoT device that is an IoT device powered by energy harvesting, being either battery-less or with limited energy storage capability. Key Work Tasks includes defining – Architecture to support Ambient IoT Ambient IoT Device management Ambient IoT Service enabler for Inventory, Read, Write and permanently Disable. | Yes, TR 22.840 TS 22.369 | SA2 | Yes, Alignment | RAN for traffic, SA3 for security
6 | Indirect Network Sharing -Phase 2 (See slide 12 for more details) | The 5G system investigate new requirements related to indirect network sharing on disaster condition and case of sharing satellite access network. Key Work Tasks includes defining - Whether and how to be aware of which NFs of Participating 5GC in the disaster area How to provide and control the participating operator’s information when UE accesses the shared satellite access network | Yes, TR22.851, TS 22.261 SP-241147 SP-241393 | SA2 | No or Don’t know | 
7 | User Identities and Authentication Architecture - Phase 2* (See slide 13 for more details) | The 5G system identifies human users and their traffic, enabling operators to implement user-based controls and offer user-based services to 3rd parties. Key Work Tasks includes defining - How 5G system identifier human user How 5G system Identifies application instances and provides differentiated service control How and what user profile information can be exposed to 3rd parties. | Yes, TS 22.101, TS 22.115 | SA2 | No | SA3 for security, SA5 for charging
* This item is selected and supported only by ETRI.

## Slide 7
Reinforcement Learning-based Recommendation
  Reinforcement learning-based policy recommendation evolved from the current machine learning-based policy assist functionality in AIML_CN
Cross-domain collaborative AI/ML operation involving UE, 5GC, and OTT
  Defining and improving AI/ML Life Cycle and related procedures across UE, 5GC, and OTT
ML model transfer to UE/RAN
  An update architecture and procedure based on ML model ID for managing machine learning models of UE and RAN in the core network
ADRF dataset profile enhancement
  Improving data management efficiency and model reusability through the extension of ADRF dataset profiles and model request procedures
AIML_CN – Phase 2

## Slide 8: EnergySys – Phase 2
Advancing 5G-A network energy efficiency with enhanced KPI frameworks, secure energy data exchange, dynamic NF optimization mechanisms, etc.
    Formalization of traffic-based energy efficiency metrics.
    Implementing robust API solutions for seamless integration of UDR and PCF energy data with vertical industries.
    Deployment of NF scaling and dynamic traffic adjustments to optimize energy efficiency while maintaining QoS.
    Standardized methods for embedding energy consumption and environmental impact evaluations into 5G network operations.
    Supporting UE-based energy-saving with battery status reporting and QoS adjustments
    Proactive measures for energy efficiency linked with AI/ML technologies
Collection
Calculation
Exposure
Subscription Information
Energy-related policy control
Dynamic service adjustment support in the network based on energy information (Src.: SA1 TR 22.883)

## Slide 9: Satellite access enhancement
Background
  SA1 Rel-20 requirements are being developed [TS 22.261, TR 22.887]
    New use cases: multi-orbit, emergency/critical, IMS using GEO, resilient notification, broadcast for unregistered UEs
  SA2 Rel-19 5GSAT_Ph3 leftovers
    GNSS-related, UE-Sat-UE via UPF-onboard
Target topics
  for multi-orbit satellite access
    Service continuity, network selection, traffic switching/steering, QoS policies, charging
  for UE-Sat-UE communications
    5G-LAN support with UPF-onboard
  GNSS-related
    GNSS-independent positioning for satellite access
  IMS Voice Call using GEO Satellite Access
    Enhancements to IMS voice call using GEO satellite access
<Multi-orbits 5G satellite access for autonomous vehicle operations> [TR 22.887]

## Slide 10: Integrated Sensing and Communications
Background
  SA1 Rel-19 requirements have been developed [TS 22.137]
    General, configurations, authorization, network exposure, security/privacy, charging
  SA2 Rel-19 SID was endorsed [SP-231365]
Target topics
  Architectural enhancement for new sensing service
  Basic functionality
    Sensing service exposure, Discovery and selection of the sensing entities, Authorization, Sensing control parameter generation and provisioning, related QoS/Policy enhancement.
  Enhancements
    for Non-3GPP sensing, sensing data transport/storage, sensing data processing with AI/ML support
<5G system support for ISAC>

## Slide 11: Ambient IoT
Items to be discussed for 5G-Adv
  Develop specification for what is studied in Rel-19 (FS_AmbientIoT)
    Study on Architecture support of Ambient power-enabled Internet of Things
  Architecture for Topology 1 and Topology 2 to support Ambient IoT service in 5GS
  Identifiers for Ambient IoT devices
  Registration and Connection Management for Ambient IoT devices
  Ambient IoT reader authorization
  Ambient IoT data transfer between AIoT device / reader / AIoTF

## Slide 12: Net Sharing- Phase 2
Further studies on the remaining issue in TEI19 Net Sharing from Rel-19
  Investigation on how to enable the NFs from the participating operator network to identify the Indirect Network Sharing case
New WTs to fulfill SA1 requirements
  Indirect Network Sharing Phase 2 on Disaster Condition(SP-241147)
    Investigation on how to fulfill the several disaster case considering the legacy UEs.
  Indirect Network Sharing on Satellite Access Network(SP-241393)
    Network access control considering the overlapping new scenarios involving the subscribed network, terrestrial shared network, and non-terrestrial shared network.
<Long-distance mobility in and across shared networks> [TR 22.851]

## Slide 13: UIA_ARC - Phase 2
Further studies on unresolved Key Issues from Rel-19
  Key Issue #1: Identifying the Human User of a Subscription
  Key issue #2: Authentication and Authorization of Users and Restrictions on Users
  Key issue #3: Exposure of User Identity Profile Information
New WTs to fulfill SA1 requirements
  Identification and differentiated service control for each application instance
Application instance 1
Application instance 2
Application
5GC
User Identity Profile provisioning
Active user identity exposing
Slice ‘A’, 5QI = ‘x’
Slice ‘B’, 5QI = ‘y’

## Slide 14: Focus Items - Summary
AIML_CN – Phase 2
ISAC
Ambient IoT
New services & Verticals
EnergySys – Phase 2
Net Sharing – Phase 2
UIA_ARC - Phase 2
Architecture enhancements
Preparatory works for 6G should be also considered (not limited to Rel-20)
  Integration of computing, routing, and storage capabilities
  RAN-Core convergence: Evolution of SBA
  Highly reliable mobile networks based on Digital Twin Network
Satellite access enhancement
Expanding the network access