## Slide 1: CATT views on SA Rel-20 5G-Advanced
Ming Ai
Delegate, CATT

## Slide 2: Outline
Overall view on SA Rel-20 5G-A content (CATT interested 6 topics)
  Detailed of those topics.
  Summary.

## Slide 3: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Integrating satellite component into 5GS_ph4 (See slide 6,7 for more details) | Further enhancing 5G system integrating with satellite components to satisfy new requirements for satellite enabled services, such as satellite IoT services, satellite voice/video services, and for satellite based network operation, including resilience notification, multi-orbit satellite access co-ordination, and satellite access network sharing. Key Work Tasks includes defining - UE-sat-UE communication: for roaming scenario, and for mission critical IMS voice call via GEO satellite(s) Co-ordination among multi-types of satellite access Store and forward services with the support of ISL. Resilience notification services Support of indirect sharing of satellite access network | Yes, TS 22.261 | SA2 | Yes, Major | SA3 for security, SA4 for codec, SA5 for charging
2. | Architecture Enhancement for XRM Ph3 (See slide 8,9 for more details) | Avatar, MBMS-based, UE2-to-UE direct XR communications are not studied, Multi-Modality XR communication needs to support the XR streams multiplexed in the same transport connection. AL-FEC is not supported. New traffic characteristics and network openness needs further enhancements. Key Work Tasks includes defining - Enhancement for Avatar-based XRM communication.; Enhancement for MBS-based XRM communication.; Enhancement for coordination control of the multiplexed data flows in the same transport connection. Enhancement for support AL-FEC. PDU Set QoS handling enhancement. QoS handling enhancement for XRM services. New XRM communication scenarios. Network capability openness. | Yes, TS 22.156 | SA2 | Yes, part | SA3 for security, SA5 for charging SA4 for traffic characteristics.

## Slide 4: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | Integrated Sensing & Communications (See slide 10 for more details) | 5G system support for NR-based sensing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g., shape, size, orientation, speed, location, distances or relative motion between objects, etc.) using NR RF signals. Key Work Tasks includes defining - Overall architecture and function enhancement to support new sensing service. Basic functionality and E2E procedure for Sensing service exposure, Discovery and selection of the sensing entities, Authorization, Sensing control parameter generation and provisioning, related QoS/Policy enhancement. | Yes, TS 22.137 | SA2 | Yes, Major | SA3 for security, SA5 for charging
4. | Architecture Enhancements for Vehicle Mounted Relays Phase 3 (VMR_Ph3) (See slide 11 for more details) | Mobile gNB with Wireless Access Backhauling was introduced in Rel-19 which provides NR access link to UEs in proximity and connects to the 5GC serving the UE through an IP connectivity provided by a backhaul PDU session. However, QoS enhancement for UE connecting to MWAB-gNB is not in scope of Rel-19 VMR_Ph2 WID. So several issues come up. Furthermore, SA1 has approved the Rel-20 VMR_Ph3 WID in SA1#108 meeting to add new requirements related to QoS for UE accessing MWAB-gNB. Key Work Tasks includes defining - QoS enhancements for UE connecting to MWAB-gNB in different scenarios, e.g. during MWAB-UE mobility between terrestrial access network and satellite access network. When MWAB-UE accesses 5GC via satellite access, how does the 5GC serving UE know the satellite backhaul type and the satellite backhaul category change. | Yes, TS 22.261 | SA2 | Yes | No

## Slide 5: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5 | Ambient IoT Ph2 | Based on Rel-19 defined Ambient IoT architecture and procedures, further enhancements to support new requirements and use cases. Key Work Tasks includes defining - Support of location service for AIoT Device for both Topology 1 and Topology 2. Support of DO-A traffic type. | Yes, TS 22.369 | SA2 | Yes, Major | SA3 for security, SA5 for charging
6. | EnergySys_Ph2 (See slide 12 for more details) | Further system architecture enhancements are required to meet R20 5G-A SA1 energy efficiency as service criteria requirements and to optimize network energy consumption. Key Work Tasks includes defining - Expose network energy information to the UE Expose network capabilities and validity conditions for energy saving Enhancements on subscription and policy control, and others UE-assisted network energy saving | Yes, TS 22.883 | SA2 | No or minor | SA5 (e.g. energy calculation), SA3 (e.g. user consent)

## Slide 6: #1.1: Integrating satellite component into 5GS_ph4
3. Co-ordination among multi-types of satellite access
  UE policy enhancement for network selection considering satellite access type.
1. UE-satellite-UE communication enhancement
  Support of IMS services for roaming UEs, including one or both UEs are in roaming status.
  Support of UPF only on board satellite to enable UE-satellite-UE communication.
  Support of mission critical services which would require 1 to many communication via satellite access
2. IMS voice call via GEO satellite access
  QoS adaption considering characteristics of NR-GEO satellite access
  Optimization of IMS call flow and signaling to shorten call setup latency.
  New codec for IMS voice media for lower bit rate, KPI set by SA1 is 1-3 kbit/s
From Rel-20 SA1 5GSAT_Ph4
In Rel-20 SA1 FS_5GSAT_Ph4, 18 use cases on multi-orbit satellite access were identified. E.g.
Access MEO/GEO in discontinuous coverage of LEO
Data transmission in LEO, and return to GEO
Different services in different orbit satellite
Service Hosting environment n different satellite
Network Entry in GEO, completion in LEO

## Slide 7: #1.2: Integrating satellite component into 5GS_ph4
6. Support of indirect sharing of satellite access network
  network selection and access control for UEs using satellite access
4. Store and forward services with ISL
  Store and forward for 5GS
  Network architecture enhancement to support Store and forward with ISL
  Cooperation between satellites connected via ISL to store UL/DL UE data, especially for user plane
5. Resilience notification services
  Define a new service to notify UE of the DL data pending
  Align with RAN2 conclusion to support new paging mechanism.
T1: Notify UE of the missing MT calls/messages via satellite access, incl. service info. e.g. caller’s info, service type;
T2： The user calls back when the network is available and regarding the urgency
Rel-20 SA1 5GSAT_Ph4 defines resilient notification service.
Rel-20 SA1 INS_SAT introduces more business models based on satellite network sharing. INS is the basic mechanism.

## Slide 8: #2.1: Architecture Enhancement for XRM Ph3
WT#1 Enhancement for Avatar-based XRM communication.
  Study the traffic characteristics of Avatar-based XRM communication;
  Study the QoS requirements for the traffic of Avatar-based XRM communication;
  Study whether and how to define new 5QI(s) for Avatar-based XRM communication;
NOTE: This will require close coordination between SA4 and SA2.
WT#2 Enhancement for MBS-based XRM communication.
  Study whether and how to enhance MBS to support PDU Set QoS;
  Study whether and how to enhance MBS to support PDU Set marking
  Study whether and how to leverage PDU Set QoS information for DSCP marking over the MBS transport network (i.e. to enable differentiated handling of PDU Sets within MBS QoS Flow).
WT#3 Enhancement for coordination control of the multiplexed data flows in the same transport connection.
  Study whether and how to coordinate the QoS control between multiplexed data flows, e.g. the PSI, PDB/PSDB, PER/PSER, Alternative QoS profile and QoS Notification Control;
  Study whether and how to perform the admission control between the multiplexed data flows, e.g. if the radio resource is not available for all the multiplexed data flows during the HO and PDU Session management procedure;
  Study whether and how to define new coordination mechanisms and parameters e.g. the delay threshold between the multiplexed data flows;

## Slide 9: #2.2 : Architecture Enhancement for XRM Ph3
WT#4 Enhancement for support AL-FEC.
  Study whether and how to support the AL-FEC with static or dynamic content radio;
  Study the enhancement of policies and PDU Set marking to support the AL-FEC;
WT#5 PDU Set QoS handling enhancement.
  Study whether and how to handle the lonely PDU to avoid the invalidity of TTNB and Periodicity.
  Study whether and how to handle the retransmitted RTP packet from the application server, e.g. PDU Set marking, and QoS handling.
  Study whether and how to handle the PDU Set Size Correction.
WT#6 QoS handling enhancement for XRM services.
  Study whether and what N6 metadata on XRM service is provided by the AS and study how to handle such N6 metadata, e.g. the AF can provide service information to 5G network based on the RTCP messages (e.g. SR, RR, NACK, etc.) to support the QoS handling of the XRM services.
WT#7 New XRM communication scenarios.
  Study whether and how to support UE to UE direct media stream communication via the UPF(s) without transferring the media gateway.
WT#8 Network capability openness.
  Study what network capability needs to be opened to the AS/AF.
  Study how the network capability is to be opened to the AS/AF e.g. via the CP or UP.

## Slide 10: #3: Integrated Sensing & Communications
Work Tasks
    WT#1: Architecture and function enhancements to support sensing.
    WT#2: Service authorization and revocation. This includes investigating mechanisms for authorization and revocation sensing service requests from the service consumer (e.g. 3rd party application, 5GC NF).
    WT#3: Discovery and selection of sensing entities (e.g. gNB, 5GC NF) based on service requirements triggered by the service request and capability of the sensing entities.
    WT#4: Sensing data and the associated information collection and transport mechanisms for result calculation.
    WT#5: Service invocation, including providing sensing associated information, and result (including sensing result and contextual information) exposure mechanisms, for one time, periodic or event based reporting.
    WT#6: Configuration parameters/policy provisioning to gNB for the support of ISAC services.

## Slide 11: #4: Vehicle Mounted Relays Phase 3 (VMR_Ph3)
Motivation
  QoS enhancement for UE connecting via MWAB-gNB is not in scope of Rel-19 VMR_Ph2 WID.
  SA1 has approved the Rel-20 VMR_Ph3 WID in SA1#108 to add new requirements related to QoS for UE accessing MWAB-gNB.
Work Tasks
    WT#1: QoS enhancements for UE connecting to MWAB-gNB in different scenarios, e.g. during MWAB-UE mobility between terrestrial access network and satellite access network.
    WT#2: When MWAB-UE accesses 5GC via satellite access, how does the 5GC serving UE know the satellite backhaul type and the satellite backhaul category change?

## Slide 12: #6: EnergySys_Ph2
WT#1: Expose network energy information to the UE
  Make more mobile subscribers aware of and contribute to carbon emission reduction / energy saving endeavors
    WT#2: Expose network capabilities and validity conditions for energy saving
  Expose network energy related capabilities (e.g. high/low energy efficiency and/or renewable energy ratio) and associated validity conditions (e.g. time/area) to enable that:
      AF selects appropriate service specific parameters (e.g. QoS requirements, DNAIs);
      UE makes right energy related decisions (e.g. when selecting network slice), which may help network energy saving
    WT#3: Enhancements on subscription and policy control, and others
  Allow QoS degradation of specific services/applications (e.g. GBR QoS flows) due to network energy saving, while fulfilling basic service requirement / SLA / user consent.
    WT#4: UE-assisted network energy saving
  UE provides dynamic UE capabilities and energy saving demands to assist on flexible network capability adjustment and service provisioning.

## Slide 13: Summary
Besides those 6 topics, CATT are open to discuss other Rel-20 5G-A topics.
Given that there are quite a few years before 6G deployment, good standardization work of Rel-20 5G-A is very important for satisfying new commercial requirements via 5G-A in the coming years, i.e. before 2030.