## Slide 1: Apple views on SA2 Rel-20 5G-A

## Slide 2: High Level Overview of Rel-20 5G-A
Rel-20 is the release that needs to handle both the 5G evolution and 6G study
  Rel-20 carries the 3rd release of 5G-Advanced (5G-A) (6th release of 5G)
  Rel-20 also, concurrently, carries the 6G study
Our preference in terms of handling of the concurrent SA2 Rel-20 5G-A and 6G study
  SA2 Rel-20 focuses the TU allocation on 6G study (e.g., ~60-70%)

## Slide 3: Overview of SA2 Rel-20
Rel-20 5G-A will be parallel with 6G SA2 study
  Reasonable to limit 5G-A Rel-20 workload, to make the 6G study more useful and productive
  Choose 5G-A topics that have practical and commercial impact
    No leftovers from Rel-19 by default into Rel-20 discussions
    Sufficient reasoning (and discussion) on why Rel-20 5G-A should continue with Rel-19 leftovers
Overlap between topics of 6G SI and Rel-20 5G-A need clear justification

## Slide 4: Potential topics for SA2 Rel-20 5G-A

## Slide 5: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Enhanced Traffic Management (See slide 6 for more details) | Study whether and how to use MASQUE capabilities in the 5GC user plane for improved traffic management to support traffic ciphered end to end and/or scenarios where application server IP address cannot be used to differentiate application traffic flows. | No | SA2 | No | TBC
2 | Emergency SMS over IMS (See slide 7 for more details) | Study the architectural evolutions of the 3GPP System to support Emergency SMS over IMS for EPS and 5GS. - Identifying Emergency SMS over IMS based on the use of emergency numbers. - Routing of an Emergency SM over IMS to an emergency response center serving the UE location, including in roaming case. - Identifying the type of emergency service (police, ambulance, fire brigade, etc.), using the same identification methods as for emergency calls. - Support both 3GPP access and non-3GPP access - Support UE in limited-service state | Yes, TS 22.101 clause 10.11 (SMS2EC) | SA2 | No | TBC
3 | Architectural enhancements for non-3GPP access | Study low complexity, deployable solution for non-3GPP access in 5GS - potential architecture and system level enhancements for 5GS interworking system to support non-3GPP access (without the use of N3IWF/TNGF) for steering, switching, and splitting of traffic | No | SA2 | No | SA3 for security
4 | IMS voice calls using GEO satellite access | Study enhancements to IMS voice service via NB-IoT GEO satellite access - Support IMS signaling and media transmission - Simplify IMS procedures to reduce call setup time | FS_5GSAT_Ph4 | SA2 | Maybe | TBC
5 | Further AI/ML aspects | Study follow-up to Rel-18 and Rel-19 release AI/ML activities: - VFL enhancements including dynamic negotiation of Features (depending on the exception sheet progress), and change of VFL clients during training - Potential enhancements to expose 5GC information to UE to facilitate application AI/ML operations (e.g. revisit conclusion for Rel-18 study on KI#2 of FS_AIMLsys) | Yes TS 22.261, clause 6.40 | SA2 | TBC | SA3 for security

## Slide 6: Enhanced Traffic Management
Background: In Rel-19, Enhanced Traffic Management SID was not approved
  The IETF MASQUE (Multiplexed Application Substrate over QUIC Encryption) WG was chartered to specify secure proxy protocols and mechanisms based on QUIC and has delivered several RFCs, including RFC 9298.
  The first 3GPP use case to incorporate MASQUE technology has been ATSSS in Rel-18.
  In the field, MASQUE specifications are being used as part of so called “relay services” where two intermediate proxies enhance user privacy by separating user identity from accessed service to all entities along the communication path.
  MASQUE sets up a connection to a relay (aka MASQUE server) using QUIC as a tunnel transport which then forwards traffic through that tunnel to a target server or another relay.
  This technology also allows end-points (UE and application server) and in-network relays (UPF) to exchange information explicitly, which may enable opportunities for collaboration between the network and the application at the endpoint.
  Explicit collaboration between parties addresses the new communication patterns and user desire for control of privacy. 5GC UPF that integrates MASQUE may enable better in-network support of existing and emerging services and may be a chance for mobile network operators to establish new and well-defined business relationships. This justifies a study of the usage of MASQUE to enhance other 5GS use cases besides ATSSS.
Proposal: ETM SID for Rel-20 5G-A (S2-2412315)
  Some of the objections from Rel-19 times may get relaxed as relay services become frequently used in the field.
  Study whether and how to use MASQUE capabilities in the 5GC user plane for improved traffic management to support traffic ciphered end to end and/or scenarios where application server IP address cannot be used to differentiate application traffic flows.

## Slide 7: Emergency SMS over IMS
Background
  A TEI-19 WI did not progress in Rel-19
  Limitations for the proposed solution were identified but a more advanced solution was not considered
Proposal: Emergency SMS over IMS SID for Rel-20 5G-A (S2-2412316)
  Study the architectural evolutions of the 3GPP System to support Emergency SMS over IMS for EPS and 5GS.
    Identifying Emergency SMS over IMS based on the use of emergency numbers.
    Routing of an Emergency SM over IMS to an emergency response center serving the UE location, including in roaming case.
    Identifying the type of emergency service (police, ambulance, fire brigade, etc.), using the same identification methods as for emergency calls.
  Support both 3GPP access and non-3GPP access
  Support UE in limited-service state

## Slide 8: Summary
In the spirit of limiting 5G-A workload in SA2:
  Limit up to 5-7 studies not exceeding 30% of total TU capacity of SA2
Our priority topics:
  Enhanced Traffic Management (proposed in S2-2412315 by Apple)
  Emergency SMS over IMS (proposed in S2-2412316 by Apple)
  Architectural enhancements for non-3GPP access
  Support for IMS voice calls using GEO satellite access
  Further AI/ML aspects
Other topics:
  Energy Efficiency and Energy Saving Phase-2, including exposure of energy-related characteristics, service adjustments based on energy-related characteristics
  Satellite enhancements Phase-4, including Resilient notification, emergency communications and mission critical services using satellite access, multi-orbit aspects
  Ambient IoT WI: Inclusion to Rel-20 5G-A depends on RAN progress
ISAC SI
  Our preference: 6G SI (native ISAC) in Rel-20 and 6G WI (native ISAC) in Rel-21
  For 5G-A ISAC to happen in Rel-20, RAN1 should identify a clear commercial use case for ISAC and ensure both network-centric and UE-centric sensing are supported