## Slide 1: Way forward proposal on Architecture support of Ambient IoT

## Slide 2: R19 Ambient IoT scope for SA
SA2 Rel-19 work item scope for Ambient IoT
  Key issue 1 - Architecture support for device 1 and D1T1: Direct interface option and Indirect interface option
  Key issue 2- Device management for device 1
  Key issue 3- Service enabler for Inventory and Command for device 1 including the exposure and data transfer
SA3
  SA3 scope (including SID and WID) shall be reduced to only specify appropriate security features for device 1 and D1T1 with direct and indirect interface options.
SA5
  SA5 scope for the charging and OAM focus on device 1 and D1T1

## Slide 3: Workplan for R19
Stick to Rel-19 ASN.1 freeze time, no impact to the timeline of Rel-20.
  Stage 3 will be completed by September 2025
  SA2 normative work duration: 2025 Q1 + Q2
  SA3 continue the study and is expected to reach conclusions in 2025 Q1. Normative work duration: 2025 Q2 + Q3
  SA5 is expected to agree the work item in 2025 Q1. Normative work duration: 2025 Q2 + Q3
  No further study in parallel with the R19 normative work
  Rel-20 Ambient IoT (if prioritized for rel.20) starts after the completion of the Rel-19 Ambient IoT WI.

## Slide 4: SA2 aspects to be resolved during R19 normative work
Coordination among different working groups
  Architecture aspects to support security (with SA3).
  Whether and how to support enabling temporarily disabled AIoT devices (with SA3)
  Temporary ID or not (with SA3)
  AIoT RAN/BS reader selection (with RAN3)
  Protocol design for AIoT Reader control, whether using NGAP or a layer above NGAP (with RAN3).
SA2 issues to be resolved during the normative work
  The entity to store the static and dynamic information, and usage for the stored information
    There is demand from operators not to impact on UDM
  The length of AIoT device ID is fixed or dynamic and its part2 information
  AIoT data aggregation or not (to be coordinated with RAN3)
  NF profile details
  Detailed procedures and parameters in the message flow

## Slide 5: Possible workplan for Rel-20
D2T2 and Device 2
  Further work on D2T2, and device 2 in Rel-20 shall follow the Rel-19 study conclusions.
A limited number of additional use cases, deployments, connectivity topologies, devices, traffic types
Final scope of R20 needs further discussion and alignment with RAN.