## Slide 1
Fazel Salimi
<3GPP SA Delegate, KPN>
5G Advanced Priorities for KPN in Release 20

## Slide 2: Outline
Overall View on Rel-20 5G-A Content
KPN’s Focus Area and Use Cases
Summary

## Slide 3: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Ambient IoT | The study on Architecture support of Ambient power-enabled Internet of Things in Release 19 addressed the initial architectural enhancements and functionalities however, multiple aspects remain to be addressed such as reader association, mobility management and roaming, configuration, positioning, and energy availability considerations (see S2-2412348 for more details) Key Work Tasks include defining: WT#1 Ambient IoT device and reader association. WT#2 Architecture to support Ambient IoT device reachability and communication in roaming scenarios. WT#3 Architecture to support AIoT device management and configuration. WT#4 Architecture to support AIoT device positioning. WT#5 Support Ambient IoT services based on energy availability. | TS 22.369 | SA2 | Yes | SA3 for security, SA5 for charging
2 | Energysys / EnergyServ | Further upgrades of what has been standardized for SA2 Rel-19 EnergySys: To finalize the EnergySys work from Rel-19 which may be remaining. To provide solutions to support SA1 requirements from EnergyServ (Rel-20): Exposing carbon emissions data. Service adjustments based on energy-related information). | Yes, TR 22.882/ TS22.261 (Rel19) and TR 22.883 (Rel20) | SA2 | Yes, minor | SA3 for security, SA5 for charging and OAM

## Slide 4: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | Prose | Complete the support for Multi-hop ProSe Relay in 5G-A by adding the missing multi-path and Layer-2 UE-to-UE features. Key Work Tasks includes defining: WT#1 Multi-path for Multi-hop UE-to-Network Relay. WT#2 Multi-path for Multi-hop UE-to-UE Relay. WT#3 Support of Layer-2 Multi-hop UE-to-UE Relay. | TS 22.278 and TS 22.261 | SA2 | Yes, particularly for Layer-2 support | SA3 for security, SA5 for charging
4 | AI/ML | Further enhancements to the 5G system for ML model lifecycle management and update particularly in case of Reinforcement/Online Learning, model and flow transmission optimization, and to further enhance energy efficiency with AI/ML predictions and action recommendations. Key Work Tasks includes defining: Enhancements to support ML model lifecycle management. Enhancements to support AI/ML model and flow transmission optimization. AI/ML support for energy efficiency. Enhancements to support AI/ML exposure. | TS 22.261 | SA2 | Yes | SA3 for security, SA5 for charging
5 | Integrated Sensing & Communications | 5G system support for NR-based sensing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g., shape, size, orientation, speed, location, distances or relative motion between objects, etc.) using NR RF signals. Key Work Tasks includes defining: Overall architecture and function enhancement to support new sensing service. Basic functionality and E2E procedure for Sensing service exposure, Discovery and selection of the sensing entities, Authorization, Sensing control parameter generation and provisioning, related QoS/Policy enhancement. Enhancements for Non-3GPP sensing. | TS 22.137 | SA2 | Yes, Major | SA3 for security, SA5 for charging

## Slide 5: KPN’s Focus Area and Use Cases
EnergySys/EnergyServ
Ambient IoT
Logistics & Transportation
Smart Cities
Agriculture
AI/ML
E2E Service performance and experience optimization
Operational Efficiency
New AI-based businesses
ProSe
Emergency Services
Mission Critical Services
Indoor/Outdoor coverage extension
ISAC
Accurate Positioning Services
Real-time Mapping and Monitoring
Enhanced User Experiences
Net Zero Obligations
Regulatory Compliance
Cost Saving (!!)

## Slide 6: Summary
All five topics selected by KPN are equally important, with no single item taking priority over the others.
For the mentioned topics (such as EnergySys, ISAC, and AIoT), KPN requests that any original scope not completed in Release-19 be prioritized for continuation and completion in Release-20.
For the mentioned topics, KPN emphasizes the importance of achieving implementable solutions in Release-20, with particular attention to Security and Charging aspects.