## Slide 1: Cisco view on 5G-Advanced in Rel-20
Charles Eckel
Cisco Systems

## Slide 2: Cisco View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | SNPN cellular hotspots | 5G system support for stand-alone non-public network (SNPN) cellular hotspots. Requirements were added to TS 22.261 in Rel-19. 5GS architecture enables a Credentials Holder (CH) responsible for authenticating User Equipment (UE) to be decoupled from the operator of the SNPN. However, security aspects remain to be addressed. Key work task includes defining - Mechanisms that enable secure connection between SNPN and CH other than pre-configuration of addresses and certificates, including the following aspects: Establishment of secure connection(s) for bidirectional signaling between an SNPN and CH with no pre-established relationships between the SNPN and CH. Required lifetime (if any) of connection(s). | Yes. SA1 completed a study on interconnect of SNPN (FS_ISN), which resulted in addition of requirements to support SNPN cellular hotspots in TS 22.261. | SA3 | No | SA2 for architectural alignment
2 | Post Quantum Cryptography (PQC) in 5G Core | IETF is updating its protocols for PQC. Support for these needs to be incorporated into 5G Core in Rel-20 timeframe. Key Work Tasks include defining – An inventory of 3GPP protocols and algorithms used within 5GC in Rel 20 (can be updated for future releases). Update corresponding usage of these protocols and algorithm to address PQC requirements. |  | SA3 | Yes | 

## Slide 3: Cisco View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | FRMCS – Future railway mobile communication system | The UIC FRMCS 3GPP Task Force analysis has concluded that refining existing use cases, defining new use cases, and deriving potential new requirements will be necessary to align FRMCS specifications and 3GPP standards as part of Release 20 timeframe. Key Work Tasks includes defining - Update TR22.989 to add new use-cases and enhance the existing ones as well as to derive new potential requirements to stage 1 TSs (e.g., 5GS, MCX), if any. | FS_FRMCS_Ph6 [SP-241392] | SA2 |  | 
4 | Energy Saving Ph2 | Following the work on Energy Efficiency as service criteria in R19, more scenarios can be addressed to improve energy saving and energy efficiency end-to-end. Key Work Tasks includes defining - Information exposure of energy-related characteristics of the network (i.e., energy consumption, energy supply mix, carbon footprint, energy capacity and availability conditions) to authorized users or authorized 3rd parties. Potential dynamic adjustments of communication service from 5G system perspective (including service performance adjustments) resulting from changes of energy-related characteristics of this service. Other aspects including security, charging, and privacy for the scenarios above. | FS_EnergyServ_Ph2 [SP-240494] | SA2 |  | 

## Slide 4: Cisco View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5 | 5G SAT Ph4 | New capabilities for satellite access such as Store and Forward Satellite operation and UE-Satellite-UE communication have been addressed in SA1 5GSat phase 3 for Release 19. First commercial deployments of 5G based satellite are happening and several new use cases for satellite access or enhancements are to be addressed still in the context of 5G advanced (i.e. in Release 20). Key Work Tasks includes defining - Enhanced support for emergency communications and mission critical services using satellite access Support for IMS voice calls using GEO satellite access Support for multi-orbits satellite access for different services Ability to notify a user that a mobile terminated communication failed when the UE was unreachable in satellite access | FS_5GSAT_Ph4 [SP-240495] | SA2 |  | 
6 | Improved support for IMS voice over Wi-Fi in 5GC | Improved support for IMS voice over Wi-Fi connected to 5GC in standalone deployments (see S2-2411498) via a modernized ePDG connecting to the 5GC via SBI (S2-2411655; S2-2411656). Key Work Tasks includes defining - Support for IMS Voice over Wi-Fi connected to 5GC in standalone deployments without relying on N3IWF. This includes architecture to support ePDG connected to AUSF, UDM and NRF, without intermediate 3GPP AAA Server Impact to procedures for Attach and PDN Connection Establishment via ePDG when interfacing with AUSF and UDM | No | SA2 | No | SA3 for potential UE impact