## Slide 1: 3GPP Newcomers "quick-start" guide
Puneet Jain, 3GPP SA Chair
Peter Schmitt, 3GPP CT Chair
Wanshi Chen, 3GPP RAN Chair
Alain Sultan, 3GPP Work Plan Co-ordinator
3GPP TSG Meeting #106 SP-241883 / RP-243207 / CP-243302
Madrid, Spain, 9 – 13 December 2024

## Slide 2: Content
<= start here to quickly check how to attend your first 3GPP meeting, in particular slide 13 on how to “Create an EOL account”
The 3GPP project
3GPP Outputs
3GPP Structure
Practical guide to contribute
Supporting information
Annexes

## Slide 3: 3GPP – How the project Works
3GPP works based on
  Participation in face-to-face meetings
  Pro-activity & Contributions – you need written proposals to get attention
  Consenus Driven – “no sustained objections”
Work organization
  Study Items (SI), Work Items (WI)
  Releases with fixed time-lines, which are partially overlapping
  Work Plan (good overview)
3 stages, often overlapping
  Stage 1: Requirements
  Stage 2: Architecture
  Stage 3: Protocols
Companies not individuals participate
  From all over the world
  All major telecommunication companies – operators, vendors, service providers
  Ministries, Regulators, and government agencies actively engaged
  More and more vertical industry representatives bring their work directly to 3GPP
Amazing Track Record
  3GPP started in 1998, since then all major standard projects have been deployed
  Seamless migration from “old” to “new” mobile generations
A new Release every 15 to 24 months
  Allows for reasonably fast standardization & deployment of new technologies
  Strong commitment to time-lines guarantees reliable planning

## Slide 4: 3GPP Membership
The 3GPP Organizational Partners – from Asia, Europe and North America – determine the general policy and strategy of 3GPP.
857 organizations have joined 3GPP via one of these seven OPs.
https://www.3gpp.org/about-us/partners

## Slide 5: 3GPP standards eco-system
Next Generation Projects
5G Projects
Official Liaisons on specification work:
Certification Bodies
3GPP Organizational Partners (OPs)
The 3GPP Organizational Partners (OP) - 7 Standards Organizations - from China, Europe, India, Japan, Korea and the United States.
Participation in 3GPP by companies and organizations becoming Members of one of these 7 OPs.
Inputs on market requirements may come in to the Project via 3GPP Market Representation Partners (MRP).
There is a lot of additional external liaison activity…SDOs, Industry bodies, projects…
450 MHz Alliance, AISG, Bluetooth, Broadband Forum (BBF), CableLabs, International Special Committee on Radio Interference (CISPR), CTIA, Digital Video Broadcasting (DVB) Project, Ecma, International, Expert Group for Emergency Access (EGEA), Eurescom, COST 273, European Radiocommunications Committee (ERC), Fixed Mobile Convergence Alliance (FMCA), GCF, Global TD-LTE Initiative (GTD), GPS Industry Council, GSM Association, HomeRF Forum, IDB Forum, IEEE, Internet Engineering Task Force (IETF), IrDA, International Multimedia Telecomunications Consortium (IMTC), Internet Streaming Media Alliance, ISO-ITU expert group, ISO MPEG / JPEG, ITU-T SG2, JAIN tm (Javatm APIs for Integrated Networks), The Java Community Process (JCP), Liberty Alliance Project, Metro Ethernet Forum (MEF), NENA, NGMN (Next Generation Mobile Networks), oneM2M, OMA (Open Mobile Alliance ), Open Networking Foundation (ONF), Open IPTV Forum, Object Management Group (OMG), PCS Type Certification Review Board (PTCRB), Portable Computer and Communications Association (PCCA), Presence and Availability Management (PAM) Forum, RSA Laboratories, SDR Forum, Sun Micro Systems Inc., Steerco, SyncML Initiative, Trusted Computing Group (TCG), TeleManagement Forum (TMF), TCCA, TIA /TR45, TIA/TR47, ITU, TV-anytime Forum, Voice eXtensible Mark-up Language (VXML) Forum, Wi-Fi Alliance, Wireless Broadband Alliance (WBA), WLAN Smart Card Consortium, Wireless World Research Forum (WWRF), World Wide Web Consortium (W3C)
(Source: extract from https://www.3gpp.org/about-3gpp/15-bodies-with-which-3gpp-has)
796 members
3GPP Market Representation Partners (MRPs)
…

## Slide 6: 3GPP groups
The Technical Specification Groups (TSGs)
  Three TSGs handle the overall planning and coordination within/between TSGs
  They meet in parallel evey quarter, with multi-TSG sessions for coordination of cross-TSG topics
  Approve the work from the WGs
The Working Groups (WGs)
  Each TSG “monitors” a set of WGs
  Sixteen WGs (left) do the technical work
  Submit it to their parent TSG for official approval
Project Coordination Group (PCG)
  Highest decision making body in 3GPP, it meets formally every six months to carry out the final adoption of 3GPP Technical Specification Group work items, to ratify election results and the resources committed to 3GPP (Not shown).
TSG RAN – Radio Access Network
RAN1 – Radio Layer 1 (Physical Layer)
RAN2 – Radio Layer 2 and Radio Layer 3 RRC
RAN3 – UTRAN/E-UTRAN/NG-RAN Architecture and Related Network Interfaces
RAN4 – Radio Performance and Protocol Aspects
RAN5 – Mobile Terminal Conformance Testing
RAN AH1 – TSG RAN ITU-R Ad Hoc
TSG SA – Service and System Aspects
SA WG1 - Services
SA WG2 - System Architecture and Services
SA WG3 - Security and Privacy
SA WG4 - Multimedia Codecs, Systems and Services
SA WG5 - Management, Orchestration and Charging
SA WG6 - Application Enablement and Critical Communication Applications
TSG CT – Core Network and Terminals
CT WG1 - User Equipment - Core Network Protocols
CT WG3 - Interworking with External Networks & Policy and Charging Control
CT WG4 - Core Network Protocols
CT WG6 - Smart Card Application Aspects

## Slide 7: Work Items & meetings
New work is initiated by member companies as Work Items => see slide 19
  Work Items are prioritised and allocated time for discussion during meetings
  3GPP member companies may contribute to any work item
3GPP seeks consensus on all technical matters
  Specific mechanisms are defined if consensus cannot be reached
Work shall be comnpleted by the Release deadline
  Unfinished work is deferred to a later release – or an exception to complete the work slightly later is granted by consensus

## Slide 8: Three-stage approach to Features
time
SA2
Architecture
SA3
Security
SA4
Media
SA5
M&O
SA6
Apps/MC
RAN
Radio Access
CT – Protocols & Coding
Stage 1 Requirements: Overall service description from the user’s standpoint.
Stage 2
Architecture: Overall description of the organization of the network functions to map service requirements into network capabilities.
Stage 3
Protocols: The definition of switching and signalling capabilities needed to support services defined in Stage 1.
SA1
Requirements

## Slide 9: 3GPP Releases and Generations
a.k.a.3G
2000
2002
Rel 99
Rel 4
Rel 5
Rel 6
2004
2006
Rel 7
2008
Rel 8
Rel 9
2010
Rel 10
Rel 11
2012
Rel 12
Rel 13
2014
Rel 16
2016
Rel 14
Rel 15
Rel 21
Rel 23
Rel 22
2018
2020
2022
2024
2026
2028
2030
1999
2001
2003
2005
2007
2009
2011
2013
2015
2017
2019
2021
2023
2025
2027
2029
2031
2033
2032
2034
Release:
Rel 17
Rel 18
Rel 19
Rel 20
?
?
?
Year
Generation:
UMTS
a.k.a.4G

## Slide 10: 3GPP Work Planning
Release-based work
  Releases are major packages of Features (There is a new 3GPP Release ~ every 15 – 24 months)
  A strong commitment to time-lines guarantees reliable planning and time-to-market
  The Work plan is built-up of Work Items that deliver the Features
  Work Items:
    WI may cover more than one specification
    WI may cover more than one TSG or WG
    WI Description document exists for each WI
  Multiple releases are maintained in parallel (see slide 38)
See the 3GPP Work Plan for details of features:
    http://www.3gpp.org/Work-Plan
Chart: Number of specifications (frozen Releases)
| R99 | Rel-4 | Rel-5 | Rel-6 | Rel-7 | Rel-8 | Rel-9 | Rel-10 | Rel-11 | Rel-12 | Rel-13 | Rel-14 | Rel-15 | Rel-16 | Rel-17 | Rel-18
Nbr of specs | 446 | 516 | 582 | 760 | 875 | 1079 | 1117 | 1063 | 1184 | 1245 | 1284 | 1322 | 1500 | 1637 | 1721 | 1817
Chart: Approved CRs per year
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024*
 | 8022 | 8430 | 7964 | 9683 | 9121 | 11887 | 14467 | 14907.3333 | 15649 | 14712.3333 | 17759 | 18204
* Current year extrapolated estimate

## Slide 11: Content
The 3GPP project
3GPP Outputs
3GPP Structure
Practical guide to contribute
  The process
  The outputs
  The inputs
Supporting information
Annexes

## Slide 12: Overview: Inputs and outputs of 3GPP
Inputs: The set of “contributions” or “tdocs”
Outputs: The set of TS/TR, describing the system for a given Release
The 3GPP Process: the meetings & online tools, decision process
The 3GPP Process
(meetings, online tools,…)
Input = Tdocs
Output = Set of TS/TRs

## Slide 13
Get an EOL (ETSI OnLine) account
  This is needed for most of these tools - See https://portal.etsi.org/createaccount#/home
Check which group(s) you like to follow
  E.g. as described on slide 4 or at either: https://www.3gpp.org/about-us/introducing-3gpp https://www.3gpp.org/3gpp-groups
Register to the e-mail reflector of the group(s) you want to follow
  E.g. to register to the SA1 list, send: Subscribe 3GPP_TSG_SA_WG1@LIST.ETSI.ORG To: listserv@list.etsi.org
Process (1/3): First steps in 3GPP

## Slide 14
Most 3GPP operations are made via https://portal.3gpp.org/ .
  Including: registering/contributing to a meeting, getting the 3GPP Specifications, etc.
To use the 3GPP portal, you must log in
  When logged in, your name will appear in the upper-right corner
  If you see only very limited functionality, you are most probably not logged in. When not logged in, the upper-right corner shows as:
Process (2/3): The 3GPP Portal

## Slide 15
An FTP repository: https://ftp.3gpp.org
  It mostly provides: permanent information (e.g. all templates), all the 3GPP Specs, some dynamic information (e.g. the Work Plan) and a dedicated structure per group (WG and TSG).
  In the group-dedicated structure, one folder is made per meeting, allowing to retrieve all info related to that meeting, mostly: the minutes, all tdocs, the invitation to a meeting.
Specific tools, used in certain context and/or only by certain WGs (e.g. Forge, etc.).
  Typically, the online conference calls tools (e.g. GoToMeetingTM, MS TeamsTM, etc.).
    The officials will inform all delegates on the e-mail reflector about any online conference: tool, agenda, registration if needed, etc.
  Be sure to follow the discussions on the reflector and/or contact the WG officials for these tools
Process (3/3): other online tools

## Slide 16: Outputs: the TS/TR
Version R.y.z = Release R
Series | Topic
21 series | Stage 1: Requirements
22 series | Stage 1: Service aspects
23 series | Stage 2 (Technical realization)
24 and 29 series | Stage 3: Network signalling protocols
25 series | 3G Radio: UTRAN; W-CDMA; HSPA
26 series | CODECs
27 series | Data
31 series | SIM, USIM
32 series | OAM&P and Charging
33 series | Security aspects
34 series | UE and (U)SIM test specifications
35 series | Security algorithms except for GERAN
36 series | 4G Radio: LTE; LTE-Advanced
37 series | Multiple Radio technolgies
44 and 45 series | 2G Radio :GSM; EDGE; GPRS
36 series | E-UTRAN
38 series | Radio technologies beyond LTE
4x series | GERAN
55 series | Security algorithms (GERAN specific)

## Slide 17: Inputs: the tdocs
Written by the 3GPP participants (delegates and officials)
22 types of tdoc, including e.g.:
  Change Request
  Work Item Description
  Presentation
  Meeting agenda
  Etc. See full list of tdoc types in the annexes
Each tdoc get a conclusion at the meeting. 18 types of conclusions, including e.g.:
  “agreed”, ”approved”,
  “revised”
  “noted”, “not pursued”, “postponed”
} see next slides

## Slide 18: Tdoc Type – CR (Change Request)
Once a TS/TR is stable, i.e. with R≥3 in the v.R.x.y, changes are still possible (and frequent), but every single change is closely tracked
Every proposal for a modification is called a Change Request (CR). It shall use a specific form as its cover page, shown here ---------------------------->
After this cover page, the rest of the CR reproduces all the TS/TR sections proposed to be modified, and the proposed modifications are shown using MS Word’s revision marks (addition or deletion of text).
The main fields of the form are:
  Release: the impacted Release. A CR is for one Release only. When different Releases are changed, different CRs shall be provided (these are called “mirror CRs”, cat. A)
  Spec# and Version#: indicate which spec the CR is proposed, in which version. For the impacted Release, the latest available version of the TS/TR shall be used as a basis
  CR# and Rev#: a set of sequential numbers provided by the Portal or MCC (unlike for tdoc number, a CR number is kept and the rev# is increased for successive revisions)
  Category: to specify whether the change is for an addition (cat. B), a modification of a feature (cat C), a correction (Cat. F or D), or other reasons (see figure)
  The Reason for change, the summary of change and the consequences if not approved
Practical steps to write a CR are available e.g. in S1-233007

## Slide 19: Tdoc Type - WID/SID (Work Item / Study Item Description)
WID/SID is a form to declare the start a new “area of work”
  It is either:
    A study – in such a case, the WID is referred to as a SID (note that a SID is officially a certain type of WID)
    Normative work – in such a case, the WID is… a WID
  It describes what is intended to be achieved, by when, and how it relates to the rest of the work
  It results in a set of CRs to modify the existing TS/TRs and/or in creating new TS/TRs
  At least four companies commit to provide the related work (the supporting companies)
  As for other tdocs, it shall be approved by a TSG (and possibly previously agreed at a WG)
By “new area of work”, it is meant either:
  New to the entire 3GPP community, or
  New to the WG where the WID/SID is submitted, but equivalent work has already been started in other WG/TSG
The WID/SID template is available at:
  https://ftp.3gpp.org/Information/All_Templates/WID_template.zip
  The template provides guidance text (to be deleted)
  The zip file also contains a PPT providing guidelines for proposing Title & Acronym (telling e.g. that, when work started elsewhere, same name and acronym shall be used as in the other group(s))
All approved WID/SIDs are recorded in the Work Plan

## Slide 20: Content
The 3GPP project
3GPP Outputs
3GPP Structure
Practical guide to contribute
Supporting information
Annexes

## Slide 21: The 3GPP Work Plan and Release descriptions TRs
The Work Plan is a big table available both in MS Project and MS Excel
  The MS Project version offers a Gantt diagram
  The MS Excel version is more universal
It is a powerful tool that keeps track of the past, present and (short-term) future of the entire 3GPP work
  Past: all completed items are kept in the WP, in a structured and organized way
  Present: the progress of all 3GPP WGs/TSGs is recorded, refreshed every quarter to inform the TSGs about overall progress
  Future: the Target Completion Date (together with the actual progress) is a key parameter to set the date of the next milestones, in particular for the freeze of the current Release
See dedicated presentation of the Work Plan in SP-230737
When a Release is “frozen” (i.e. it is roughly completed and no new functionality can be added), all rapporteurs are asked to contribute (via a tdoc of the type “WID summary”), to a TR summarising all what was achieved by 3GPP for this Release.
  This is the series 21.9xx of TRs, where xx is the Release.
  See right colon of the slide “Some useful specs”

## Slide 22: Tools: the 3GPP web site
www.3gpp.org
The 3GPP web site is the web entry point to all 3GPP activities publicly available.
It contains:
General, permanent information
A detailed description of all WG/TSG
A short description of all main technologies developed in 3GPP: 5G Intro, VoLTE, IVAS, etc.
More practical info, in the style of these slides
Latest news and events related to 3GPP technologies

## Slide 23: https://www.3gpp.org/get-involved/

## Slide 24: Links
ETSI guides:
Guide to Writing World Class Standards
Chair’s guide
Rapporteurs' guide
Delegates guide
Member Official Contact's guide
NSOs' guide
Meeting Hosts guide
Use of gender-inclusive language guide
3GPP guides:
About 3GPP https://www.3gpp.org/about-3gpp/about-3gpp
3GPP User (3GU) Portal http://portal.3gpp.org
3GPP FAQ https://www.3gpp.org/about-3gpp/3gpp-faqs
3GPP News http://www.3gpp.org/news-events
3GPP TSG SA – Home http://www.3gpp.org/specifications-groups/sa-plenary/sa-plenary/home
3GPP Working Procedures http://www.3gpp.org/ftp/Information/Working_Procedures/3GPP_WP.pdf
Liaison Statements https://www.3gpp.org/specifications-groups/liaison-statements
3GPP Awards https://www.3gpp.org/about-3gpp/3gpp-award-roll-of-honour

## Slide 25: Some useful specs
The essential rules of 3GPP:
  3GPP Working Procedures http://www.3gpp.org/ftp/Information/Working_Procedures/
  3GPP TR 21.900 Technical Specification Group working methods http://www.3gpp.org/DynaReport/21900.htm
  3GPP TR 21.801 Specification drafting rules http://www.3gpp.org/DynaReport/21801.htm
Summary of Release content:
  Releases overview:
    Release 14 – TR 21.914 http://www.3gpp.org/DynaReport/21914.htm
    Release 15 – TR 21.915 http://www.3gpp.org/DynaReport/21915.htm
    Release 16 – TR 21.916 http://www.3gpp.org/DynaReport/21916.htm
    Release 17 – TR 21.917 http://www.3gpp.org/DynaReport/21917.htm
    Release 18 (draft) – TR 21.918 http://www.3gpp.org/DynaReport/21918.htm
Note to get the TRs: click on the links above, then select the “Version” tab, then click on the top (latest) version number

## Slide 26: Thank You!
Presentation maintained by: Alain Sultan 3GPP Work Plan Coordinator alain.sultan@etsi.org
Please give us your feedback & improvement proposals.
Special Thanks to all contributors to this slide set!