## Slide 1: Discussion on Integrated Sensing and Communication in R19
Xiaomi
SP-221291

## Slide 2: Overview
5G Wireless sensing: 5GS feature providing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g. shape, size, speed, location, distances or relative motion between objects, etc) using NR RF signals and, in some cases, previously defined information available in EPC and/or E-UTRA.
    Concept
    with and without 5G coverage
    licensed and unlicensed spectrum
    5G NR RF, non-RF, and previously defined information available in EPC and/or E-UTRA (no impact to EPC/E-UTRA is assumed)
    UE on board target object or non-UE on board target object
    Scenarios
    Intruder detection, Rainfall monitoring, V2X, Industry 4.0, UAV, smart city, smart home, health monitoring, XR, emergency …
    Use Cases
NOTE: The above concept, scenarios, use cases and definitions are summarized based on 3GPP TR 22.837 v0.3.0.
Object
Sensing receiver
Sensing transmitter
Environment
Sensing receiver: an entity that receives the sensing signal which the sensing service will use in its operation. A sensing receiver is an NR RAN node or a UE. A Sensing receiver can be located in the same or different entity as the Sensing transmitter.
Sensing transmitter: the entity that sends out the sensing signal which the sensing service will use in its operation. A Sensing transmitter is an NR RAN node or a UE. A Sensing transmitter can be located in the same or different entity as the Sensing receiver.

## Slide 3: Potential Architecture Requirements
The 5G system shall be able to authorize Sensing receiver(s) and Sensing transmitter(s) to participate in a sensing service.
Subject to user consent and national or regional regulation, based on operator policy, the 5GS shall support a mechanism to receive uplink sensing measurements from a UE that is authorized to provide uplink sensing measurements to the network.
Subject to user consent, network operator policy and national or regional regulation, the 5GS shall support a mechanism to enable RAN entities and UEs to acquire NR-based sensing measurement data to capture information about the nearby environment.
The 5G system shall be able to support means to select suitable base station(s) to perform sensing, e.g. based on the base station’s location, sensing capability, and the sensing service information requested by trusted third party application.
The 5G system shall be able to support means to enable a base station to transfer sensing measurement data to the core network.
The 5G system shall be able to support means to enable the core network to process sensing measurement data for obtaining sensing results.
The 5G system shall be able to support an authorized UE in the discovery of UEs and RAN entities with the required NR RF sensing capabilities for the sensing service.
Based on operator’s policy, the 5G system shall enable a trusted 3rd party to request the activation of the sensing service with specific KPI requirement, as well as deactivation of the same service.
The 5G system shall allow an authorized UE to discover the precise location of other UEs in proximity that are authorized to provide sensing measurement data from non-RF sensors and sensing results from RF sensors, within a maximum latency.

## Slide 4: Potential QoS Requirements
KPIs on sensing qualitative requirements:
  Sensing service area: a service area where sensing services would solely rely on infrastructures and sensing technologies that can be assumed to be present anywhere where 5G is present. This includes both indoor and outdoor environments.
KPIs on sensing quantitative requirements:
  Accuracy of positioning estimate describes the closeness of the measured sensing result (i.e. position) of the target object to its true position value. It can be further derived into a horizontal sensing accuracy – referring to the sensing result error in a 2D reference or horizontal plane, and into a vertical sensing accuracy – referring to the sensing result error on the vertical axis or altitude.
  Accuracy of velocity estimate describes the closeness of the measured sensing result (i.e. velocity) of the target object’s velocity to its true velocity.
  Confidence level describes the percentage of all the possible measured sensing results that can be expected to include the true sensing result considering the accuracy.
  Sensing Resolution describes the difference of the measured magnitude of two target objects, which is the magnitude needed to distinguish the two target objects.
  Range resolution denotes the minimum difference in distance between target objects to have a measurably different range.
  Velocity resolution denotes the minimum difference in velocity between target objects to have a measurably different velocity.

## Slide 5: Potential Architecture Impacts
3rd Party App
5GC NF
gNB1
UE2
API
Sensing measurement data
Object
Environment
NOTE:
The above architecture is derived based on existing requirements defined in TR 22.837 v0.3.0, more updates may be needed with the progress of the SA1 work
5GC NF in the figure performs sensing measurement data processing, which can be a new NF or an existing NF
Not all gNB or UE participating in sensing have to establish a connection with the 5GC NF performing sensing measurement data processing for providing sensing measurement data
UE1
gNB2

## Slide 6: Current Status in SA/RAN
SA1
  SID FS_Sensing created (SP-220717), expected to be completed @ TSG#100 (Jun 2023)
  Work/Study Item Completion: 65% （S1-223664）
  Definitions, 16 use cases, considerations on confidentiality and integrity, and Consolidated potential KPIs of sensing results defined
RAN WGs
  Discussion papers have been submitted by multiple companies； however, no official discussion has ever happened

## Slide 7: Potential SA2 Impacts
Overall architecture reference model
Sensing Transmitter/Sensing receiver and group management
Service authorization and policy/parameter provisioning for a UE or a gNB
Sensing Transmitter/Sensing receiver device discovery and selection
Sensing service operation procedures
  Coordination between Sensing Transmitter(s) and Sensing receiver(s)
  Sensing measurement data collection and transmission to the 5GC by the gNB or the UE or both
  Sensing measurement data processing
Sensing service activation/deactivation and result reporting to the 3rd party application and to the UE
QoS mechanism and QoS handling
Sensing service continuity
Power saving considerations
Architectural implications to NG-RAN will be coordinated with RAN WGs
Security aspects will be coordinated with SA3
Charging aspects will be coordinated with SA5

## Slide 8: Potential SA3 Impacts
New aspects of security implications for sensing
  Besides UEs supporting 3GPP capability, sensed objects not supporting 3GPP capability can also become the targets of attacks, imposing threats on the owner or authorized user/management of the sensed objects
  More factors wrt sensing (e.g. type of application, environment, resolution, updating frequency) may have influence on security implications
Considerations on security and privacy
  Integrity, confidentiality and availability need to be provided to ensure proper protection
  Permission or consent may be required for sensing operation in both private and public environments
  Sensing information reporting may be restricted, up to the authority of sensing requester
Potential security and privacy requirements
  [P.R.6.1.2-1] 5GS shall limit sensing information to users authorized to receive that information
  [P.R.6.1.2-2] 5GS shall support encryption and integrity protection of sensing results, to protect the data inside the 5G system and when used
  [P.R.6.1.2-3] 5GS shall support appropriate level of sensing for both situations where consent can be obtained and where it cannot
  More to be identified in SA3 by taking architecture impacts into consideration

## Slide 9: Potential SA5 Impacts
Charging related requirements
  [PR 5.2.6-7] The 5G system shall be able to support charging data collection for the sensing services (e.g. considering service type, sensing accuracy, target area, duration) requested by a trusted third party application.
  [PR 5.20.6-4] The 5G system shall be able to support charging for the sensing services (e.g. considering service type, sensing accuracy, target area, duration).
Charging data collection and charging based on service type, sensing accuracy, target area, duration, etc.

## Slide 10: Proposed Way Forward
Integrated Sensing and Communication is proposed as a R19 theme across multiple WGs in SA with RAN dependency
  Whether it is qualified as a theme will be re-evaluated once the definition of Theme is agreed in SA plenary
Work scope in different impacted SA WGs and RAN WGs should be aligned on a high level
Timelines for the studies in the impacted SA WGs can be defined and synchronized along with the establishment of the theme (if qualified)