## Slide 1: Support SEAL LMS with multi-accesses by including Non-seamless WLAN offload
CATT

## Slide 2: Backgrounds:
In the SEAL Location Management architecture ( please refer to TS 23.434 V18.3.0), the UE location information could be obtained over 3GPP access (e.g. NR and LTE) based on the SEAL LM architecture as defined in clause 9 of TS 23.434.
During the work of 5G FLS, it is agreed to use more accesses to get UE location information from more sources to further improve the LCS QoS(e.g. accuracy, latency).
CR#0173 (S6-230973) suggests that the UE location information can be obtained over non-3GPP access connecting to the EPC or 5GC as described in TS 23.402 and TS 23.501.
Using the non-3GPP access without traversing the EPC or 5GC is also a good option to get the UE location information. However, it is not included by the CR#0173. The omission is NOT acceptable for CATT. Thus CATT object the CR#0173 (S6-230973) as is.
Note: “Non-seamless WLAN offload” as defined in clause 5.42 of TS 23.501 and clause 4.1.5 of TS 23.402 is one kind of “non-3GPP access without traversing the EPC or 5GC”.

## Slide 3: Includes the “Non-seamless WLAN offload” into TS 23.434
In order to fulfil and improve the LCS QoS for the 5GFLS WI, the “Non-seamless WLAN offload” (e.g. as defined in clause 5.42 of TS23.501 and clause 4.1.5 of TS 23.402 ) is proposed for the SEAL Location Management architecture of TS 23.434(as described in Figure 3).
Figure1-UE location information is obtained over 3GPP access (e.g. NR,LTE) as described in TS 23.434
Figure2-UE location information is obtained over accesses including the non-3GPP access traversing the EPC or 5GC, which suggested by CR#0173 (S6-230973)
Figure3-UE location information is obtained over accesses including the non-3GPP access without traversing the EPC or 5GC

## Slide 4: Benefit from introducing “Non-seamless WLAN offload”
It is proposed to introduce the “Non-seamless WLAN offload” in SEAL Location Management architecture for the 5GFLS WI into TS 23.434, because it can:
  Provide additional IP path for the UE to increase the network connection reliability and bandwidth.
  Provide low latency than that of using the non-3GPP access traversing 5GC.
  Cost less and easier for deployment for the customers/operators.
  Extend the SEAL LMS to those areas where only “Non-seamless WLAN offload” is available.

## Slide 5: Proposal:
Considering the above analyses, it is proposed to SA to discuss and agree:
  Introduce the “Non-seamless WLAN offload” between the LMC of UE and the SEAL Location Management Server for the 5GFLS into TS 23.434, and
  the corresponding CR#0173 (SP-230305) has above changes.

## Slide 6
Thanks