## Slide 1: Discussion on UE-to-UE Relay Discovery Security
Interdigital

## Slide 2
Contentious Issue:
  TR 33.740 KI#1 conclusion deadlocked
  2 alternative approaches (next slides) with even support
  U2U Relay Discovery security is critical for the U2U Relay feature security
SA3#110bis (April)
  Last meeting for any solution
Other groups impact and dependencies:
  Stage 3 (Discovery procedures)
  Potential impact on SA2
UE-to-UE Relay Discovery Security after SA3#110

## Slide 3
Approach#1 - single key set
  One key set associated with RSC used by End UE and U2U Relay for U2U Relay discovery message protection
Approach#2 - multiple key sets
  One first key set as above plus additional key set used at the End UE for per direct discovery set protection
U2U Relay Discovery Security Alternatives

## Slide 4
Alternatives Comparison
Approach#1 | Approach#2
Reuses existing RSC based discovery security mechanisms | Impacts existing procedures with new mechanism for embedded direct discovery set security within discovery message
Supports both Model A and B | Supports Model B Model A has a pending open issue (next slide)
Security isolation among ProSe services possible via configuration (e.g., dedicated RSC per ProSe service) | Security isolation among ProSe services sharing RSC possible via direct discovery set security material provisioning
Can be used in straightforward deployment options (e.g., dedicated RSC, Public safety use case) | Can be used in more complex deployment options (e.g., mix and match unrelated ProSe services sharing common RSC, Commercial use case)

## Slide 5
Open issues
Support for Model A with Approach #2
  Open Issue of direct discovery set protection freshness at the U2U Relay:
    Protection is time bound (UTC time based) at the announcing End UE
    However, U2U Relay Announcements are in general not synchronized with End UE’s announcements and a connected End UE may not be sending Announcements at all.
    How to ensure freshness of the protected direct discovery sets at the U2U Relay to enable the Relay to Announce End UEs in all cases (e.g., previously discovered, connected)?
Co-existence between Approach #1 and Approach #2:
  Assuming a solution for Model A open issue is agreed, a mechanism for co-existence of both approaches, depending on use cases, will need to be defined.

## Slide 6
Rel-18 timeline considerations and Questions
Based on current Work Plan for FS_5G_ProSe_Ph2
  SA3#110bis-e (April 17-21 , 2023): last meeting for new solutions
  SA3#111 (May 22-26 , 2023): evaluation conclusion, normative work
  i.e., in principle only one meeting left to resolve the identified open issues
Observations:
  Observation#1: Solution for KI#1 is critical for the U2U relay feature security.
  Observation#2: KI#1 has been discussed over several meetings without a clear agreement in sight.
  Observation#3: Approach#1 provides the necessary basic set of discovery security capabilities with minimal impact to existing procedures. Approach#2 introduces additional security capabilities to possibly cover different use case scenarios. Support for both approaches should be beneficial to cover different use cases (see comparison slide).
Proposal:
  SA to provide guidance to SA3 (see draft LS out SP-230312) to progress work based on support for Approach #1, and Approach #2 assuming the resolution of pending open issue (Model A).