## Slide 1: Rel-19 Network Sharing Enhancements SA2 Status
Shabnam Sultana
Moderator for Rel-19 Network Sharing proposals
Ericsson
SP-231052

## Slide 2: Status
Moderated discussions held during July 2023 on this topic indicated very different views on what and how to proceed with any work in Rel-19. The input documents with Moderated discussion status report and draft SI to SA2#158 are as follows: S2-2308408, S2-2308751.
Moderator together with some of the interested companies had offline discussions during SA2#158 to better understand the architectural requirements as well as what is available as baseline network sharing in 5G, both RAN functions like PLMN IDs in cell broadcast, UEs PLMN (re)selection using such information and 5GC support of PLMN IDs as well as 4G MOCN/GWCN aspects.
Some operators discussed/explained the issues and answered questions to clarify what is lacking.
Then discussions moved towards reuse of existing features in 5G such as “deployments topologies with specific SMF Service Area” (i.e. ETSUN) and “Cell in shared NG-RAN broadcast system information include the PLMN-IDs concerning available core network operators in the shared network”, existing Cell (re)selection and UE configuration aspects in 5G, as well as expanding concepts from 4G such as “similar to GWCN” .
Interested companies are asked to investigate further possible solutions which may allow the work to be conducted via TEI19 or WI with solutions described already instead of a study.
Companies plan to re-convene via offline conference calls to progress the discussion and try to resolve towards an agreeable way forward during Q4, 2023 in SA2. As such, there is no input SI proposal to SA#101 on this topic.
The next slides were the outcome of unofficial/informal discussions that took place during SA2#158 and included for information purposes only.

## Slide 3: Rel-19 Network Sharing offline discussion summary
Moderator- Shabnam Sultana
August 23, 2023
Ericsson

## Slide 4
Participants
China Unicom, CableLabs, Comcast, CMCC, CATT, CISCO, Ericsson, Huawei, Nokia, Qualcomm, ZTE

## Slide 5
Discussed two documents related to background, scenarios, use cases and potential requirements:
China Unicom document S2-2308592
Comcast document S2-2308784
Question on co-existence between MOCN and GWCN a la 5G (or Indirect network sharing), clarified CU does not have exact same requirement but Comcast does, some discussion on the meaning of co-existence (NGRAN supporting both and operator deploying both), seems expectation it is needed.
CU Remark: “in 5G, we have the scenario of the co-existence between 5G MOCN and 5G indirect network sharing (this name may be changed to extended GWCN in 5G or another). So I think the meaning of co-existence need to clarify to avoid ambiguity.” (Mod comment: little unclear what is meant so further clarification needed).
Discussed as presented by CU, the requirements and discussed the scenarios and how it related to overall 5GS. CU clarified requirements including avoiding to maintain a large number of interfaces between Hosting Operator’s Shared NR and Participating Operator’s core network (e.g. N2/N3 interfaces).
Discussion

## Slide 6
Open discussion on the similarities of “a la GWCN” and the key difference between 4G and 5G about PLMNs, clarified that in 5G multiple PLMN IDs and their service support aspects are broadcast where 4G it was an added feature. Also, there is no “supporting and non-supporting UE” concept in 5G.
23.501, 5.18.3: “A UE that has a subscription to one of the sharing core network operators shall be able to select this core network operator while within the coverage area of the shared network and to receive subscribed services from that core network operator.
Each cell in shared NG-RAN shall in the broadcast system information include the PLMN-IDs concerning available core network operators in the shared network.
When a UE performs an Initial Registration to a network, one of available PLMNs shall be selected to serve the UE. UE uses all the received broadcast PLMN-IDs in its PLMN (re)selection processes which is specified in TS 23.122 [17]. UE shall inform the NG-RAN of the selected PLMN so that the NG-RAN can route correctly. The NG-RAN shall inform the core network of the selected PLMN.
As per any network, after Initial Registration to the shared network and while remaining served by the shared network, the network selection procedures specified in TS 23.122 [17] may cause the UE to perform a reselection of another available PLMN.
UE uses all of the received broadcast PLMN-IDs in its cell and PLMN (re)selection processes.”
Companies discussed then the potential use of “GWCN like” solution to address the control plane based network sharing as a way forward.
Initial quick analysis seems to indicate it will be sufficient to go in that direction, but further checking is needed for any additional charging requirements (e.g. CU considers charging aspect as an operator, the charging and accounting crossing PLMNs need to be supported flexibly in this scenario).
Companies are encouraged to further investigate and see if the proposed solution works to satisfy the requirements.
Discussed if SBA based approach and handling of PLMN ID would satisfy or need to add additional parameter in some interfaces/SBA. also )please see slide later with Vodafone proposed potential update)
Discussion

## Slide 7
Comcast also explained the use cases and need for user plane diversion that is needed.
It was then discussed if ETSUN (I-SMF/I-UPF) selection criteria is sufficient to address the specific CN NF selection and initial impression is that it should be possible to make it work.
Investigate potential reuse of feature in TS 23.501 clause 5.34 “Support of deployments topologies with specific SMF Service Areas” in this context where operator can deploy certain configuration enabling the deployment requirements.
May need to check if some form of informative Annex explaining such option can be documented, if it can be made to work.
We also discussed SNPN aspects and recommendation is that we do not include this for Rel-19 as it has other complexity and need further discussion/understanding.
Discussion

## Slide 8
Discussion
CMCC indicated the following aspects they consider important to maintain:
1. Considering the system impact and requirement, we don't think handover between the serving PLMN and home PLMN is necessary, as well as AMF to AMF interface.
2. In case there is no roaming agreement, the roaming UE can not access to the serving 5GC network, otherwise, the existing roaming mechanism can be re-used if there is roaming agreement. Therefore, this original WT#3 can be removed.
3. For the UE in the serving PLMN, the logo of the serving PLMN shall be displaced in the UE.

## Slide 9
Investigate use of GWCN approach for 5GS and if it can be made to work.
Investigate use of “deployments topologies with specific SMF Service Areas” to address user plane network sharing.
If requirements are fulfilled with such approach, identify potential stage 2 impacts on SA2 specifications.
Agreement among the participants to limit scope to NR with 5GC.
Agreement/understanding is that with this approach no additional UE impacts foreseen.
Current understanding is that there are no impacts to NG-RAN, existing AMF selection would work as is, but companies will further check if this can be confirmed.
Potential Solution reusing existing available features

## Slide 10
Vodafone (Chris) was not present, but the following he proposed via NWM discussion of potential enhancement of “GWCN” like solution for 5G to address the requirements.
Vodafone: what is missing from Release 15 is the inclusion of the ”selected PLMN ID” in the signalling from the AMF to the vSMF (and perhaps to the vUPF?) and hSMF. This information is needed for CDR generation and inter-operator accounting (in both VPLMN and HPLMN) in the vSMF, and perhaps for functionality in the vUPF. However, adding this IE would seem to be TEI-19.
Potential Solution reusing existing available features

## Slide 11
Companies to investigate the solutions proposal described in previous slides.
Discuss offline further the outcome as well as possibility of having:
  a TEI19 (if solutions can be developed as suggested),
  directly a WI with proposed solution description for Rel-19, or
  define a new SI scope for discussion during Q4.
Plan to set up offline discussions with interested parties.
Next Steps

## Slide 12: Summary