## Slide 1: Proposed Way Forward related to SBA over N2
SP-231064
Agenda: 3.6

## Slide 2: Agenda
Considerations for Supporting SBA over N2 in SA2 Rel-19 SIs
Proposed Way Forward

## Slide 3: Considerations for Supporting SBA over N2 in SA2 Rel-19 SIs
Existing 5G Core Intra SBA between NFs
Consideration of “new” SBA between RAN & 5G Core
During SA2#158, there were intense discussions on the considerations to include the possible support of SBA over N2 in some Rel-19 SIDs.
  Companies not in favour of supporting SBA over N2 in 5G-Adv insist on including a NOTE to explicitly exclude such possible consideration in the Rel-19 SID
  Proponents for supporting SBA over N2 insist on excluding such a NOTE
  Considerations/Observations:
SBA support over N2 interface impacts BOTH RAN and 5G Core
  Requires RAN3 support in RAN and CANNOT solely be based on SA2 decision
SBA support over N2 interface is a system-wide feature
  Requires a generic framework to support SBA over N2
  Shall NOT be specific for a particular SA2 feature(s)

## Slide 4: Considerations for Supporting SBA over N2 in SA2 Rel-19 SIs
SBA over N2 is a system-wide feature that impacts BOTH RAN and 5G Core, hence,
  SBA over N2 SHALL NOT be defined specifically for a particular SA2 feature
    A generic architecture framework shall firstly be considered for supporting SBA over N2 before any 5G feature has its services defined over such interface
    Previously proposed Rel-18 SID, S2-2105493 (see attached), for supporting SBA over N2 estimates that 8 TUs are required just for the Study Phase. In fact, it could require significantly higher # of TUs to redefine system procedures.
  Enabling SBA over N2 would require agreement/commitment from RAN3 to define support for such interface/protocol framework in their Rel-19 package
  Given the fundamental changes to the communication between RAN and 5G Core for supporting SBA over N2, the impacts to the Rel-19 gNB as well as to the 5G Core would need to be assessed by RAN and SA2 for Rel-19 overall system impacts.
  Introducing SBA over N2 would require a holistic system wide architectural update to fully leverage the benefits of N2 SBI as all the system procedures will need to be re-designed due to SBI for N2. It will also drastically destabilize the specification for 5G System as all the procedures would need to be updated. Even if the SBA objective is targeted for only specific new feature(s), the overall system impacts remain the same.
SBA over N2 for specific new functionality and/or new feature imply the need to introduce a second stack on gNB towards the core network creating extra implementation (including security, OAM) and inter-operability testing efforts for specific features in a late stage of 5GA.
Risk to fragment the market for 5G SA and further slowdown adoption of 5G SA.

## Slide 5: Proposed Way Forward
Two possible options to be considered for Way Forward:
  OPTION-1: SA provides guidance to SA2 to exclude the support of SBA over N2 in Rel-19 due to fundamental impacts towards 5G system
  OPTION-2: SA sends an LS to RAN and RAN3 to ask if support of SBA over N2 is considered as part of RAN Rel-19 package discussions and SA wait for RAN / RAN3 answer before the final decision is made in SA. Until decision is made in SA, no discussion shall happen in SA2 regarding support of SBA over N2.
    If RAN/RAN3 do not respond SA’s LS in-time by SA#102 or RAN Rel-19 package does not include SBA as part of the scope, SA should interpret that SBA shall not be included in any SA2 Rel-19 SIDs.
  We ask for a decision on SA level so we don’t need to go back to this issue again in Rel-19 SID discussions.