## Slide 1: Discussion on Rel-19 SA1 Dualsteer
Huawei, HiSilicon, MediaTek Inc.

## Slide 2: Scope of the study (from TR22.841)
1 Scope
The scope of this TR is to document use cases, gap analysis and potential service requirements related to 5GS support of enhanced mechanisms for steering, splitting and switching of user data, pertaining to a UE data session, across two 3GPP networks. The following scenarios are covered, where only one single PLMN subscription is assumed:
Single PLMN;
PLMN and NPN;
two PLMNs.
The two 3GPP networks may use same or different RAT, i.e. NR plus NR or E-UTRA, where NR RAT can be terrestrial or satellite NR access (including different staellite orbits, e.g., GEO/MEO/LEO).
For the PLMN plus PLMN / NPN scenarios, the two networks can be managed by the same operator or by different operators (assumed to have a business agreement among them). In both cases, it is assumed that a single PLMN subscription is used to access both networks (including the NPN).
Simultaneous connectivity over two 3GPP networks presumes UE support of proper capabilities (e.g., dual radio).
It is assumed that there are no impacts to normal inter-PLMN roaming scenarios.
Dual subscription scenarios are not in scope of this TR.
Regarding potential new requirements, one general consideration is that they assume 5GS functionalities that do not introduce RAN impacts. However, as it is clarified in subsequent slides, it is impossible to achieve them without involving RAN (e.g. dual radio requires RAN analysis).

## Slide 3: Definition from SA1 Dualsteer study
Traffic steering: the procedure that selects an access network for a new data flow and transfers the traffic of this data flow over the selected access network. This can apply to two 3GPP access networks, when available.
Traffic splitting: the procedure that splits the traffic of a data flow across multiple access networks. When traffic splitting is applied to a data flow, some traffic of the data flow is transferred via one access and some other traffic of the same data flow is transferred via another access. This can apply to two 3GPP access networks, when available.
Traffic switching: the procedure that moves all traffic of an ongoing data flow from one access network to another access network in a way that maintains the continuity of the data flow. This can apply to two 3GPP access networks, when available.
NOTE: Traffic switching can also apply to multiple/all UE data flows.

## Slide 4: Use cases captured in TR22.841
UC1: Use case on dual 5G satellite access in maritime scenario
UC2: Use case on Inter PLMN Mobility Scenario
UC3: Use case on Inter-PLMN or PLMN-SNPN scenario
UC4: Use case on Inter-PLMN scenario - TN and NTN
UC5: Use case on NTN-based dual 3GPP access
UC6: Use case on UE using Terrestrial and Satellite Access
UC7: Use case on intra-PLMN scenario for XR gaming
UC8: Use Case on intra-PLMN traffic redundancy
UC9: Use case on dual steering through Satellite and UAV
UC10: Use case on NTN and TN Inter-PLMN Multi-access in a Maritime scenario
UC11: Use case on inter PLMN scenario for XR service
UC12: Use case on different VPLMN scenarios
UC13: Use case on Interworking with non-3GPP access
UC14: Use Case on Inter-PLMN scenario - TN and multiple NTN
UC15: Use Case on access to local NPN services (inter NPN – PLMN scenario)
UC16: Use Case on set of devices accessing local NPN services (inter NPN – PLMN scenario)
UC17: Use Case on Vehicle IoT devices steering via NTN and TN
UC18: Use Case on UAV UE connecting to 3GPP TN and NTN access networks

## Slide 5: Categorization of the use cases in TR22.841
 | TN-TN | TN-NTN | NTN-NTN
Intra-PLMN | UC7/UC8/UC12 | UC5/UC9 | UC1/UC5
Inter-PLMN | UC2/UC3/UC11/UC12 | UC4/UC5/UC6/UC10/UC14/UC17/UC18 | UC10
PLMN-NPN | UC3/UC15/UC16/UC12 | N/A | N/A
UC13 Use case on Interworking with non-3GPP access can be considered later, as it adds non-3GPP access on top of dual-3GPP access
Group the UCs from TR22.841 for analysis in this contribution
UC Group 1: Intra-PLMN, TN-TN
UC Group 2: Inter-PLMN, TN-TN
UC Group 3: PLMN-NPN, TN-TN
UC Group 4: Intra-PLMN, TN-NTN
UC Group 5: Inter-PLMN, TN-NTN
UC Group 6: Intra-PLMN, NTN-NTN
UC Group 7: Inter-PLMN, NTN-NTN

## Slide 6: Functionalities already supported in existing specifications
Intra-PLMN IDLE/CONNECTED mobility
Inter-PLMN IDLE/CONNECTED mobility
Inter-PLMN roaming
EN-DC
NR-NR CA
access to PLMN services via Stand-alone Non-Public Network and access to Stand-alone Non Public Network services via PLMN [23.501 Annex D.3]

## Slide 7: Analysis on UC Group 1 Intra-PLMN, TN-TN
Examples of the use cases (TR 22.841)
NR+NR, Intra PLMN
NR+LTE, Intra PLMN
Potential performance | NR+NR, intra PLMN NR+LTE, intra PLMN | NR-NR CA EN-DC
Efficient radio resource utilization | X Potential interference and performance degrade | √ Considering spectral efficiency, achievable data rate etc.
Efficient utilization of terminal AS capabilities | X | √ Terminal capabilities are aware and coordinated by RAN
Traffic routing policy | X Static, low accuracy No sufficient RAN information | √ Dynamic, high accuracy Considering cell load, QoS etc.
Additional specification impacts and UE/system complexity | X Dual cells (re)selection* Dual RRC connection* Dual registration for MM, SM | √ none
* Requiring RAN impacts, which violates the “no RAN impact” assumption made for this study
  Observation: existing NR-NR CA/EN-DC can well support the targets of the use cases with superior performance.
  Conclusion: No new requirement is needed for UC Group 1.
Target of the use cases: data rate aggregation, duplication, etc.
NR+NR CA/EN-DC can already support the targeted use cases
Fig. 5.8.2 User data routing: single and dual 3GPP access connectivity

## Slide 8: Analysis on UC Group 2 Inter-PLMN, TN-TN
Examples of the use cases (TR 22.841)
VPLMN + VPLMN
VPLMN + HPLMN
Target of the use cases: data rate aggregation, duplication, etc.
NR+NR CA/EN-DC can already support the targeted use cases
  Observation 1: existing NR-NR CA/EN-DC can well support the use case with superior performance Observation 2: no clear motivation for the UE to select two PLMNs at the same time. It would introduce a dramatic change to UE arch. and assumptions of 5GS late in the 5G lifecycle.
  Conclusion: No new requirement is needed for UC Group 2.
Potential performance | NR+NR, intra PLMN NR+LTE, intra PLMN | NR-NR CA EN-DC
Efficient radio resource utilization | X Potential interference and performance degrade | √ Considering spectral efficiency, achievable data rate etc.
Efficient utilization of terminal AS capabilities | X | √ Terminal capabilities are aware and coordinated by RAN
Traffic routing policy | X Static, low accuracy No sufficient RAN information | √ Dynamic, high accuracy Considering cell load, QoS etc.
Additional specification impacts and UE/system complexity | X Dual cells (re)selection* Dual RRC connection* Dual registration for MM, SM | √ none
Additional deployment complexity | Coordination among 2~3 operators** | none
Requiring RAN impacts, which violates the “no RAN impact” assumption made for this study
** Such business agreements among operators may not be practical
Fig. 5.12.3 Inter-VPLMN scenario, with home-routed traffic
UC2： HPLMN's user data is transmitted additionally via another PLMN (e.g. VPLMN) to improve throughput, using NR in both networks.

## Slide 9: Analysis on UC Group 3 PLMN-NPN, TN-TN
NR (PLMN) + NR (SNPN)
NR (PLMN) + NR (PNI-NPN)
Examples of the use cases
Claimed target of the use cases: increase network throughput by simultaneous transmission/connection via PLMN+NPN
Scenarios | Violate the NPN principle | Performance | UE and system complexity
PLMN+SNPN | UP & SMF interconnection between SNPN and PLMN * | Inefficient radio resource utilization | Dual cells (re)selection*** Dual RRC connections*** Dual registration for MM, SM
PLMN+PNI-NPN | using both PLMN and PNI-NPN slices at the same time ** | Inefficient radio resource utilization | Dual cells (re)selection*** Dual RRC connections*** Dual registration for MM, SM
  Conclusion: No new requirements are needed for UC Group 3, which violate the NPN principles.
* Violates the SNPN principle and requires interaction with network functions (e.g. UPF/SMF) provided by PLMN
** Violates the Slice principle and using two slices for the same service
***Requiring RAN impacts, which violates the “no RAN impact” assumption made for this study
Fig. 5.3-3 Step-2: scenario with Alice’s data session using dual-3GPP access connectivity
Figure 5.15.2. AGV-A#1

## Slide 10: Analysis on UC Group 4 Intra-PLMN, TN-NTN & UC Group 5 Inter-PLMN, TN-NTN
Figure 5.5.1b: Multi connectivity involving transparent NTN-based NG-RAN and cellular NG-RAN (same PLMN)
Examples of the use cases (TR 22.841)
Claimed target of the use cases:
  Improve QoS (e.g. more throughput, less PER)
  Obtain the continuous and reliable service with the minimum impact of terrestrial access network unavailability
Concurrent transmission over NTN and TN is not a strong requirement
TN throughput is much larger than NTN throughput  concurrent transmission over NTN and TN does not provide meaningful gain. Any Added throughput from NTN leg will be negligible.
Inter-PLMN case, would introduce a dramatic change to UE arch. and assumptions of 5GS late in the 5G lifecycle.
Traffic switching between NTN and TN
Could be useful when TN becomes unavailable
Need to assess the additional benefits of traffic switching between NTN and TN over existing mechanism, e.g. inter-PLMN/intra-PLMN handover.
  Conclusion: No new requirement for concurrent transmission over NTN and TN. Other cases require future gap analysis over existing mechanism before any decision.
Figure 5.5.1a: Multi connectivity involving transparent NTN-based NG-RAN and cellular NG-RAN different PLMN)

## Slide 11: Analysis on UC Group 6 Intra-PLMN & Group 7 Inter-PLMN, NTN-NTN
Figure 5.1.3-2: Traffic switching due to loss of connection with LEO satellite access network
Figure 5.1.3-1: Dual 5G satellite access for autonomous ship operations
Claimed target of the use cases:
  Delay sensitive service to be switched to another NTN connection（GEO）due to loss of one NTN connection（LEO）.
  Delay-tolerant applications is aggregated via both LEO and GEO satellite links.
Increasing throughput is not a strong requirement
Worst-link latency dominates overall performance: Significant latency difference over LEO and GEO(~30ms for LEO and 280ms for GEO)
There is no justification for cross GSO/NGSO constellation.
Switching between two NTNs
Need to assess the additional benefits of traffic switching between NTN and NTN over existing mechanism, e.g. inter-PLMN handover.
  Conclusion: No new requirement for concurrent transmission over NTN and NTN. Other cases require future gap analysis over existing mechanism before any decision.
Examples of the use cases (TR 22.841)

## Slide 12: Summary
Current SA1 situation:
  Working agreement declared in SA1#103, which requires 5G system to support simultaneously all three mechanisms (i.e. switching, steering, splitting) for all scenarios
Based on analysis in previous slides, it is concluded that having requirements for all scenarios is not justified.
Proposed way forward:
Not to confirm the working agreement
SA1 to continue the discussion on Rel-19 Dual Steer, aiming to find a workable compromise.

## Slide 13
Thank you!