## Slide 1: Discussion on NPN support for ProSe for release 19
Philips International B.V., Siemens AG

## Slide 2: Introduction
Based on the SA Plenary Release 19 Workshop in June a list of topics was identified to improve ProSe, one of these topics was “NPN Enhancements for ProSe”.
During SA2 Moderated E-mail discussions 7 companies indicated support or conditional support for “NPN Enhancements for ProSe”, but at least 5 companies requested additional information to clarify the scope of this topic before they could indicate support. Hence this topics was not yet included by the moderator in the resulting draft release 19 SID for ProSe.
This presentation aims to clarify this topic and address the comments.
It is important to consider this topic for inclusion in release 19, given that without NPN support deployment of ProSe (e.g. in factories) is hampered, and important SA1 use cases identified for ProSe (e.g. collaborating mobile robots) cannot be supported. It also affects other programs, such as Ranging, i.e. ranging cannot be deployed in NPNs unless NPN support for ProSe is added.

## Slide 3: What needs to be studied and specified?
As indicated in 23.501 clauses 5.30.2.0 and 5.30.3.1, ProSe is currently not supported for NPNs. The main purpose is therefore to study and identify the gaps and enhancement to support the ProSe service in NPNs.
Detailed work would include:
  Architecture and procedure updates to enable UEs to access NPNs via a ProSe relay, including studying and specifying how to authorize and identify Relay Service Codes for UEs accessing NPNs.
  Study potential updates to architecture and procedures for support of direct device communication in NPNs.
  Study how to convey NPN related identifiers, such as NID, CAG ID, GIN during ProSe discovery, to aid in selection of ProSe peer UEs or relay UEs that match the network selection criteria for NPNs.
  Study whether and how CAG is used for access control for ProSe UEs.
  Study whether and how authentication/authorization procedures and key management functions need to be updated to support 3rd party credential holders and key generating EAP methods (e.g. EAP-TLS).
  Study whether and how a UE can access an Onboarding Standalone Non-Public Network (ON-SNPN) via ProSe relay for UE onboarding.
Other important topics related to NPN support, such as support for URLLC/TSC need to be discussed as well, but can be discussed as part of the URLLC/TSC release 19 study item proposal.

## Slide 4: Conclusion
Lack of understanding on the topic of NPN enhancements for ProSe led to topic not yet being included by the moderator for release 19 study.
Several enhancements needed to be able to use and deploy ProSe in NPNs.
Important to include this topic in release 19 study for ProSe, otherwise it hampers deployment of ProSe, does not address important use cases, and also affects other features such as Ranging.
Proposal for endorsement:
Add “NPN support for ProSe” with the clarifications mentioned on slide 3 to the draft release 19 SID for ProSe, as input for further discussion on the SID during Q4.