## Slide 1: MASQUE for Enhanced Traffic Management
Ericsson, Apple
Agenda item 3.5

## Slide 2: MASQUE enabled 5GS Benefits this proposal brings
Applying Traffic differentiation within a PDU Session is becoming a challenge:
  New Transport protocols like QUIC are being widely adopted
  Privacy concern drives reduced traffic visibility: encrypted Layer 4 (QUIC), Layer 3 impacted by relay proxy deployments, encrypted signaling (DNS, TLS handshakes…)
MNO may be able to address both End-user concerns for privacy and its own Traffic differentiation needs by deploying a (MASQUE based) Relay service in 5GC:
  MASQUE can be used to exchange information between the UE and mobile network.
  Integrated in UPF (Policy Enforcement Point), MASQUE conveyed information can be used to assist Traffic differentiation for:
    Differentiated Traffic Management (e.g. QoS, charging…)
    Differentiated Traffic Data Collection (e.g. for Analytics)
  At the same time, the 5GS maintains and improves end-user privacy
Application
Server
Application
Application
MASQUE proxy
Application
Access
network
Internet
UE
UPF
SMF
PCF
NEF

## Slide 3: MASQUE enabled 5GS Benefits this proposal brings
  In UPF, Traffic differentiation can be based on UE provided guaranteed information:
  The information exchanged is controlled (acceptable for user to share), correct and useful. It is not subject to changes in communication patterns and in how traffic flows are observed by the network.
  (This is compared to information from passive listeners in UPF, which is conditioned to traffic changes and increasing encryption)
An opportunity for new use cases and for MNOs to establish new and well-defined business relationships

## Slide 4: Use Cases - Overview
Network Collaboration
  Policy enforcement like zero rating, subscription awareness
  QoS signalling and differentiation
  Data Collection
Additional privacy
  Data used for interaction is only exposed to participating nodes.
  Hiding of client IP.
  App-exposure data can be customized to maximize utility and minimize privacy impact.
Traffic Monitoring
  Accurate loss and latency measurements
  Better troubleshooting
  SLA Assurance
Notes: DEMO:
- Realtime visualization of loss, RTT & CWND – green
Video should show the non-impaired version and we can backup with retransmission metrics – purple
  a button to switch between datagram and streaming – when datagram is used the video impairment should be visible and streaming should solve
show the client is following the policy and consented by the server
  Should be able to show high Quality video even when there is loss
A button to change the TC rules.

## Slide 5: Network Collaboration for Traffic Management and Reporting
2. UE selects MASQUE proxy
4. UPF Differentiates traffic assisted by UE-provided information: executes rules and exposes data
1. MNO provides to UE:
MASQUE Proxy information
UE Rules for In-band Information (e.g. Traffic Category (as in URSP TD))
6. Example UC: NWDAF can perform analytics (e.g. URSP assistance)
MASQUE is used to convey information between the UE and the network (UPF) that can be used for traffic differentiation.
Information is:
Explicit
Correct
Stable (not subject to changes in communication patterns).
Information needs to be acceptable both for user privacy and network operation.
Application
Server
Application
Access
network
Internet
Application
MASQUE Proxy
Application
UE
UPF
NWDAF
3. UE provides the requested info to UPF (e.g. Traffic Category)
5. UPF relays traffic with respect to user privacy (encryption E2E)

## Slide 6: Current MASQUE Examples
3GPP Release 18 ATSSS
Support for MP-QUIC and MASQUE was introduced to enable packet splitting of UDP flows across 3GPP and non-3GPP access
Could also support general IP flows but this was not part of rel-18 (could be future extension)
Relay Service for Privacy (currently deployed in the field)
It consists of two QUIC/MASQUE proxies (relays):
  Ingress proxy: assigns the user an anonymous IP address (maps to their region but not their actual location).
  Egress proxy: decrypts the web address they want to visit and forwards them to their destination.
This separation of information protects the user’s privacy. No single entity can identify both who a user is and which sites they visit.
Application
Server
Application
Application
MASQUE
Ingress proxy
Application
MASQUE Egress proxy
Client
Non-3GPP
AN
RAN
UPF
SMF
N3IWF
Multi-access PDU Session
MASQUE / MP-QUIC client
MASQUE / MP-QUIC proxy
W-AGF
MN

## Slide 7: Enhanced E2E Privacy by dual proxy deployment
Dual proxy deployments intend to further enhance user privacy: they add privacy for user to both network provider and Application Server.
This is an opportunity for MNOs to monetize Privacy enhancing functionality.
A MASQUE proxy in UPF can act as ingress proxy. Egress proxy is provided by a 3p.
UPF has no visibility of the traffic destination, but MASQUE can be used for UE to assist traffic differentiation.
Solutions to convey information between UE and UPF may be the same in single and dual proxy deployments.

## Slide 8: Traffic Monitoring
Proxy Enabled Measurements
The QUIC connection on the access leg provides information on packet loss and round-trip times due to the use of packet numbers and acknowledgements.
Proxy in UPF becomes a source of probing data for various use cases.
Additional data telemetry data could be conveyed using Masque extensions.
Application
Server
Application
Access
network
Internet
Application
MASQUE Proxy
Application
Client
UPF

## Slide 9: SID Summary
Main objective of this study is to study the potential of MASQUE technology to enhance 5GC Traffic management capabilities.
This study determines whether and how MASQUE capabilities in the 5GC user plane:
  Can benefit the 5GS Traffic management by explicit information exchange on fully encrypted traffic. The study identifies the relevant information that would be exposed.
  Can benefit other 5GC functions like reporting of user plane data as input to analytics or to monitor the correct URSP enforcement in the UE.
  Need to be advertised towards the UE, and which information the UE needs to be provisioned with if any.
  Can integrate in the PCC Framework, and which enhancements are required the PCC framework, if any.
The Study evaluates whether ATSSS MASQUE proxy in UPF should be generalized in Rel-19.
Any solutions consider user plane transmission efficiency and are not be limited to work with QUIC traffic only or specific MASQUE deployments (i.e. one or two-proxies).
Proposal is to leave HR roaming scenarios out of scope in this release.

## Slide 10: Further details

## Slide 11: MASQUE Technology Principles
An HTTP-based tunnel is established between a client and a relay (aka MASQUE server) which receives traffic from the client through the tunnel and forwards it to a target server or another relay. While earlier versions of HTTP are supported it is mostly intended to be used with HTTP3 over QUIC.​
The MASQUE server provides a proxy service that forwards multiple flows inside an HTTP3 connection:​
  HTTP3 settings indicate support for HTTP datagrams. Extended HTTP CONNECT method with new upgrade tokens indicate UDP or IP proxying. ​
  The HTTP-based CAPSULE protocol allows for tunnel configuration messages and stream-based encoding of encapsulated datagrams.​
  Multiple encapsulated connections: End-to-end security is unaltered by proxy​
​
​
​
​Client establishes HTTP3 tunnel connection to MASQUE proxy (yellow)
Client establishes HTTP3 tunnel connection to MASQUE proxy (yellow)​
This technology allows endpoints and in-network relays to exchange information explicitly​
Client
MASQUE
Server
Target
Server
(or second relay)
HTTP3 / QUIC tunnel
End-to-end
connection

## Slide 12: Optimized Delivery Without Double Encryption (for QUIC)
Client / UE
@UPF
Server
MASQUE Proxy
Client establishes a HTTP3 / MASQUE connection with the UPF masque proxy.
Initial connection setup messages between client and server are encapsulated in the Masque connection.
Subsequent packets are sent outside the crypto envelope of the Masque connection. The proxy identifies the flows associated with a tunnel by use of QUIC connection IDs.
The connection Ids to be used are exchanged through the control channel between client and proxy.
Each endpoint can unilaterally decide whether a packet should be encapsulated or sent outside the tunnel.
Use cases that do not require full tunnelling can benefit since a layer of encryption and encapsulation is removed.
Currently specified in: draft-pauly-masque-quic-proxy-06 - QUIC-Aware Proxying Using HTTP (ietf.org)
  The draft is likely to be adopted by the MASQUE working group in IETF soon.
  The Masque charter has been updated and it does explicitly reference this type of solution as a goal for the WG.
Control
Encapsulated datagrams
Forwarded datagrams
Target server
(or another MASQUE relay)

## Slide 13: MASQUE Specifications
IETF MASQUE (Multiplexed Application Substrate over QUIC Encryption) WG was established in June 2020.​
It was Chartered to specify secure proxy protocols and mechanisms based on QUIC.
Main deliverables include so far:​
RFC 9297 - HTTP Datagrams and the Capsule Protocol (ietf.org)​
Defines the concept of datagrams for HTTP. Primarily to be used for HTTP3 over QUIC with support for the datagrams. ​
RFC 9298 - Proxying UDP in HTTP (ietf.org) ​
Extends HTTP with support for UDP proxying. It uses HTTP datagrams​
Work ongoing and soon to become RFCs as well​
draft-ietf-masque-connect-ip-01 - IP Proxying Support for HTTP ​
Extends HTTP with support for IP proxying​
The MASQUE WG has been rechartered to focus on extensions to the base specifications. This allows the WG to work on extensions such as QUIC aware proxying and adding sequence numbers to HTTP datagrams (which will be used by ATSSS).