## Slide 1: Study on User Plane Redundancy
Ericsson
Agenda item 3.5

## Slide 2: Background
In the SA2 moderated discussion (S2-2309919), many companies indicated support for Rel-19 Study on Redundancy mechanisms.
  Replication and elimination mechanism
  Both Ethernet and IP
  For single UE (dual registration), or device with dual UEs.
  Exposure framework

## Slide 3: Need for flexible framework
Diverse market needs and future extension requirements call for flexible framework
  Replication and elimination endpoints may or may not be co-located with a 3GPP system entity.
  Controller for the replication and elimination may be within the 3GPP system, or be outside of the 3GPP system.
  Should be compatible with state-of-the-art IETF and IEEE solutions.

## Slide 4: State-of-the-art IP redundancy solution: DetNet service sub-layer
Redundant paths with packet replication and elimination
  Failure of one path does not affect e2e traffic
Redundancy e2e or for a segment
3GPP support for redundant paths:
  Mutiple UEs (23.501 Annex F)
  Dual connectivity (23.501 clause 5.33.2.1)
  Redundancy handling for replication and elimination not part of 3GPP spec.
IETF solution for DetNet IP user plane service sub-layer now mature
  draft-ietf-detnet-mpls-over-ip-preof expected to become RFC in rel-19 timeframe
  Uses MPLS headers for encapsulation without requiring MPLS support.
DetNet controller
PREOF
PREOF
Host1
Host2
PREOF: Packet Replication, Elimination and Ordering Function (DetNet)

## Slide 5: Redundancy scenario - Example 1
UE2
UE1
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS
Redundant 5GS path using 2 UEs
DetNet controller provided in operator domain
Operator self-contained solution for redundancy as a service

## Slide 6: Redundancy scenario - Example 2
Redundant 5GS path using dual connectivity (single UE)
DetNet controller provided in operator domain
Operator self-contained solution for redundancy as a service
UE
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS

## Slide 7: Redundancy scenario - Example 3
Redundant 5GS path using 2 UEs
External DetNet controller
Redundancy can be extended e2e, PREOF possible outside of 5GS
UE2
UE1
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS

## Slide 8: Summary
Ericsson supports Rel-19 Study on redundancy solution for IP and Ethernet
  Work can be separated from rest of the work tasks
  No RAN dependency
Solution should be general to support use cases including
  Replication/elimination endpoints within 5GS or outside
  Controller within 5GS or outside
  Mixed scenarios
Be compatible with state-of-the-art IETF and IEEE solutions
  3GPP specific optimizations, simplifications may be considered.
Adds operator value to flexibly integrate 5GS to industrial deployments and provide 5GS redundancy as a service.