## Slide 1
SP-200xxx
On 5G GUTI reallocation
Source: Qualcomm Incorporated,xxx
3GPP SA #89e
September 15-21, 2020

## Slide 2: Proposal for endorsement
SA discussed and acknowledged the trade-off between user privacy protection and signalling optimisation for 5G CIoT.
Considering this trade off if the same 5G-GUTI is used multiple times for paging even for CIoT UEs, there exists a privacy risk (identification of the UE’s presence in a particular location). Therefore, for a UE in 5GMM-IDLE mode with suspend indication, the network shall always allocate a new 5G-GUTI after paging and resume of a connection, even if a NAS message is not sent.