## Slide 1: User Centric Application Service Transfer (UCAST)
3GPP TSG- SA1 Meeting # 104 S1-233134
Chicago, United States, 13 - 17 November 2023
Notes: From people looking for function to function looking for people

## Slide 2: User centric application service transfer
Today, User Centric Application Service Transfer is a popular trend to optimize user experience (e.g. vehicle infotainment) by using different UEs to support an application service (e.g. video call, gaming, navigation). By doing the transferring, the (full/a part of) application service functionality needs be transferred across UEs in real time.
The 3GPP devices can be used by a person, a family, or anyone in public place to fulfil the same user’s application service transferring among the devices

## Slide 3
The vehicle infotainment is one of important scenario, as the left picture shows. A user can transfer his/her application service from mobile-phone to vehicle-phone or vice versa on demand, such as for an ongoing video call, online-gaming, navigation service, et al.
Same mechanism also applies to other scenarios such as Could UE, public office.
However, current 3GPP system is lack of capability to support an consistent/optimized user experience for the scenario as the network has no idea about multiple 3GPP devices are serving the same user’s application service and unable to provide communication services coordinately.
The mobile phone and vehicle device(s) connected to 5G network, serving a user
User centric application service transfer – cont.

## Slide 4: Example UC: Ongoing video call
Devices: Mobile phone, display screen, camera and speaker for online video call
A user uses mobile phone used for video call and approach to his car for driving home
When getting on car, the user transfers the ongoing video call to the vehicle devices,
(camera for face shot, screen for display, speaker for voice)
When car arrives, the user transfer the video call back to the his mobile phone and walk back home
Gap analysis for example
The video call need to be served with the consistent user experience in both communication layer and application layer before and after the application transferring e.g. same/optimized QoS, same GW.
Authorization for enabling multiple devices serving for the service simultaneously

## Slide 5: Example UC: Video gaming
Devices: Mobile phone, display screen, speaker for video gaming
A user uses mobile phone used for input which is for more friendly input experience
Vehicle display screen and loudspeaker is used to display the gaming video in real time
Gap analysis for example
Simultaneous UL and DL data transmission via mobile phone and vehicle device for the same service
Round-trip latency (Time for UL + DL data transmission) for the service
Authorization for enabling multiple devices serving for the service simultaneously

## Slide 6: Potential related WIs
LUCIA：
Lucia is mainly about an authentication and identification of a user id and profile configuration accordingly. However, it focus on a certain single UE, no consideration of service transfer, and multi-device coordination in use cases
PIN
PIN is mainly about one GW UE and tethered (non-3GPP)devices behind. However, this proposal (the UCAST) is for multiple UEs connecting directly to network to support a service transfer. Moreover, this proposal is about the multiple (3GPP) UEs used by one person, a group of persons (e.g. family), or any people in a public place to support a user’s service transferring between 3GPP devices.

## Slide 7: New R20 SID Proposal
Study how 3GPP system support user centric application service transfer. Identify scenario and use cases that 3GPP system to support providing multiple 3GPP UEs for a user or a group of users (e.g. family users).
The requirements may include:
- Seamless transferring of an ongoing application service or a part of functionalities among 3GPP UEs, which may have the same subscription, context, policy, et al.
Round-trip latency for UL and DL transmission of 3GPP UEs to support a user’s real-time application service
Consistent/optimized service experience for the application service transferring among 3GPP UEs
KPI requirements to (e.g. UL and DL) support user centric application service transfer
Security aspects, such as authentication and authorization for enabling the application service transfer among UEs
Charging
NOTE: For this study, the vehicle infotainment is one of important scenario, while it also applies to other scenarios such as Cloud UE, public area office.

## Slide 8: THANKS