## Slide 1
SA1#96E
Non-3GPP device definition
vivo

## Slide 2: Non-3GPP device in other places (Not in PIRates)
22.101
  Gateway UE: a UE, which acts as a gateway providing access to and from the 3GPP network for one or more non-3GPP devices that are connected to the gateway UE.
  User: As defined in TR 21.905 [29]: An entity, not part of the 3GPP System, which uses 3GPP System services. Example: a person using a 3GPP System mobile station as a portable telephone.
  Additional examples for a user in the context of this TS: a non-3GPP device connected to the 3GPP system via a gateway, or an application running on a UE.
  26a.2.1 User Identifiers and user authentication
  The 3GPP network shall be able to provide a User Identifier for a non-3GPP device that is connected to the network via a UE that acts as a gateway.
  The 3GPP network shall support to perform authentication of a User Identity used by devices that are connected via a UE that acts as a gateway.
22.261
  8.3 Authentication
  The 5G network shall support a 3GPP supported mechanism to authenticate legacy non-3GPP devices for 5G LAN-VN access.

## Slide 3: The definition of 3GPP device: User Equipment
22.101
  14 Types of features of UEs
  3GPP specifications should support a wide variety of user equipment, i.e. setting any limitations on terminals should be avoided as much as possible. For example user equipment like hand-portable phones, personal digital assistants and laptop computers can clearly be seen as likely terminals.
  ……
  The basic mandatory UE requirements are:
  - Support for USIM. Optional support of GSM phase 2, 2+, 3GPP Release 99 and Release 4 SIM cards [34]. Phase 1, 5V SIM cards shall not be supported. Support for the SIM/ISIM is optional for the UE, however, if it is supported, the mandatory requirements for SIM/ISIM shall be supported in the UE;…..
22. 261
  User Equipment: An equipment that allows a user access to network services via 3GPP and/or non-3GPP accesses.

## Slide 4: Way forward proposal
[Observation]
  In 22.101 Clause 14: “The basic mandatory UE requirements are: Support for USIM.”
  Observation: A UE shall support USIM. Supporting USIM doesn’t mean having USIM. A UE supporting USIM may not have USIM.
[Way forward options]
  Option1: As S1-214094r2(for 22.261) and S1-214200r1(for 22.101)
    non-3GPP device: a device that does not support USIM.
  Option2: As S1-214094
    non-3GPP device: a device that doesn’t support 3GPP credentials.

## Slide 5
Thank You!