## Slide 1: Upper Layer TRaffic Aggregation and Steering, over dual 3GPP access (ULTRAS)
SA1 Rel-19 Study proposal - Overview
3GPP SA WG1 Meeting #97e S1-220112r1
Electronic Meeting, 14 - 24 Feb 2022 (revision of S1-yyxxxx)

## Slide 2: High-level Proposal: Summary
Current ATSSS (Rel-16 onward):
  Optional feature/support in the UE and 5GC
  3GPP access + non-3GPP access
  Intra and inter-PLMN
Our Proposal: add support of
  3GPP access + 3GPP access
  Intra and Inter-PLMN (PLMN + PLMN/SNPN)
In a nutshell: ATSSS + dual 3GPP access
ATSSS: Access Traffic Steering, Switch and Splitting, see TS 23.501
  Assumption: UE supports dual (3GPP) radio

## Slide 3: Motivations and Target scenarios
Main goals & benefits
Enable additional 5GS tools, under MNO control/policy, to improve access/NW resources utilization, capacity, coverage, reliability and QoE, using dual 3GPP access
Provide flexible user plane traffic aggregation, steering & switching at higher layers.
  Complement other solutions, e.g. RAN-based (where not available or suitable).
Target scenarios / options
Single PLMN
PLMN1 + PLMN2
  Single or dual subscription
PLMN + SNPN
  Single or dual subscription
Same or different 3GPP access/RAT
  E.g. NR&NR, NR&LTE, NR&NTN, 2xNTN

## Slide 4: Use cases
Few examples
Single PLMN
  Terrestrial + Satellite access
    NTN can be used to extend TN capacity/Tput, or vice versa
    Can be temporary dual RAT coverage
      e.g. UEs in a train / cruise-ship / plane, at a stopover
Other examples/options:
  NR + LTE
    E.g. if/where MR-DC (option 4) is not available
PLMN1 + PLMN2/SNPN
  Local dual-NW connectivity, e.g. in a stadium
    Using local SNPN/PLMN2 RAT for extra PLMN1 capacity, or vice versa
      Can be temporary / on-demand
    (May apply to other local scenarios, e.g. campus, enterprise, factory, home)
Other examples:
  Terrestrial + Satellite 3GPP access, or dual SAT access
    E.g. partnership by PLMN1 with SAT MNO, or bw 2 SAT MNOs
    (similar to the single-PLMN scenarios, assuming 2 separate MNOs)
UE
3GPP access (SNPN)
3GPP access (PLMN)
UPF(PSA)
Data Network
SHIP
TRAIN
[Fig. from 38.821]

## Slide 5: Existing reqs & functionalities Gaps
SA1 requirements (22.261)
(R15+) Sec. 6.3: Multiple access technologies
  Covers support of simultaneous data transmission via different access technologies (e.g. NR, E-UTRA, non-3GPP)
(R15+) Sec. 6.18: Multi-network connectivity and service across operators
  Covers simultaneous connectivity to multiple serving networks operated by different operators
  Other multi-NW connection reqs were added in R17/18: sec 6.1 (Network slicing); 6.41 (PALS)
Others
  MUSIM (dual USIM and simultaneous multi-NW access)
  Simultaneous access to PLMN and SNPN
Stage-2/3
ATSSS (R16+)
  Supports 3GPP and non-3GPP access
  Do not cover specific (ATSSS-like) upper-layers functionalities
  Focus on different services over different NWs, don’t cover same data session over multi-access connectivity and ATSSS-like functionalities
  Does not cover dual 3GPP access
Proposal for SA1 Rel-19: study use cases and potential requirements to extend ATSSS support to dual 3GPP access => See SID proposal for detailed objectives
Gaps and Proposal

## Slide 7: Annex A
ULTRAS scenarios – extra slides

## Slide 8: Scenarios: Single PLMN
  UE in coverage of dual 3GPP access, managed by a single PLMN/MNO
      Dual 3GPP access coverage can be permanent or temporary
  Dual 3GPP access can be
    different 3GPP RATs
      e.g. NR&NTN, NR&LTE
    same RAT
      e.g. NTN LEO and MEO
Example of scenarios and connectivity diagrams
PLMN
AMF
UPF
N6
N4
SMF
N11
Data Network
N1
N2
PC
F
N7
3GPP
Access
N3
N3
UE
3GPP
Access
N1
N2

## Slide 9: Scenarios: PLMN + PLMN
Area covered by both PLMNs’ 3GPP RATs
  Permanently or temporarily
The two PLMNs can be managed by the same MNO or by two partner operators
  No RAN sharing between PLMNs
Single subscription
  HPLMN+VPLMN
Dual subscription
  HPLMN1 + HPLMN2
3GPP access can be same/diff. RAT, e.g.
  NR&NR, NTN&NTN
  NR&LTE, NR&NTN
Example of scenarios and connectivity diagrams
PLMN 2
PLMN 1
AMF
UE
UPF
N3
N4
SMF
N11
3GPP access
Data
Network
N1
N2
PCF
N7
3GPP
Access
N3
UPF
AMF
SMF
N11
N2
N1
Fig shows only an example diagram - some of the interfaces may vary, e.g. based on the deployment & subscription scenario
N6
N6

## Slide 10: Scenarios: PLMN + SNPN
Location covered by PLMN and local SNPN
  permanent or temporary dual coverage
PLMN and SNPN can be managed by the same operator or by two partner operators
  No RAN sharing
Single subscription, or Dual subscription
  Dual subscription can be single-SIM (e.g. non-USIM credential for SNPN)
3GPP access can be same/diff. RAT, e.g.
  NR&NR, NTN&NTN
  NR&LTE, NR&NTN
Example of scenarios and connectivity diagrams
SNPN
PLMN
AMF
UE
UPF
N3
N4
SMF
N11
3GPP access
Data
Network
N1
N2
PCF
N7
3GPP
Access
N3
UPF
AMF
SMF
N11
N2
N1
N6
Fig shows only an example diagram - some of the interfaces may vary, e.g. based on the deployment & subscription scenario
N6

## Slide 11: Annex B
(Rel-16/17) ATSSS highlights

## Slide 12: ATSSS aspects
The ATSSS feature is an optional feature that may be supported by the UE and the 5GC network.
The ATSSS feature enables a multi-access PDU Connectivity Service, which can exchange PDUs between the UE and a data network by simultaneously using one 3GPP access network and one non-3GPP access network and two independent N3/N9 tunnels between the PSA and RAN/AN.
The UE may request a MA PDU Session when registered via both 3GPP and non-3GPP accesses, or when the UE is registered via one access only.
From 23.501
Figure 4.2.10-1: Non-roaming and Roaming with Local Breakout architecture for ATSSS support
The UE supports one or more of the steering functionalities, e.g. MPTCP functionality and/or ATSSS-LL functionality. The ATSSS-LL functionality is mandatory in the UE for MA PDU Session of type Ethernet.
The UPF may support MPTCP Proxy functionality, which communicates with the MPTCP functionality in the UE using MPTCP (IETF RFC 8684).
The UPF may support ATSSS-LL functionality (not shown in Fig)…ATSSS-LL functionality is needed for MA PDU of type Ethernet.
In addition, UE and UPF can support Performance Measurement Functionality (PMF), which may be used by the UE to obtain/report access performance measurements
The AMF, SMF and PCF are also extended with new functionalities.

## Slide 13: ATSSS aspects
From 23.501
UE/UPF measurements related protocol stack for 3GPP access and for an MA PDU Session with type IP
Steering functionalities in an example UE model