## Slide 1: DualSteer
Way Forward options
Qualcomm
3GPP TSG SA WG 1 Meeting #104 S1-233316
Chicago, USA, 13 - 17 November 2023

## Slide 2: Way Forward-1 - No split, only steer & switch (for diff services) - Both single-active and dual-active transmission, assuming dual SIM/subscription
Scenario | Proposal
Intra-PLMN | Steer/switch with no simultaneous data Optional Steer/switch with simultaneous data (dual active) Assuming two [SIM/subscriptions/Identifiers]
Inter-PLMN | Steer/switch with no simultaneous data Optional Steer/switch with simultaneous data (dual active) Assuming two [SIM/subscriptions/Identifiers]
PLMN - NPN | PNI-NPN: same as inter-PLMN SNPN: only single active steer (no sim transmission)
Notes:
- Inter-PLMN can be same or different MNO
- No restriction/exclusion on RAT combos, i.e. can be both TN, NTN or a mix

## Slide 3: Way Forward-2 - No split, only steer & switch (for diff services) - Both single-active and dual-active transmission - Using single or dual subscription - Dual subscription can be from the same operator
Scenario | Proposal
Intra-PLMN | Steer/switch with no simultaneous data Optional Steer/switch with simultaneous data (dual active) Single or two [SIM/subscriptions/Identifiers]
Inter-PLMN | Steer/switch with no simultaneous data Optional Steer/switch with simultaneous data (dual active) Single or two [SIM/subscriptions/Identifiers]
PLMN - NPN | PNI-NPN: same as inter-PLMN SNPN: only single active steer (no sim transmission)
Notes:
- Inter-PLMN can be same or different MNO
- No restriction/exclusion on RAT combos, i.e. can be both TN, NTN or a mix