## Slide 1: Network selection for a subscriber to establish an additional connection to another network (Secondary Network Selection)
Kurt Bischinger, Deutsche Telekom, Feb. 2024
S1-240021

## Slide 2: Requirements and use cases for NW selection to another network
Several requirements for a UE or a subscriber to establish concurrent connections to two networks
    Rel. 16 – Multi-network connectivity and service delivery across operators
    Rel. 18 – EASNS, PALS
    Rel. 19 – DualSteer
Some very generic requirements spread across 22.261 for the HPLMN to be able to give some priorities / policies / criteria for the selection of the (additional) network. (Ref. backup slides for details / requirements.)
However, there are no detailed requirements in stage 1, nor stage 2 or 3 specifications
Proposal for a (R20 phase 1) study to review existing requirements, examine the use cases, identify gaps and come up with detailed potential requirements for a common enhancement of PLMN selection for secondary networks.
  Level of detail for SA1 network selection requirements is beyond the typical SA1 level and covers part of stage 2. This should also be the case for this work and the potential requirements should fit in 22.011.
  Secondary networks can be PLMNs or NPNs.
  Dual SIM scenarios except DualSteer are out of scope.

## Slide 3: Potential Use Cases
Permanent selection of a secondary network in addition to a primary network connection
    According to configured user and operator preferences
    To enable Multi-network connectivity and service delivery across operators & EASNS
Temporary / on-demand selection of a secondary network
    As needed, e.g. for certain services, triggered by the UE or the network
    To enable Multi-network connectivity and service delivery across operators, EASNS & PALS
Selection of secondary networks for DualSteer use cases, e.g. coverage extension or backup connection
    Using one or two subscriptions (USIMs), but sharing the same configuration / subscription profile
Enable DualSteer / seamless service continuity across country / network borders, e.g. for V2X

## Slide 4: Issues to be considered / studied
Definition / configuration of priorities and parameters
  Dependencies between primary and secondary network selection, for both initial selection as well as periodic reselection
  Define the validity of the settings dependent on location, time, application/content etc., e.g. for PALS use cases
  Consistency with legacy network selection (of one network), differences, e.g. selection of PLMNs from a different country
Definition of what happens if connection to a secondary network is lost
  E.g. immediate reselection, reselection after some time, no reselection. Configuration of the behaviour.
Definition when none of the preferred secondary networks is available
  E.g., configuration to select no secondary network or to select any available network.
Definition when connectivity to primary network is lost
  E.g. Immediate or delayed release of secondary connection, trigger re-selection, make the secondary selection the new primary network
Similar, when primary network is re-selected to a higher priority network

## Slide 5: Study item proposal - objectives
  Study existing and potential new use cases that are related to a UE or DualSteer device being concurrently connected to a PLMN and another network.
  Study those use cases concerning the network selection of secondary networks and derive potential enhancements to network selection requirements and configurations to define
    priorities,
    dependencies between the primary and secondary network selection,
    behavior if one of the networks becomes unavailable or there are no preferred secondary networks at all,
    restrictions and validity of the information (e.g. location, time, service)
  Consolidate the requirements with an appropriate level of detail to fit in the PLMN selection text in 22.011.
  Note 1: Secondary networks can be PLMNs or NPNs.
  Note 2: Dual SIM scenarios except DualSteer are out of scope.

## Slide 6
Backup

## Slide 7: Connections to more than one network, R16
22.261, Rel. 16 – Clause 6.18 Multi-network connectivity and service delivery across operators
  The 5G system shall enable users to obtain services from more than one network simultaneously on an on-demand basis.
  For a user with a single operator subscription, the use of multiple serving networks operated by different operators shall be under the control of the home operator. […]

## Slide 8: Connections to more than one network, R18
22.261, Rel. 18 – EASNS (ref. clause 6.1)
  For UEs that have the ability to obtain service from more than one VPLMN simultaneously, the following requirements apply:
    When a roaming UE with a single PLMN subscription requires simultaneous access to multiple network slices and the network slices are not available in a single VPLMN, the 5G system shall enable the UE to:
      be registered to more than one VPLMN simultaneously; and
      use network slices from more than one VPLMN simultaneously
      The HPLMN shall be able to authorise a roaming UE with a single PLMN subscription to be registered to more than one VPLMN simultaneously in order to access network slices of those VPLMNs.
      The HPLMN shall be able to provide a UE with permission and prioritisation information of the VPLMNs the UE is authorised to register to in order to use specific network slices.

## Slide 9: Connections to more than one network, R18 & 19
22.261, Rel. 18 – PALS (ref. clause 6.41.2)
The 5G system shall support secure mechanisms to allow a home network to coordinate with a hosting network for a subscriber to temporarily access the hosting network (e.g., based on temporary credentials) at a given time (start time and duration) and location.
Based on localized service agreements, the hosting network shall be able to provide required connectivity and QoS for a UE simultaneously connected to the hosting network for localized services and its home network for home network services.
22.261, Rel. 19 – DualSteer (ref. clause 6.50)
  Technically two UEs (with two subscriptions / USIMs) attaching to two networks, but sharing the same subscription profile  should act like one UE:
  For traffic steering and/or switching of user data across two 3GPP access networks, the 5G system shall be able to allow a HPLMN to provide policies and criteria for a DualSteer device to connect to an additional PLMN/NPN, or an additional RAT within the same PLMN.