## Slide 1
Lessons learnt from 5G study: Coordination with RAN study
S1-241121 3GPP SA1#106, 27-31 May 2024 - Korea, Jeju
© 3GPP 2024
Source: Nokia
Agenda item: 10.2
Document for: Discussion

## Slide 2: Outline
Alignment with RAN requirements
General system requirements
Support of legacy services
KPI study/work
© 3GPP 2024

## Slide 3: Alignment with RAN requirements
Observations:
Apart from radio specific requirements, system/service-related requirements were defined in 5G RAN TR 38.913.
  Architecture, migration, NW operation, etc.
Some are (partially) covered by SA1 study/work, but not all (see Annex in detail)
No need to be aligned one by one, but It would be desirable to cross check between SA1 and RAN at some point of time.
Proposals:
After RAN study is approved, setup a cross-checking mechanism between SA1 and RAN when the study is matured (at intermediate phase or end of study).
When RAN stage-2/3 is completed, SA1 performs clean-up of normative SA1 requirements to be aligned with RAN specs.
NOTE: Numbering of normative requirements in stage-1 spec can facilitate cross-checking and clean-up works.
© 3GPP 2024
From analysis of 5G study/work in SA1 and 5G study at RAN plenary

## Slide 4: General system requirements
Observations:
For every new system/generation, there exists basic requirements how to design the overall mobile communication systems (architecture, migration, security, operation and management, etc.).
Those requirements can be studied mostly w/o the need to drive from detailed use case description, rather can be studied from lessons learnt from commercial 5GS deployments.
  There are some exceptions for which target use cases are useful (e.g., mobility for NTN, high speed train, etc.).
It also enables early input to RAN study on basic requirements.
Proposals:
From the beginning of SI phase, start to develop basic requirements common to all use cases. Examples are:
  Energy consumption in total, per subscriber​, per bit
  Support for new and expanded differentiators for 6G ​
  Enhanced user experience, e.g. device power saving, instant access to high bandwidth, coverage, uplink performance/coverage, security​
  Migration architecture (e.g. SA, NSA, aggregation, etc…)​
  Inter-RAT co-existence and interworking​
  TCO reduction
© 3GPP 2024
Basic requirements common to all use cases

## Slide 5: Support of legacy services over 6G System
Observations:
Not all of the legacy services/features have been deployed in commercial networks.
  There are services/features introduced every generations but never been implemented as of now…
Whenever a new system is deployed, it is expected to offer the same services/features as supported in the legacy systems (i.e., same use cases and requirements).
Downstream WGs sometimes performed down scoping to introduce stage-2/3 functionalities from stage-1 requirements. Nonetheless, it is desirable if SA1 can play a pivotal role to focus on promising 6G Day-1 services/features even from stage-1 level.
  It helps downstream WGs to avoid down scoping discussion and focus on the promising features to produce high quality standard until stage-3/coding freeze target.
Proposals:
Only the stage-1 requirements for 6G Day-1 services are introduced in Rel-21.
  If there is no new requirement for the legacy services, the requirements are referred to the existing 5G/5G-Adv stage-1 specs.
Do not introduce any stage-1 requirements in Rel-21 for the legacy services/features not deployed in commercial networks, unless there exists clear market demand for 6G Day-1 services.
  Except for the requirements ensuring forward compatibility for future release support (to avoid non-backward compatible change).
After Rel-21 and onwards, when those services/features are introduced, the stage-1 spec for 6G refers to the existing 5G/5G-adv stage-1 requirements.
© 3GPP 2024
Legacy services supported up to 5G-Adv

## Slide 6: KPI study/work in SA1
Observations:
Both SA1 and RAN introduced KPIs during 5G study, where most of the cases defined KPIs were not aligned between SA1 and RAN studies.
  E.g., peak data rate of DL 20G/UL 10G in RAN SI, whereas, several values specific to use cases/deployments in SA1 SI (100M MBB for pedestrian and vehicle, 300 Mbps for broadcast, etc.)
KPIs defined by RAN were self-evaluated by themselves to assess if the defined value can be fulfilled, according to the standardized radio access technologies (for the purpose of ITU-R submission).
In contrast, there was no assessment and evaluation whether KPIs defined by SA1 can be fulfilled on the target assumptions (e.g., hotspot area, moving slowly, etc.)
Proposals:
Discuss if KPI study/work is continued in SA1.
  If so, discuss how to assess and evaluate if the defined value is realistic from service perspective.
© 3GPP 2024
In relation to parallel study/work in RAN

## Slide 7: Summary
After RAN study is approved, setup a cross-checking mechanism between SA1 and RAN when the study is matured (at intermediate phase or end of study).
When RAN stage-2/3 is completed, SA1 performs clean-up of normative SA1 requirements to be aligned with RAN specs.
NOTE: Numbering of normative requirements in stage-1 spec can facilitate cross-checking and clean-up works.
From the beginning of SI phase, start to develop basic requirements common to all use cases. Examples are:
  Energy consumption in total, per subscriber , per bit
  Support for new and expanded differentiators for 6G ​
  Enhanced user experience, e.g. device power saving, instant access to high bandwidth, coverage, uplink performance/coverage, security​
  Migration architecture (e.g. SA, NSA, aggregation, etc…)​
  Inter-RAT co-existence and interworking​
  TCO reduction
Only the stage-1 requirements for 6G Day-1 services are introduced in Rel-21.
  If there is no new requirement for the legacy services, the requirements are referred to the existing 5G/5G-Adv stage-1 specs.
Do not introduce any stage-1 requirements in Rel-21 for the legacy services/features not deployed in commercial networks, unless there exists clear market demand for 6G Day-1 services.
  Except for the requirements ensuring forward compatibility for future release support (to avoid non-backward compatible change).
After Rel-21 and onwards, when those services/features are introduced, the stage-1 spec for 6G refers to the existing 5G/5G-adv stage-1 requirements.
Discuss if KPI study/work is continued in SA1.
  If so, discuss how to assess and evaluate if the defined value is realistic from service perspective.
Proposals in relation to RAN study

## Slide 8
Annex:
Analysis on 5G RAN study

## Slide 9
Evolution of RAN study from LTE to LTE-adv
Not much structural change from TR 25.913 to TR 36.913
SA1 related

## Slide 10
5G RAN Study
Service requirements and operational requirements expanded in TR 38.913
RP-160811: The inputs from other organizations and WGs, e.g., NGMN, ITU-R, and 3GPP SA1, can be referred to in the discussions. The study item will convert required capabilities in those inputs to technical metrics that can be evaluated from RAN perspective.

## Slide 11
Methodology
Only take RAN 5G study SA1 relevant requirements (can be subjective) into the analysis.
Within one requirement, include not SA1 relevant part for completeness.
For the evaluation of SA1 cover or not, we only consider SA1 relevant part.
Only include the references to SA1 TR and TS.
Check TS 22.261 v16.6.0 (at the time of SMARTER_Ph2 completion Dec. 2018) and other R16 TS to see what were taken up by SA1 normative work.
Covered, partially covered, not covered

## Slide 12
Requirements for architecture and migration of Next Generation Radio Access Technologies
RAN requirements relevant to SA1 | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
The RAN architecture shall support tight interworking between the new RAT and LTE. Considering high performing inter-RAT mobility and aggregation of data flows via at least dual connectivity between LTE and new RAT. This shall be supported for both collocated and non-collocated site deployments. | TR 22.864 [PR 5.7.2.2-001] [PR 5.6.2-001] | TS 22.261 clause 5.5.1 | Aggregation of data flows not covered in TR. Tight interworking not explicitly covered in TS.
The RAN architecture shall allow for deployment flexibility e.g. to host relevant RAN, CN and application functions close together at the edges of the network, when needed, e.g. to enable context aware service delivery, low latency services, etc... | TR 22.864 [PR 5.4.2-003] | TS 22.261 clause 6.6.2 clause 6.11.2 | Content caching entity under the control of the operator not adopted.
The RAN architecture shall allow for the operation of Network Slicing. | TR 22.864 clause 7.1 | TS 22.261 clause 6.1.2.2 | 
The RAN architecture shall support sharing of the RAN between multiple operators. | TR 22.891 clause 5.4.3 | TS 22.101 clause 28.1 | 
The design of the RAN architecture shall allow the deployment of new services rapidly and efficiently. |  |  | Generally covered.
The design of the RAN architecture shall allow the support of 3GPP defined service classes (e.g. interactive, background, streaming and conversational). | TR 22.864 [PR 5.1.2.2-007] | TS 22.261 clause 6.4.1 | Implicitly from UE perspective.
The design of the RAN architecture shall enable lower CAPEX/OPEX with respect to current networks to achieve the same level of services. |  |  | Not covered.
The RAN architecture shall support operator-controlled sidelink (device-to-device) operation, both in coverage and out of coverage. | TR 22.891 clause 5.24.2 TR 22.862 [CPR 7.7-021] | TS 22.186 clause 5.1 | Operator-controlled and coverage aspects not covered.
Notes: 7:7

## Slide 13
Multimedia Broadcast/Multicast Service
RAN requirements relevant to SA1 | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
The new RAT shall support existing Multicast/Broadcast services (e.g. download, streaming, group communication, TV, etc.) and new services (e.g. V2X, etc). | TR 22.864 clause 7.4 | TS 22.261 clause 6.13.2 | Not explicitly covered. V2X was left out for further study.
The new RAT shall support dynamic adjustment of the Multicast/Broadcast area based on e.g. the user distribution or service requirements. |  | TS 22.261 clause 6.13.2 | Dynamic adjustment aspect not covered in TS.
The new RAT shall support concurrent delivery of both unicast and Multicast/Broadcast services to the users. | TR 22.864 [PR 5.1.2.4-003] | TS 22.261 clause 6.13.2 | Not explicitly on unicast. Concurrent via a broadcast/multicast carrier and another carrier.
The new RAT shall support Multicast/Broadcast network sharing between multiple participating MNOs, including the case of a dedicated MBMS network. |  |  | Not covered.
The new RAT shall make it possible to cover large geographical areas up to the size of an entire country in SFN mode with network synchronization and shall allow cell radii of up to 100 km if required to facilitate that objective. It shall also support local, regional and national broadcast areas. |  | TS 22.261 clause 6.13.2 | Inter-site distances of up to 200 km covered in TS.
The new RAT shall support Multicast/Broadcast services for fixed, portable and mobile UEs. Mobility up to 250 km/h shall be supported. |  | TS 22.261 clause 6.13.2 | Support for stationary and mobile UEs covered.
The new RAT shall leverage usage of RAN equipment (hard- and software) including e.g. multi-antenna capabilities (e.g. MIMO) to improve Multicast/Broadcast capacity and reliability. | TR 22.864 [PR 5.1.2.4-007] [PR 5.1.2.4-004a] | TS 22.261 clause 6.13.2 | Implicit requirements on improved capacity and reliability in TR. Reliability not covered in TS.
The new RAT shall support Multicast/Broadcast services for mMTC devices. |  |  | Not covered.
Notes: 3:6

## Slide 14
Location/Positioning Service
RAN requirements relevant to SA1 | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
The NR should enable, and improve if suitable, state-of-art positioning techniques, such as RAN-embedded (Cell-ID, E-Cell ID, OTDOA, UTDOA, etc.) and RAN-external (GNSS, Bluetooth, WLAN, Terrestrial Beacon Systems (TBS), sensors, etc.). Additionally, potential D2D based positioning techniques should be considered. |  | TS 22.261 clause 6.27.2 clause 7.3.2.1 | D2D based positioning not covered in TS.
The NR positioning shall exploit high bandwidth, massive antenna systems, network architecture/ functionalities (e.g. heterogeneous networks, broadcast, MBMS) and deployment of massive number of devices. NR positioning shall support indoors and outdoors use cases. | TR 22.862 [PR 5.4.3-001] | TS 22.261 clause 6.27.1 Clause 7.3.2.2 | Indoors and outdoors are covered. Requirements related to higher accuracy positioning have not been confirmed and left for further study.
NR shall support regulatory positioning requirements. |  | TS 22.261 clause 6.27.2 | 
NR design targets for commercial positioning use cases include: Support for range of accuracy levels, latency levels and device categories Support accuracy and latency as defined in TR 22.862 for some use cases Reduced network complexity Reduced device cost Reduced device power consumption Efficient signalling over the air interface and in the network Support for hybrid positioning methods Scalability (support for large number of devices) High security High availability Support UE speed as defined in TR 22.862 | TR 22.862 clause 5.4 | TS 22.261 clause 6.27.2 clause 7.3.2 clause 8.5 clause 8.7 | Requirements related to higher accuracy positioning have not been confirmed and left for further study. 1/2/5/7/9/10/11 covered in TS.
Notes: 2:4

## Slide 15
Critical Communications services
RAN requirements relevant to SA1 | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
The RAN design for the Next Generation Radio Access Technologies shall support D2D. | TR 22.862 [CPR 7.6-005][CPR 7.7-021] | TS 22.280 clause 7.2 | 
The RAN design for the Next Generation Radio Access Technologies shall support Mission Critical Communications for diverse types of services (e.g. MCPTT, MCVideo, MCData in 3GPP TS 22.179, 3GPP TS 22.280, 3GPP TS 22.281, and 3GPP TS 22.282). | TR 22.862 [CPR 7.5-005][CPR 7.5-006] [CPR 7.5-007][CPR 7.5-008] | TS 22.179 clause 4.1 TS 22.280 TS 22.281 clause 4.1 TS 22.282 clause 4 | From performance perspective in TR.
The RAN design for the Next Generation Radio Access Technologies shall support efficient group communications (e.g. GCSE_LTE, SC-PTM in 3GPP TS 22.468). |  | TS 22.468 clause 5.1.4 | 
The RAN design for the Next Generation Radio Access Technologies shall support isolated communications (e.g. IOPS in 3GPP TS 22.346). | TR 22.862 [CPR 7.2-006][CPR 7.3-007] [CPR 7.4-004][CPR 7.5-010] [CPR 7.6-007][CPR 7.7-017] | TS 22.261 clause 8.2 | Not exactly on isolated communications, but more about isolation of traffic and system resources in TR.
The RAN design for the Next Generation Radio Access Technologies shall provide mechanisms to enable emergency calls including positioning/location for emergency calls (such as is found in 3GPP TS 22.101 section 10 for emergency calls and 3GPP TS 22.071 for position/location) when appropriate. | TR 22.862 [CPR 7.7-011] TR 22.864 [PR 5.6.2-021] | TS 22.101 clause 10.1 clause 10.6 TS 22.071 clause 4.0 | Not explicitly in TR.
The RAN design for the Next Generation Radio Access Technologies shall provide mechanisms to enable Multimedia Priority Services (such as is found in 3GPP TS 22.153). | TR 22.862 [CPR 7.7-011] | TS 22.153 clause 4 | Not explicitly in TR.
The RAN design for the Next Generation Radio Access Technologies shall provide mechanisms to enable public warning services that provides warning/notifications to users meeting regional regulatory requirements (such as is found in 3GPP TS 22.268). |  | TS 22.268 clause 4.2 | 
Notes: 5:7

## Slide 16
V2X communication
RAN requirements relevant to SA1 | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
The RAN design for NR V2X shall provide communication via infrastructure, including MBMS support, for V2X services (such as found in 3GPP TS 22.185) and advanced V2X services (such as found in the outcome of the SA1 study 3GPP TS 22.886). | TR 22.891 clause 5.33.2 | TS 22.186 clause 5 | More from performance perspective, but MBMS is covered in TR. V2X was left out for further study. MBMS not explicitly covered in TS.
The RAN design for NR V2X shall provide communication via sidelink for V2X services (such as found in 3GPP TS 22.185) and advanced V2X services (such as found in the outcome of the SA1 study 3GPP TS 22.886). | TR 22.891 clause 5.33.2 | TS 22.186 clause 5.1 | More from performance perspective in TR. V2X was left out for further study.
It is not intended for NR V2X to replace the services offered by LTE V2X. Instead, the NR V2X shall complement LTE V2X for advanced V2X services and support interworking with LTE V2X. |  |  | Not covered. V2X was left out for further study.
Notes: 0:2

## Slide 17
Operational requirements (1)
RAN requirements relevant to SA1 | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
Support for wide range of services means the system shall be inherently flexible enough to meet the connectivity requirements of a range of existing and future (as yet unknown) services to be deployable on a single continuous block of spectrum in an efficient manner. | TR 22.864 [PR 5.1.2.5-001] | TS 22.261 clause 7.2.2 | Not exactly, but more about deploying networks for a specific set of services.
3GPP system shall support procedures for interworking with non 3GPP RATs. | TR 22.864 [PR 5.6.2-007] [PR 5.6.2-008] | TS 22.261 clause 6.3.2.1 | 
The next generation access network shall support interworking with WLAN. The number of solutions selected should be minimized. | TR 22.864 [PR 5.6.2-006] [PR 5.6.2-007] [PR 5.6.2-008] | TS 22.261 clause 6.3.2.1 | Implicitly covered, but not on the solutions.
User / application level QoS and QoE monitoring capability by UEs and network elements shall be supported. |  | TS 22.261 clause 6.23.2 | QoE monitoring not covered.
3GPP shall support ultra-low cost network infrastructures, ultra-low cost devices, and ultra-low cost operation and maintenance to enable economically viable deployments for the Provision of minimal services (Data and Voice) for very low-ARPU areas. | TR 22.891 clause 5.48 | TS 22.261 clause 6.16.2 | Cost not covered.
The RAN system shall have the capability to minimize the backhaul and signalling load in line with the requirements in section 5.48 of 3GPP TR 22.891). | TR 22.891 clause 5.48.2 TR 22.864 [PR 5.1.2.6-005] | TS 22.261 clause 6.4.2 | 
The design of the 5G RAN and Radio Interface Technology shall aim at supporting wireless relay functions. |  |  | Not covered, but more on relay UE.
The RAN availability is characterized by its availability rate X, defined as follows: a base station is available for the targeted communication X% of the time. Unavailable communication for shorter period than [Y] ms shall not be counted. | TR 22.862 clause 3.1 | TS 22.261 clause 3.1 | 
The NR specification’s ability to provide URLLC services shall not be compromised by the functions defined to improve the network or UE energy efficiency, or by system reconfigurations and software upgrades. |  |  | Not covered.
Notes: 6:7

## Slide 18
Operational requirements (2) - Security and Privacy
RAN requirements relevant to SA1 | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
The RAN design for the Next Generation Radio Access Technologies shall ensure support for integrity and confidentiality protection of radio signalling messages, including messages between RAN and Core network nodes. | TR 22.861 / TR 22.864 [PR 6.1-001a] |  | Only UEs using 5G LAN-type service and data protection covered in TS.
The RAN design for the Next Generation Radio Access Technologies shall ensure the ability to support integrity and confidentiality protection of user plane messages, including messages between RAN and Core network nodes, with the use of such security to be configurable during security set-up. | TR 22.861 / TR 22.864 [PR 6.1-001] | TS 22.261 clause 8.9 | Configurable during set-up not covered.
The RAN design for the Next Generation Radio Access Technologies shall ensure support for the allocation and use of identities to provide user privacy, e.g. reduce the need for sending any permanent identities in the clear. | TR 22.864 [PR 5.2.2-008][PR 5.6.2-020] [PR 5.8.2-003][PR 5.8.2-004] | TS 22.261 clause 8.5 | 
The RAN design for the Next Generation Radio Access Technologies shall ensure the efficient establishment of RAN security mechanisms. | TR 22.861 / TR 22.864 [PR 5.1.3.3-001] [PR 5.1.3.5-003] [PR 5.3.3.1-005] [PR 6.1-002] [PR 6.1-002a] | TS 22.261 clause 8.8 | 
The RAN design for the Next Generation Radio Access Technologies shall ensure resilience against jamming. |  |  | Not covered.
The RAN design for the Next Generation Radio Access Technologies shall provide mechanisms to enable lawful intercept for appropriate services. | TR 22.864 [PR 5.1.2.2-006a] [PR 5.4.2-002a] [PR 5.8.2-010] [PR 5.8.2-011][PR 5.8.2-012] | TS 22.261 clause 8.6 | 
Notes: 5:4

## Slide 19
Some observations from 5G
In total, 45 RAN requirements relevant to SA1
Chart: Study
| Covered | Partially covered | Not covered
Study | 21 | 7 | 17
Chart: Normative work
| Covered | Partially covered | Not covered
Normative work | 24 | 13 | 8
Chart: 
| Umbrella | eMBB | mIoT | CRIC | NEO
Study | 4 | 0 | 3 | 9 | 17
Chart: 
| SMARTER | Other TS
Normative work | 26 | 10
Requirement statistics covered by SA1 study
Statistics where RAN requirement is covered
NOTE: Sum of the pie chart is not aligned with the sum of “(partially) covered” as some requirements are covered by multiple TR/TS.