## Slide 1
Motivation for Rel-20 5G Advanced for MBS NTN to revise the Study on Satellite access – Phase 4
Agenda Item: 4 “New Work Items Rel-20 5G Advanced Only”
SES, NOVAMINT, Thales, ESA, Inmarsat, Viasat, EchoStar, JSAT, TNO, Gilat, Airbus, Dish Network, IIT Bombay, ETRI, ISSDU, EBU
S1-242117, 3GPP SA1#107, 19-23 August 2024 – The Netherlands, Maastricht
© 3GPP 2024

## Slide 2: Considerations for Enhanced Support for Broadcast services with Satellite Access System for Unregistered UE
To enable Public Service Broadcast (PSB) services to Unregistered UE
To take benefits of Satellite Access System for their scalability, vast geographical coverage areas
Satellite Access with PSB designed today for unregistered UE: this ensure equitable access, reduces complexity of the receiving device and reducing power consumption at UE
Unregistered UE = sim-card less EU or no 3GPP subscription needed to access the broadcast service  no need to provision this type of UEs, reducing OPEX for satellite operators
Free-to-air service characterised by no content encryption and being made available at no additional cost to the end user
Satellite operators require this feature to enable deployment for Broadcast over 5G Advanced as continuity of the existing legacy system for Broadcast
Doesn’t not require complexity in the system specification
Will allow to provide Broadcast using 3GPP system rather than other systems – important to reach markets where satellite is the main access system for Broadcast => Not addressing this in 5G Advanced will likely maintain non 3GPP systems for Broadcast for at least the next 15-20 years if not more

## Slide 3: Considerations for Enhanced Support for Broadcast services with Satellite Access System for Unregistered UE
RAN WI for Broadcast NTN in Rel-19
Justification: when the intended service area is expected to be smaller than the coverage of a Uu cell, some enhancements need to be done to notify the service area of a Broadcast service.
Objective:
  Specify signalling of the intended service area of a broadcast service (e.g. MBS broadcast) via NR NTN [RAN2, RAN3]
  Specify SIB signalling to indicate the intended service area in case the satellite footprint covers a larger area. [RAN2]
  Specify the necessary signalling between CN and NG-RAN. [RAN3]
This WI in RAN doesn’t consider unregistered UE for Broadcast

## Slide 4: Considerations for Enhanced Support for Broadcast services with Satellite Access System for Unregistered UE
SA1 perspective:
Such capabilities to support unregistered UE were defined by SA1 in the context of 4G Free-to-air (FTA) as specified in TS 22.101 clause 32 (3GPP enhancement for TV application support)
However, this is not supported in the context of 5G system and not taking into account satellite access as such as part of the 5G system.
UE aspects:
The UEs impacted are dedicated UEs adapted for receiving broadcast services by satellite access.
The UEs are not expected to initiate transmission
Terrestrial Network impacts:
It is assumed that if these UEs need to access terrestrial network, they will need to be registered UEs.
When broadcasting through satellite access, it will not use any MNO spectrum
Therefore, it is important to include the “Enhanced Support for Broadcast Services with Satellite Access System for Unregistered UE” in the context 5G-Advanced timeline

## Slide 5: Conclusion
We propose to revise the SID on Study on satellite access - Phase 4 to include:
“Enhanced Support for Broadcast Services with Satellite Access System for Unregistered UE”
With the following additional objective:
to identify the gaps between the 4G Free-to-air (FTA) as specified in TS 22.101 clause 32 (3GPP enhancement for TV application support) and the 5G system and identify potential new service requirements to support the use case of broadcast services using satellite access.

## Slide 6
Annex:
Considerations for Enhanced Support for Multicast Services with Satellite Access System

## Slide 7: Considerations for Enhanced Support for Multicast Services with Satellite Access System
To enable Multicast over Satellite Access System aiming to conserve spectrum resources, enhance energy efficiency and improves system scalability
Targeted multicast applications: remote control of vehicles, media content distribution to moving vehicles, distributing operating system patches or antivirus updates … Mainly Reliable Multicast and Mission Critical Multicast Services
Multicast applications served by Satellite Access System: Ensuring that all multicast data is delivered to each group member reliably and orderly within a maximum latency range
NGSO orbits are the one to address such applications
NGSO orbits is not yet mature in 3GPP while considering the different deployment models more specifically the ones with regenerative payload (in progress: Phase 2 within Release 19)
Even if this feature is seen as a 5G-Advanced feature, the timeline of 5G-Advanced will not make it possible to introduce Multicast for Satellite Access System

## Slide 8: Considerations for Enhanced Support for Multicast Services with Satellite Access System
Multicast Services with Satellite Access System is of great importance for satellite operators due to all the advantages that it brings especially for NGSO deployment
Baseline requirements of 6G should support natively Satellite Access System (NGSO with Transparent and Regenerative) which will enable to support in a proper way the Multicast Services mentioned earlier and not precluding others: Reliable Multicast, Mission Critical Multicast …

## Slide 9
Thank you