## Slide 1
Considerations for AIoT LSs
Source: Qualcomm
Agenda item: 3
Document for: Discussion
© 3GPP 2024
S1-242121, 3GPP TSG-SA1 Meeting #107, Maastricht, The Netherlands, August 19 – 23, 2024

## Slide 2: Introduction
In this discussion paper, we will discuss the two Ambient IoT LSs received by SA1:
  LS from SA2 (S2-2407231):
  LS from SA plenary (SP-241016):
To address the questions asked in the LSs, we will
  present candidates for two candidate business models and discuss the features of each model.
  present info. on the subscriptions and UICC support for IoT devices.
We employ SA1 to take the information presented in this discussion paper into consideration when responding to the LSs.

## Slide 3: Background: Highlights of LS Requests
LS from SA2 (S2-2407231):
  Are requirements for support of an unalterable/permanent equipment identification, and any specific usage, also valid for Ambient IoT devices that only send uplink messages when triggered by the network?
  Do the requirements listed in clause 5.2.6 of TS 22.369 for privacy protection apply to any Ambient IoT device that need to be supported in Rel-19? If not, does this imply that such devices would be restricted to certain deployment scenarios?
    TS 22 369 clause 5.2.6:
      The 5G system shall enable security protection suitable for Ambient IoT, without compromising overall 5G security protection.
      The 5G system shall be able to provide a mechanism to protect the privacy of information (e.g., location and identity) exchanged during communication between an Ambient IoT device and the 5G network or an Ambient IoT capable UE.
  Does command / inventory response signaling, e.g., for sensor data collection or actuator control in TS 22.369 clause 4.3, need to generally be security protected (privacy, integrity and confidentiality protection)?
LS from SA plenary (SP-241016):
  SA3 reported on contentions issues regarding authentication requirements and communication security requirements in the Ambient IoT Service Study.
  Unclear business models (e.g., subscription of devices or of application servers, i.e., does each device need to be charged individually, or aggregated charging per application server).
  3GPP scope of lifecycle management (e.g., initial provisioning, transfer of ownership, etc.) for Ambient IoT Services and devices.
  One of the controversial discussions in SA3 is regarding the requirements of secure storage, tamper resistance of credentials for access security with the use of USIM on UICC with regards to the limited capabilities of A-IoT devices.

## Slide 4: Business models for AIoT

## Slide 5: Business Models for AIoT devices (1)
For Ambient IoT devices, the business Models could follow an Application-managed model or an MNO-managed model .
For the Application-managed model
  devices have unique identifier tied to physical assets, subscription and security are managed through the application.
  example of application managed model is the RFID model where RFID tags are used to track physical objects/assets throughout the supply chain.
  RFID tags are identified using a universal ID called Electronic Product Code (EPC) which can be read by an RFID reader.
  RFID tags do not require per device subscription.
  Tag security is optional and can be applied for selected operations only (e.g., for the initial writing of Electronic Product Code (EPC) to the tag).
Production
RFID tag
Logistics
RFID tag
Warehouse
RFID tag
Distribution
RFID tag
Retail
RFID tag

## Slide 6: Business Models for AIoT devices (2)
MNO-managed Model: In this model, the AIoT device is managed by the MNO including identity, subscriptions, security, etc.
  Each AIoT device would be require a subscription and provisioning with a unique ID such as IMSI/SUPI.
  Network layer security is provided by the MNO
  Roaming services would be required for scenarios where the AIoT device is outside the home network
1) Provision IMSI-like subscription ID and keys to AIoT device
MNO (Home network)
MNO
MNO
MNO
MNO
Interconnect/
Roaming
Production
AIoT Device
Logistics
AIoT Device
Warehouse
AIoT Device
Distribution
AIoT Device
Retail
AIoT Device
2) Authenticate AIoT device based on home network subscription / apply wholesale charging.

## Slide 7: Business Models: Summary and Next Step
Note: MNO can host the application-managed business model via Application function.
Next Step: Given the two AIoT business models presented, it is imperative that SA1 decides which business model(s) to be supported for AIoT devices.
Business Model/ Features | Application-Managed | MNO-Managed
Identifiers | Universal ID (e.g., EPC) | Subscriber ID (e.g., IMSI/SUPI)
Per Device Subscription | No | Yes
Security Support | Optionally provided at the application based on pre-shared keys | 3GPP Security (e.g., AIoT device ID verification, encryption and confidentiality protection)
Life Cycle Management | - EPC can be modified; optionally protected by pre-shared key - Requires pre-shared key to be shared with next owner | - MNOs directly or indirectly involved in provisioning of subscriber ID and keys to individual tags - MNOs directly/indirectly involved in re-provisioning in case of MNO
Summary

## Slide 8: AIoT Subscription

## Slide 9: Subscription for AIoT Devices (1)
Based on the current definition of AIoT and the existing IoT device requirements in TS 22.261, it seems the support of 3GPP subscription is necessary for AIoT devices.
  1. According to TS 22.261 v19.7.0, in Subclause 3.1.
  ….
  Ambient IoT device: An ambient power-enabled Internet of Things device is an IoT device powered by energy harvesting, being either battery-less or with limited energy storage capability (e.g., using a capacitor).
    ….
    IoT device: a type of UE which is dedicated for a set of specific use cases or services and which is allowed to make use of certain features restricted to this type of UEs.
      NOTE 5: An IoT device may be optimized for the specific needs of services and application being executed (e.g. smart home/city, smart utilities, e-Health and smart wearables). Some IoT devices are not intended for human type.
    Observation 1: An Ambient IoT device is an IoT device and a UE.

## Slide 10: Subscription for AIoT Devices (2)
According to TS 22.261 v19.7.0, Subclause 6.14.2 (Requirements for Subscription Aspects):
    An IoT device which is able to access a 5G PLMN in direct network connection mode using a 3GPP RAT shall have a 3GPP subscription.
    The 5G system shall allow the operator to identify a UE as an IoT device based on UE characteristics (e.g. identified by an equipment identifier or a range of equipment identifiers) or subscription or the combination of both.
    The 5G system shall be able to provide mechanisms to change the association between a subscription and address/number of an IoT device (e.g. changing the owner and subscription information associated with the IoT device) within the same operator and in between different operators in an automated or manual way.
    The 5G system shall be able to support identification of subscriptions independently of identification of IoT devices. Both identities shall be secure.
    An IoT device which is able to connect to a UE in direct device connection mode shall have a 3GPP subscription, if the IoT device needs to be identifiable by the core network (e.g. for IoT device management purposes or to use indirect network connection mode).
    Based on operator policy, the 5G system shall support a mechanism to provision on-demand connectivity (e.g. IP connectivity for remote provisioning). This on-demand mechanism should enable means for a user to request on-the-spot network connectivity while providing operators with identification and security tools for the provided connectivity.
    The 5G system shall support a secure mechanism for a home operator to remotely provision the 3GPP credentials of a uniquely identifiable and verifiably secure IoT device.
    The 5G system shall support a secure mechanism for the network operator of an NPN to remotely provision the non-3GPP identities and credentials of a uniquely identifiable and verifiably secure IoT device.
    Based on MNO and NPN policy, the 5G system shall support a mechanism to enable MNO to update the subscription of an authorized UE in order to allow the UE to connect to a desired NPN. This on-demand mechanism should enable means for a user to request on-the-spot network connectivity which is authorized by its MNO.
    Based on operator policy, the 5G system shall provide means for authorised 3rd parties to request changes to UE subscription parameters for access to data networks, e.g., static IP address and configuration parameters for data network access.
    Observation 2: Since AIoT devices are considered IoT devices the subscription requirements in TS 22.261, 6.14.2 apply to AIoT devices.
    Note: AIoT devices support direct and indirect network connection as well as AIoT to UE direct device connection mode, TS 22.369, v19.2.0

## Slide 11: UICC Support

## Slide 12: UICC Support for AIoT Devices (1)
According to TS 22.261 v15.9.0 Clause 8.2
  …
    3GPP subscription identifier(s) and long term key(s) shall be stored and processed within a UE using a tamper resistant secure hardware component. This requirement does not apply to non-AKA based subscription credentials used for private networks.
…
  Note: After v15.9.0 of TS 22.261, this requirement was moved to the SA3 specifications TS 33. 501
According to TS 33.501 Clause 5.2.4 (Secure storage and processing of subscription credentials)
      The following requirements apply for the storage and processing of the subscription credentials used to access the 5G network:
    The subscription credential(s) shall be integrity protected within the UE using a tamper resistant secure hardware component.
    The long-term key(s) of the subscription credential(s) (i.e. K) shall be confidentiality protected within the UE using a tamper resistant secure hardware component.
    The long-term key(s) of the subscription credential(s) shall never be available in the clear outside of the tamper resistant secure hardware component.
    The authentication algorithm(s) that make use of the subscription credentials shall always be executed within the tamper resistant secure hardware component.
    It shall be possible to perform a security evaluation / assessment according to the respective security requirements of the tamper resistant secure hardware component.
  NOTE: The security assessment scheme used for the security evaluation of the tamper resistant secure hardware component is outside the scope of 3GPP specifications.

## Slide 13: UICC Support for AIoT Devices (2)
According to TS 22.261 v15.9.0 Clause 8.2 TS 33.501 clause 6.1.1.1 (specific to EAP-AKA’ and 5G AKA)
      UE and serving network shall support EAP-AKA' and 5G AKA authentication methods.
      NOTE 2b: It is the home operator's decision which authentication method is selected.
      The USIM shall reside on a UICC. The UICC may be removable or non-removable.
      NOTE 3: For non-3GPP access networks USIM applies in case of terminal with 3GPP access capabilities.
      If the terminal supports 3GPP access capabilities, the credentials used with EAP-AKA' and 5G AKA for non-3GPP access networks shall reside on the UICC.
  NOTE 4: EAP-AKA' and 5G AKA are the only authentication methods that are supported in UE and serving network, hence only they are described in sub-clause 6.1.3 of the present document. For a private network using the 5G system as specified in [7] an example of how additional authentication methods can be used with the EAP framework is given in the informative Annex B.
  NOTE 5: For non-public network (NPN) security the Annex I of the present document provides details.
Observation 3: according to the current requirements across TS 22.261 and TS 33.501:
    UE and serving NW shall ONLY support EAP-AKA’ and 5G AKA for public networks
    USIM/UICC is required for EAP-AKA’ and 5G AKA for public networks
    Additional authentication methods are allowed for private networks
    Tamper resistant hardware component is required for all authentication methods, not necessarily UICC

## Slide 14: Summary
Considering the two AIoT business models presented, Application-managed and MNO-managed presented, it is imperative that SA1 decides which business model(s) to be supported for AIoT devices (see Slide 7 for a summary).
Based on the definition of AIoT devices and existing SA1 and SA3 requirements, we make the following observations:
  Observation 1: An Ambient IoT device is an IoT device and a UE.
  Observation 2: Since AIoT devices are considered IoT devices the subscription requirements in TS 22.261, 6.14.2 should apply to AIoT devices.
    Note: AIoT devices support direct and indirect network communication as well as AIoT to UE direct communication modes [TS 22.369, v19.2.0, Subclause 4.4]
  Observation 3: according to the current requirements across TS 22.261 and TS 33.501:
      UE and serving NW shall ONLY support EAP-AKA’ and 5G AKA for public networks
      USIM/UICC is required for EAP-AKA’ and 5G AKA for public networks
      Additional authentication methods are allowed for private networks
      Tamper resistant hardware component is required for all authentication methods, not necessarily UICC.
    Note: UICC is not specified by 3GPP and would require external impacts for updates.

## Slide 15
Thank you

## Slide 16: TS 22.369 - AIoT
Observation 2: An Ambient IoT device can use of the three communication modes:
Direct Network Communication
Indirect Network Communication
Ambient IoT Device to UE direct communication mode