## Slide 1
Motivation for 6G SID: Quantum Safe Network (QSN)
Source: III, GE Network Technologies, ISSDU
Agenda item: 8.1
Document for: Discussion
Contact: Yi-Hsueh Tsai lucas@iii.org.tw Stephen F Bush stephen.bush@ge.com Feng-Ming Yang kelvinfomi@issdu.com.tw
S1-242126, 3GPP TSG WG1#107, August 19-23, 2024, Maastricht , NL

## Slide 2: Outline
Why We Need ‘Post Quantum Cryptography’ (PQC) for 6G?
Why We Need to QKD for 6G?
Potential Key Value Indicators (KVIs)
Potential Use Cases for QSN
  Potential Use Case for PQC
  Potential Use Case for TSQKD: Mitigating a Quantum Computing Attack on a 5G-TSN System in an Additive Manufacturing Facility

## Slide 3: Why We Need PQC for 6G?
As specified in clause 6.12.2 of 3GPP TS 33.501, the SUCI is generated using a protection scheme such as Elliptic Curve Integrated Encryption Scheme (ECIES) with the Home Network public key.
The main vulnerability of the ECIES protocol with respect to the quantum threat is actually the Diffie-Hellman key exchange step, regardless of the used profile.
Source: GSMA, “PQ.03-Post-Quantum-Cryptography-Guidelines-for-Telecom-Use-v1.0”

## Slide 4: Why We Need PQC for 6G? (cont.)
When considering the move from AES-128 to AES-256, the level of entropy that is used to generate the keys for symmetric key encryption maybe overlooked as part of the transition to PQC.
Current SA3 documents has not considered if entropy is poor, then even a 256 bit key can be easily compromised by Quantum computer.
Source: ATIS, “Implications of Entropy on Symmetric Key Encryption Resilience to Quantum”

## Slide 5: Why We Need to QKD for 6G
For time sensitive industrial control system use, the ultra-low latency service has extreme requirements on user-plane data transmitting delay. Without security, data transmitting is very quick using nowadays technology.
Introducing of security in user-plane data transmitting may unacceptably increase latency for time sensitive applications, but it is a trade-off between performance and security.
Source: 3GPP TR 33.825-g01, “Study on the security of URLLC for the 5G System (5GS)”

## Slide 6: Why We Need to QKD for 6G? (cont.)
Besides integrating PQC into 5G Time-Sensitive Networking (TSN) define in 3GPP TS 22.261 is essential for future-proofing the network against quantum computing threats.
However, this integration can introduce performance overheads in several areas, primarily due to the inherent characteristics of proposed new post quantum cryptography (PQC) algorithms compared to their classical counterparts.
Source: 3GPP TS 22.261, “Service requirements for the 5G system”

## Slide 7: Why We Need to QKD for 6G? (cont.)
Here's a detailed explanation of where performance overhead might increase:
  Increased Computational Complexity
  Larger Key Sizes
  Increased Latency
  Impact on Battery Life
  Challenges in Real-Time Applications
  Time synchronization is crucial and vulnerability for TSN

## Slide 8: Why We Need to QKD for 6G? (cont.)
Therefore, we are concerned that the increasing complexity of implementing PQC, as this may be too slow and unacceptable for time sensitive industrial control system application. Introducing Quantum Key Distribution (QKD) technology could reduce overhead, shortens latency, and provides warnings of eavesdropper attacks.
Source: Bush, Stephen F., “Time-Sensitive Quantum Key Distribution (TSQKD)”

## Slide 9: Potential Key Value Indicators (1/4)
Security Strength Levels:
  Define specific security strength levels for PQC algorithms that are equivalent to or better than current classical algorithms against quantum attacks. For example, specify minimum key sizes for symmetric and asymmetric encryption that are deemed quantum-resistant, such as 256-bit keys for symmetric encryption and larger key sizes for asymmetric encryption based on the specific PQC algorithm used.
Performance Benchmarks:
  Establish performance benchmarks for PQC algorithms, including maximum allowable computational overhead and latency for encryption/decryption processes, key generation, and secure communication establishment. These benchmarks should consider the impact on devices with limited processing capabilities and network infrastructure.

## Slide 10: Potential Key Value Indicators (2/4)
Bandwidth Efficiency:
  Set quantitative limits on the increase in bandwidth consumption due to larger key sizes and encrypted payloads in PQC. This could include specifying maximum overhead percentages relative to classical encryption methods to ensure efficient use of network resources.
Energy Consumption Metrics:
  Define metrics for the additional energy consumption allowed for devices performing PQC operations, considering the impact on battery life for mobile and IoT devices. These metrics should balance security requirements with device longevity.

## Slide 11: Potential Key Value Indicators (3/4)
Real-Time Communication Requirements:
  For applications requiring ultra-reliable low-latency communications (URLLC), specify maximum allowable delays introduced by PQC and quantum key distribution mechanisms. This includes defining acceptable levels of jitter and ensuring determinism in network performance.
Quantum Key Distribution (QKD) Performance:
  For QKD implementations, establish quantitative requirements for key generation rates, maximum allowable distances between nodes, and error rates. These requirements should ensure the practicality and reliability of QKD in various network scenarios.

## Slide 12: Potential Key Value Indicators (4/4)
Entropy Requirements
  Specify minimum entropy requirements for the generation of cryptographic keys to ensure their resistance to quantum attacks. This could include guidelines for entropy sources and methods for quantifying entropy.
Time Synchronization Accuracy:
  Define strict accuracy requirements for time synchronization in networks utilizing Time-Sensitive Networking (TSN), considering the potential security overhead introduced by quantum-safe mechanisms.

## Slide 13: Potential Use Case for PQC (1/5)
Description
This use case describes a scenario where user’s identity (UID) such as SUCI is generated using a protection scheme such as Elliptic Curve Integrated Encryption Scheme (ECIES) with the Home Network public key, and deciphered by hacker via Quantum Computer.

## Slide 14: Potential Use Case for PQC (2/5)
Pre-condition
Sarah Connor scribed to mobile network service and received an new SIM card provided by SkyNet Telecom.
SkyNet Telecom is still using a protection scheme such as Elliptic Curve Integrated Encryption Scheme (ECIES) with the Home Network public key to generate user’s identity (UID) such as SUCI.

## Slide 15: Potential Use Case for PQC (3/5)
Service Flows
Connectivity Details:
  Sarah inserts the received SIM card to her smart phone.
  She wants to watch a video and turn on her smart phone.
Interception Scenario:
  When Sarah’s smart phone tries to connect to base station, her smart phone’s UID is intercepted by SUCI-catcher of the hacker group named Genisys.
  After the value of SCPI was deciphered by Quantum Computer, Her location was track by the hacker group, Genisys.
Source: 5G SUCI-catchers: still catching them all? (https://dl.acm.org/doi/10.1145/3448300.3467826)

## Slide 16: Potential Use Case for PQC (4/5)
Post-conditions
Sarah figures out she was track by unknown group and report to the Lawful Authorities.
After investigating by the Lawful Authorities, the Authorities demand SkyNet Telecom to upgrade their mobile network service using new protection scheme supporting Quantum-Safe Cryptography.

## Slide 17: Potential Use Case for PQC (5/5)
Potential Requirements
The system shall support Post Quantum Cryptography (PQC) for both asymmetric and symmetric key encryptions to protect user’s identity and wireless communication between user equipment and base station, respectively.

## Slide 18: Potential Use Case for TSQKD (1/5)
Mitigating a Quantum Computing Attack on a 5G-TSN System in an Additive Manufacturing Facility
Description
John Connor's facility specializes in the additive manufacturing (3D printing) of life-critical parts, such as medical devices and aerospace components, relying on 5G Time-Sensitive Networking (TSN) for real-time control and monitoring. The facility faces a sophisticated attack where an adversary, using quantum computing, aims to compromise the integrity of the manufactured parts by maliciously altering the manufacturing instructions.

## Slide 19: Potential Use Case for TSQKD (2/5)
Pre-condition
Operational 5G TSN System: The facility's manufacturing processes are controlled and monitored in real-time via a 5G TSN system, ensuring low latency and high reliability crucial for the precision manufacturing of life-critical parts.
Classical Encryption Vulnerability: The network's communications are encrypted using classical encryption methods, which are vulnerable to decryption by quantum computing techniques.

## Slide 20: Potential Use Case for TSQKD (3/5)
Service Flows
Attack Scenario
Quantum Computing Implementation: The attacker uses a quantum computer to break the classical encryption of the 5G TSN system. This is achieved by exploiting algorithms like Shor's algorithm, which can efficiently factor large numbers and break RSA encryption, a common classical encryption method.
Malicious Message Insertion into TSN Flow: With the encryption compromised, the attacker gains the ability to insert malicious commands into the TSN flow. Using Sarah Connor's UE as a vector, the attacker sends commands that subtly alter the dimensions or material properties of the parts being manufactured. These alterations are designed to be difficult to detect but could lead to catastrophic failures in the parts' intended applications.

## Slide 21
Life-Critical Application: The facility manufactures components critical to the safety and functionality of medical devices and aerospace systems. Any compromise in the integrity of these parts could have dire consequences, including system failures and endangering lives.
Mitigation with Satellite-based Quantum Key Distribution
To counteract such threats, the facility implements a satellite-based QKD system:
Satellite-based QKD Implementation: A trusted satellite generates quantum keys, establishing secure communication channels with ground stations at the facility. The satellite broadcasts the bit-wise parity of each key to create a common, secure key between stations, immune to quantum decryption efforts.

## Slide 22
Integration into 5G TSN: The quantum-secure keys are integrated into the 5G TSN system, ensuring all communications are encrypted with quantum-resistant algorithms. This involves updating the network infrastructure to support QKD and ensuring compatibility with 5G protocols.
Continuous Key Renewal and Monitoring: The system is designed for the continuous renewal of quantum keys and real-time monitoring for any signs of tampering or unauthorized access attempts, maintaining secure communications even in the face of evolving threats.

## Slide 23: Potential Use Case for TSQKD (4/5)
Post-conditions
Secured 5G TSN System: The network is now secured with quantum-resistant encryption, effectively neutralizing the threat of quantum computing attacks.
Protected Manufacturing Processes: The integrity of the manufacturing process is restored, ensuring the production of life-critical parts without compromise.
Benchmark for Quantum-Safe Manufacturing: The facility becomes a model for secure manufacturing operations, encouraging the adoption of quantum-safe networks in critical sectors.
Quantum-Resistant Requirements and Implementation in 5G

## Slide 24
Quantum-Safe Encryption Algorithms: Post-quantum cryptographic algorithms are employed for all network communications, ensuring long-term security against quantum attacks.
Standardization and Compliance: The implementation adheres to emerging standards for quantum-safe communications in 5G networks, ensuring interoperability and compliance with international security protocols.
Education and Training: Staff and network administrators are trained in the operation and management of quantum-safe systems, maximizing the effectiveness of the network's security measures.
This use case illustrates the critical need for quantum-safe networks in securing 5G TSN systems, particularly in applications where the stakes, such as the manufacturing of life-critical parts, could not be higher.

## Slide 25: Potential Use Case for TSQKD (5/5)
Potential Requirements
The system shall support Quantum Key Distribution (QKD) to provide secure key management and ultra-low-latency small-data-rate communication for critical applications like smart factory.