## Slide 1
China Telecom
Discussion on FN-RG supporting 5G LAN-type service

## Slide 2
  Motivation
Smart Home is one of the most popular scenarios for 5G and 5G-A. FN-RG is the legacy residential gateway that is easy to deploy and is widely used nowadays.
The following use case is one of the key use cases for efficiently access to the local data in home from the UE that is away from home and belong to the same family group. It is highly desirable for 3GPP to support such use case.
Bob owns the UE and those non-3GPP devices in his house connected to the 5GC via the FN-RG, which all belong to the same 5G-LAN.
Bob is away from home with his UE.
When Bob want to check the video surveillance in home, he could access the video efficiently through the user plane and via the FN-RG.

## Slide 3
  Gap Analysis
In Rel-18, there are use cases and requirements on the connection between the non-3GPP devices via the eRG and the UE from the same 5G LAN-VN.
eRG is a gateway between the public operator network (fixed/mobile/cable) and a customer premises network.
The existing requirement does not consider the legacy residential gateway between the 5G network and the customer premises network.

## Slide 4
  Proposal
It is proposed to add the definition of FN-RG and the following changes to TS 22.261 subclause 3.1, 3.2, 6.26.2.2 and 6.38.2.2 and some description in subclause 6.38.1.
3.1 Definition
Fixed Network Residential Gateway: a legacy residential gateway that is not 5GC capable.
3.2 Abbreviation
FN-RG Fixed Network Residential Gateway
6.26.2.2 5G LAN-virtual network (5G LAN-VN)
The 5G system shall support a communication path between a UE in the 5G-LAN and the non-3GPP devices in the CPN via the FN-RG of the CPN, for an FN-RG that is part of the 5G LAN-VN.
6.38.2.2 Gateways The 5G system shall be able to support access to the 5G network and its services via at least one gateway (i.e. PIN Element with Gateway Capability or eRG or FN-RG) for authorised UEs and authorised non-3GPP devices in a PIN or a CPN.

## Slide 5
THANKS
感 谢 聆 听