## Slide 1: Draft reply to LS of AIoT security (S1-242185/SP-241016)
OPPO

## Slide 2: Background
There is a LS from SA regarding to AIoT security (S1-242185/SP-241016). Several LSreply contributions are submitted by companies (S1-242193, 2231, 2242, 2283, 2121, 2158).
It is to propose the reply the LS based on the aspects and corresponding answers addressed in all companies’ contributions:
- How to collect and expose data with 3rd party based on SLA;
- Subscription and Lifecycle management;
- Charging;
- Operator-managed v.s. application-managed model;
- Secured storage and secured data transfer.

## Slide 3: How to collect and expose data with 3rd party based on SLA
Proposed reply:
In 22.369, there are three communication modes:
Ambient IoT Direct Network Communication, Ambient IoT Indirect Network communication: requires a 3GPP network entity to collect data and expose it to a trusted 3rd party;
Ambient IoT Device to UE Direct Communication: requires an authorized UE to collect data from Ambient IoT devices and expose it to an trusted 3rd party.
In 22.369 clause 5.2.4, there are “exposure” requirements based on SLA.

## Slide 4: Subscription and Lifecycle management
Proposed reply:
AIoT device as a kind of IoT device, is a UE with subscription. The requirements for subscription (TS22.261 clause 6.14.2) and security (clause 8.1) can apply to AIoT device, which includes the ownership and provisioning requirements.

## Slide 5: Charging
Proposed reply:
In 22.369, the charging requirement is as below. SA1 understands it is possible for AIoT device to be charged individually, or aggregated charging per application server
  - The 5G system shall be able to collect charging information in a suitable way for using Ambient IoT services on per Ambient IoT device basis or a group of Ambient IoT devices (e.g., total number of communications per charging period).

## Slide 6: Operator-managed v.s. application-managed model
Proposed reply:
SA1 thinks operator-managed model is a typical scenario, while SA1 does not exclude application-managed model.

## Slide 7: Secured storage and secured data transfer
Proposed reply:
SA1 thinks some kind of tampered resistant storage for credential make sense, but whether it needs UICC is solution specific.
Data transfer with Ambient IoT device may require security protection (crypted, integrity protected) depending on scenarios.
Considering the characteristics of Ambient IoT devices is described in 22.369 clause 4.2 (incl. low complexity, low data rate, long life span, energy harvesting), it is up to downstream group to decide whether the existing security mechanism suitably applies to Ambient IoT device, or a light-weight mechanism is needed.