## Slide 1
Baseline for Release 20 6G Sensing Requirements
Qualcomm
S1-244095, 3GPP TSG #108, 18 – 22 November 2024, Orlando, Florida, US

## Slide 2
ISAC Release 19 SA1 SI/WI
In Release 19, SA1 start an Integrated Sensing and Communication study which is a 3GPP 5G system where the sensing capabilities are provided by the same 5G wireless communication system and infrastructure as used for communication” [TR 22.837]
5G Wireless sensing: 5GS feature providing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g., shape, size, orientation, speed, location, distances or relative motion between objects, etc) using NR radio frequency signals.
Non-3GPP sensing: data provided by non-3GPP sensors (e.g., video, LiDAR, sonar, WiFi,…) about an object or environment of interest for sensing purposes.

## Slide 3
SA1 Outputs:
  TR: 32 Use cases were contributed to the TR (TR 22.837).
  TS: 27 Functional requirements and KPIs for 7 categories of sensing use cases/scenario were standardized for ISAC in TS 22.137
Other WGs:
  Limited ISAC activities in down stream groups:
    RAN 1 is developing Channel Models for sensing in Rel-19, TBD about R20 normative work
    SA2 is not working on Sensing for R19, TBD for Release 20
  No other WG is working on ISAC
Observations:
  It is still unknown whether and how much ISAC normative work will be done in 5G-A.
  IMT-2030 requirements will likely include 6G support of ISAC
ISAC Stage-2/3 Progress & Observations

## Slide 4: Proposals for 6G Study Release 20 Sensing Requirements
Proposal 1: SA1 ISAC Requirements in TS 22.137 should be assumed to be supported by 6G.
Release 19 Requirements | Proposed 6G Requirements
Subject to regulation, the 5G network shall enable UEs without 5G coverage to use unlicensed spectrum to provide 5G wireless sensing service. | Proposal: (New requirement for TR 22.870 sec. 6) 6.X Enhanced Sensing Requirements Subject to regulation, the 6G network shall enable UEs to perform 6G Wireless sensing when in full or partial network coverage or not served by RAN.
Subject to regulation, the 5G network shall enable UEs supporting V2X application to perform 5G Wireless sensing when not served by RAN using the allowed ITS spectrum and unlicensed spectrum. | 
Based on location, the 5G network shall be able to ensure that sensing transmitters and sensing receivers use licensed spectrum only in network coverage and under the full control of the operator who provides the coverage. NOTE 3: The above requirement does not apply for public safety and V2X networks with dedicated spectrum, where 5G wireless sensing can be allowed out of coverage or in partial coverage as well. | 
Proposal 2: Propose to update/enhance some of the functional requirements for 6G:
Notes: Option 2 (Remove requirement): Remove Req. 2 and 3 and 4

## Slide 5: Conclusions
Consider Proposals 1 and 2
Further updates would also be needed for KPI requirements for categories such as category 7 since the positioning accuracy and sensing resolutions were limited based on 5G capabilities.