## Slide 1
Summary of discussion on Options to support Broadcast by satellite for unregistered UE
NOVAMINT (Rapporteur for FS_5GSAT_Ph4)
S1-244106, 3GPP SA1#108, 18-22 November 2024 – US, Florida, Orlando
© 3GPP 2024

## Slide 2: Options possibles for support Broadcast by satellite for unregistered UE
We discussed in SA1#107 the way forward for supporting MBS broadcast without authentication by Satellite and we agreed to "keep this open for SA1#108 and that all options are still open, including revising the SID".
=> 3 options:
- option 1: simple CR for clarification in TEI18 for TS 22.101 - applies for Rel-18 & 19
- option 2: revised SID to integrate this topic in Rel-20 / impact: TS 22.261 + TS 22.101?
- option 3: Mini-WID - applies for Rel-20 (& 19?) - impact: TS 22.261 + TS 22.101
The 3 options were discussed the 31st of October in a call set up by SA1 – informal call with no decision power

## Slide 3: Option 1 – simple CR
Simple CR to TS 22.101: Clarification and alignment on NTN reception of TV transport services via MBS broadcast without authentication
Change proposed:
  The 3GPP network shall enable a MNO to allow a UE to receive TV transport services via eMBMS/MBS broadcast without authentication.
  NOTE: This requirement applies to both terrestrial access networks and satellite access networks.

## Slide 4: Option 2 - SID
to revise the SID on Study on satellite access - Phase 4 to include:
“Enhanced Support for Broadcast Services with Satellite Access System for Unregistered UE”
With the following additional objective:
to identify the gaps between the 4G Free-to-air (FTA) as specified in TS 22.101 clause 32 (3GPP enhancement for TV application support) and the 5G system and identify potential new service requirements to support the use case of broadcast services using satellite access.
Will likely lead to one use case with, at least, the following requirements in 22.261 (+ 22.101):
[PR x.1.6-00x] Subject to regulatory requirements and operator’s policy, a 5G System supporting satellite access and Broadcast Services, shall be able to deliver Media Broadcast to a UE which is not registered.
  NOTE 1: The UE may not have any SIM/USIM.
  NOTE 2: This will apply only to UEs adapted for receiving broadcast services by satellite access. It is assumed that if these UE need to access terrestrial network, they will need to be registered UEs
[PR x.1.6-00x] Subject to regulatory requirements and operator’s policy, a 5G System supporting satellite access and Broadcast services shall be able to support a mechanism for an unregistered UE supporting satellite access and terrestrial access with 5G System to select the appropriate RAT to receive the broadcast service while moving between terrestrial network and satellite network.

## Slide 5: Option 3 – Mini WID
Same justification as SID
Mini-WID - applies for Rel-20 (& 19?) - impact: TS 22.261 + TS 22.101
Changes proposed at minimum:
  For TS 22.261
Subject to regulatory requirements and operator’s policy, a 5G System supporting satellite access and Broadcast Services, shall be able to deliver Media Broadcast to a UE which is not registered.
  For TS 22.101
The 3GPP network shall enable a MNO to allow a UE to receive TV transport services via eMBMS/MBS broadcast without authentication.
NOTE: This requirement applies to both terrestrial access networks and satellite access networks.

## Slide 6: View from satellite community
Basically the 3 options are boiling down mostly to one simple requirement: to support broadcast by satellite for unregistered UE
Question is more:
  which TS it applies (TS 22.261, TS 22.101 or both)
  For which release
The option 1 & 3 have the advantage to be "simple" and with limited use of SA1 meeting time in general
Satellite industry is willing to compromise to find a solution to support broadcast by satellite for unregistered UE as this is a fundamental service for them

## Slide 7: Summary of the discussions
No fundamental objection on the needs to address this topic (for the satellite and the media – the LS from 5GMAG is reinforcing this)
No company considering this as a novelty – it is not a 6G topic
Several companies (offline and online) have expressed their preferences for option 1 due to the simplicity and could also support option 3
Among those companies, one company was opposed to option 2 as it is due to the workload it will create if we include a new objective in the SID
At least, one company opposed to option 1 as option 1 is perceived as bypassing SA1 principles as providing no justification for the change proposed and is questioning why only this change to be done in 22.101
Same company believes option 3 is requiring more justification and will require basically a study so unlikely to be accepted
Same company believes the only way is to go for the option 2 – to include this topic in the study

## Slide 8: Potential compromise
In order to address concerns about the workload generates by the topic, compromise could be to go for option 2b: To revise SID to integrate the topic with the following restrictions:
  Limit the objective to study only one use case of broadcast services using satellite access for unregistered UE
  Target impact only TS 22.261 / not TS 22.101
Revision of the SID for Satellite access have been proposed in this direction - S1-244103
+ 1 use case: Use case on Broadcast Services with satellite access for unregistered UEs (S1-244078)